## Slide 1: Discussion Paper on Identifiers in SS_VALServiceData API
Igor Pastushok
Ericsson

## Slide 2: Agenda
Background
  Received LS
  Location-based group creation clause 10.3.7
Identifiers in the SS_VALServiceData API
Proposed solution and summary

## Slide 3: Received LS from CT3
Question: Is it possible to provide the combination of VAL user IDs and VAL UE IDs in the "Identity list" ["of clause 11.3.2.13"*] information element, e.g., [VAL UE ID A, VAL user ID B, VAL UE ID C]?
Observation 1: 3GPP TS 23.434 from Rel-16 does not contain any limitations for providing the combination of VAL UEs or VAL User IDs in the SEAL interfaces.

## Slide 4: Background Location-based group creation
Overview of clause 10.3.7 of 23.434:
  VAL server or GM Client requests the GM server to create a VAL group of VAL UEs or Users within the given location.
  The GM server requests the LM server to retrieve all VAL UEs and/or VAL Users within the given location via SS_LocationAreaInfoRetrieval API.
  The LM server via SS_LocationAreaInfoRetrieval API responses to the GM server with the list of all VAL UEs and/or VAL Users (correspond to different VAL services) within the given location.
  The GM server shall filter the relevant VAL UEs or VAL Users to create the group: “If VAL service ID list was received in step 1 as part of group formation criteria and not in step 4 for the composed list of users or UEs, the group management server shall retrieve the VAL service data from the configuration management server as described in clause 11.3.2.13 and form the group with relevant users or UEs.”
Observation 2: In step 4, the GM Server may receive the composed list of VAL UEs and/or VAL Users (correspond to different VAL services) within the given location and require SS_VALServiceData API to identify the VAL Service for each VAL UE or VAL User within the composed list.

## Slide 5: Identifiers in the SS_VALServiceData API
Observation 2: In step 4, the GM Server may receive the composed list of VAL UEs and/or VAL Users (correspond to different VAL services) within the given location and require SS_VALServiceData API to identify the VAL Service for each VAL UE or VAL User within the composed list.
The observation above clarifies that the VALServiceData API require to have a combination of VAL UEs and/or VAL Users in the request message in order to provide an efficient and user-friendly service to the GM server in SEAL-X reference point.

## Slide 6: Proposed Solution and Summary
Proposed solution: the combination of VAL Users and VAL UEs may be provided in the request message (clause 11.3.2.13 of 23.434) of the SS_VALServiceData API.
It is proposed to agree on LS out S6-241211.