## Slide 1: Discussion on connection and flow in SEALDD
Cuili Ge
Huawei, Hisilicon

## Slide 2: Issue: The concept “connection” and “flow” in SEALDD is not clear(1)
VAL client
DD client
DD server
VAL server
SEALDD-UU connection
SEALDD-S connection
connection
flow
The “connection” and “SEALDD flow” concepts are used, the relationship between them are not clear
“Connection” used in the TS:
end-to-end connection between VAL client and VAL server, such end-to-end connection (also termed SEALDD flow)
SEALDD-S Data transmission connection
SEALDD connections
application connection
SEALDD regular connection
application signalling transmission connection
signalling connection
application layer connection
data transmission connection between VAL server and SEALDD server
the connection between VAL server and SEALDD server
After the negotiation and establishment of the connections, the SEALDD client gets the mapping information between the application traffic and SEALDD flow ID.
SEALDD-S connection
URLLC transmission connection
regular data transmission connection
……
“Flow” used in the TS:
SEALDD flow: The SEALDD flow ID is used by the SEALDD client and SEALDD server to identify different VAL application traffic
To be
Application connection
Application connection: Association between the VAL client and the VAL service to provide the VAL service.
Application traffic: a set of signaling messages or a set of media packet constituting a application service flow. E.g., a picture may be an application traffic, the audio stream and the video stream are two different application traffic.
SEALDD–S connection: Association between the SEALDD server and the VAL server to achieve data delivery of the application traffic. One application connection may have one SEALDD-S connection, e.g., for all the application traffic flows, or have more SEALDD-S connections, e.g., one for application signaling flow, and the other or application media traffic flow(s). A SEALDD-S connection shall be uniquely identified between the VAL server and the SEALDD server.
SEALDD-S flows: a set of packets have the same attributes, e.g., the same 5-tuple, media type. The application traffic flow may be mapped to one ore more SEALDD-S flow(s). A SEALDD-S flow should be uniquely identified with the SEALDD-S connection.
SEALDD-UU connection: Association between the SEALDD server and the SEALDD client to achieve the data delivery of the application traffic from the SEALDD serve or the VAL client. One SEALDD-S connection may be associated with one SEALDD-UU connectionore multiple SEALDD-UU connections. A SEALDD-UU connection shall be uniquely identified between the SEALDD client and the SEALDD server.
SEALDD-UU flows: a set of packets have the same attributes, e.g., the same 5-tuple, media type, QoS requirements. One SEALDD-S flow(s) maybe mapped to one or multiple SEALDD-UU flows. A SEALDD-UU flow should be uniquely identified with the SEALDD-Uu connection.
SEALDD-Uu flow(s)
SEALDD-S flow(s)
Application traffic(s)

## Slide 3: Issue: The concept “connection” and “flow” in SEALDD is not clear (2)
To be
Current: in regular transmission case, only one SEALDD flow is created.
It is not sufficient, one application may have multiple application media traffic flows ( e.g., for a webpage, each element type (text, pictures, video), and those application media traffic flow may require different SEALDD flows to avoid the Head-of-line blocking.
So the regular transmission requires one or more SEALDD flows.
9.2.2.2 SEALDD enabled regular data transmission connection establishment procedure
6.The SEALDD client allocates a SEALDD flow ID mapping to the identifiers of the application traffic . The SEALDD client sends Sdd_RegularTransmissionConnection_Establish request to SEALDD server with the SEALDD client ID, the SEALDD flow ID, the SEALDD traffic descriptor of the SEALDD client side (the address/port of the SEALDD client for receiving the downlink SEALDD traffic), VAL server ID, VAL service ID . ……

## Slide 4: Issue: The concept “connection” and “flow” in SEALDD is not clear (3)
To be
Current: in URLLC transmission case, only one SEALDD flow is created.
It is not correct as in step 10 and 11, a new flow is added .
So the regular transmission requires two SEALDD flows. The procedure descriptions should be corrected.
…….
7. The SEALDD client allocates a SEALDD flow ID mapping to the application traffic. The SEALDD client sends Sdd_URLLCTransmissionConnection_Establish request to SEALDD server. The request includes the SEALDD client ID, SEALDD flow ID, VAL server ID, VAL service ID for SEALDD server to identify the specific application traffic.
9.3.2.1 E2E redundant transmission path establishment procedure