## Slide 1: MC logging, recording and replay
AIRBUS proposal
3GPP TSG-SA WG6 Meeting #62 S6-243036
Maastricth, Netherlands, 19-23 August 2024

## Slide 2: Terminology
In this proposal:
  Log metadata (signalling)
  Record media
  Replay both (media and/or metadata)
  NOTE: Discreet listening/monitoring are not yet included in this proposal.
SA3: TS 33.180 (clause 10)
  ’Event’ = Metadata (essentially signalling, clause 10.1.2.1)
  ’Audit’ = Replay
  ”Discreet monitoring” (not yet defined in SA6)
SA1: TS 22.280 (A.1, A.2)
  ”log metadata”
  ”record the transmissions of the Group Communications and Private Communications “
  ‘Audit’ (with no definition)
SA6 study: TR 23.784
  “log media and metadata”
  “record and replay the content of calls”

## Slide 3: New (functional) elements
MC Recording Server: A server that is able to log the metadata and record the media of MCPTT, MCData, and MCVideo Group Communications and Private Communications and store them into a mass storage. This server is also able to retrieve the stored metadata/media when requested by an authorized user.
MC Replay UE: A user equipment that can (only) be used to fetch and replay recorded MCPTT, MCData, and MCVideo metadata (i.e. signalling) and media of MCX Service Group Communications and MCX Service Private Communications under the UE user’s authority. MC Replay UE can be a mobile device or a (computer) workstation.
MC Replay Client: A client application that is able to fetch and replay logged metadata and recorded media from a Recording Server and replay them to an authorized user.
Mass storage: A generic name for a storage where the MC logs and recordings are stored. Storage(s) can be owned by MC operator or end user organization and can be physically located anywhere. The details of a storage(s) are out of the scope of the current specification.

## Slide 4: Functional model and reference points
No separate client for ”MC log capture function” (S6-242344) in the functional model.
Instead, a new server (Recording server) is introduced.

## Slide 5: A replay client can also be located in MC service UE

## Slide 6: RCS-7 between Recording server and mass storage(s) is out of 3GPP scope
Remove the SA3 assumption - or clarify that this is optional – in TS 33.180, clause 10.2.3:
“User media in the MC System is end-to-end encrypted by default. Consequently, media can be recorded without modificiation and without additional protection…”
…which leads to complex key retrieval procedures before the media can be replayed (ref TS 33.180, clause 10.2.4).
Instead, keep RCS-7 out of 3GPP scope to enable different security implementations based on operator requirements/policies.

## Slide 7: RCS-1 between replay client and recording server is also out of 3GPP scope
The only thing that shall be mentioned in 3GPP (SA6) specification about RCS-1 is that:
  “The RCS-1 reference point shall use the HTTP-1 and HTTP-2 reference points”

## Slide 8
  Please see also CR in S6-243037
  Thank You!