## Slide 1: Location reporting and eMBMS support via MCGWUE
Ericsson

## Slide 2: Functional model
Figure 11.2.0-1: Functional architecture
TS 33.180 clause 5.12:
NOTE: How information is protected in transit between the non-3GPP device and the MC client when the MC Client resides on the MC gateway UE is out of scope of 3GPP.
Specification of the protocol and security used on the interface between the MC gateway UE and the non-3GPP device is out of scope of 3GPP.
Question: why do we define messages over the non-3GPP connection, which its security is out of scope of 3GPP?

## Slide 3: Location reporting support
The proposed functional model includes LMC in the MCGWUE
The LMC in the non-3GPP device includes the MC service ID of the MCGWUE, which is responsible of reporting 3GPP related parameters
Hence, the MC service server is aware of the mapping between the MC client(s) in the non-3GPP device and the respective MCGWUE
In order to obtain 3GPP access location parameters of MC client(s) in non-3GPP device, the MC service server requests location reporting from the corresponding MCGWUE according to existing procedures
The report sent from the LMC in the MCGWUE is applicable to all MC clients behind it. Hence, the reporting is done for one or multiple MC clients in an efficient way
Proposal Figure 11.2.1-1: Functional model of MC gateway UE application plane with MC client hosted in the non- 3GPP device
Non-3GPP connection
Notes: For MC UEs that support mission critical location services, authorization is accomplished by including an access token in each location message (i.e. location information report, location reporting trigger, etc.) sent by the location management client to the location management server.

## Slide 4: Location reporting support

## Slide 5: eMBMS support
An MBMS user agent can be hosted in MC gateway UE to support the MC service client in the non-3GPP device in receiving MBMS bearer
Procedures and respective aspects are as defined in TS 23.479
There is nothing more needed to be done
Proposal Figure 11.2.1-1: Functional model of MC gateway UE application plane with MC client hosted in the non- 3GPP device
Non-3GPP connection

## Slide 6: Functional model of MCGWUE with the support of MBMS and location reporting
Proposal Figure 11.2.1-1: Functional model of MC gateway UE application plane with MC client hosted in the non- 3GPP device

## Slide 7: Alternative approach
keep location reporting and eMBMS related information over the non-3GPP connection out of scope of TS 23.280
Figure 11.2.0-1: Functional architecture