## Slide 1: Discussion on Available Capabilities and Information for XR Services
Jing Yue
Ericsson

## Slide 2: Agenda
Background
  TR for FS_XRApp
  Available Capabilities and Information
AIML Capability for XR Services
Available 5G Network Information for XR Services
Proposed solution
Summary

## Slide 3: Background – FS_XRApp
FS_XRApp - TR 23.700-23 v1.1.0
  4.4 - Key issue 4: Application enablement layer capabilities usage to supporting the XR services
    To support online AR gaming, the following capabilities could be leveraged (with potential enhancements): AI/ML may be required for Image & Object Recognition.
    It is proposed to study the following open issues:
    Whether and how the identified application enablement capabilities could be utilized to jointly support the XR service.
    Whether and how the application enablement architecture could support the XR service taking advantage of the identified application enablement capabilities.

## Slide 4: Background – FS_XRApp
FS_XRApp - TR 23.700-23 v1.1.0
  4.7 - Key issue 4: E2E KPI optimization for XR service
    In real-time XR service, E2E KPI (e.g. low latency) is critical to provide immersive experience for XR users. The E2E performance of XR service is impacted not only by data transmission, but also by data processing.
    This key issue includes the following aspects:
    How to support the E2E KPI optimization to meet real-time XR service requirements, taking the processing delay of XR application server into account, e.g. considering the potential enhancements to EDGEAPP in XR application server discovery or instantiation.
    What available information from 5G network can be used by enable layer to optimize the real-time XR service requirements.

## Slide 5: Background – Available Capabilities
For key issue 4: AI/ML for XR Service
  Use cases on AI/ML support XR relevant services in TR 23.874 and TR 23.876:
    Split AI/ML image/object recognition
    Split image/video processing
  Available solutions in TR 23.700-82 v19.0.0 for FS_AIMLAPP:
    AIMLE server can provide assistance information to the SEALDD server for assisting deliver/distribute XR data to the split AI/ML endpoints
For key issue 7: Available 5G Network Information for XR Service
  Available 5G network information for low latency data transmission, e.g.:
    NWDAF: E2E data volume transfer time, etc.
    NEF: Set up AF session with required QoS
Open issues: How the available capabilities be used for supporting XR services.

## Slide 6: AIML Capability for XR Services
Consumer (e.g. VAL server) decides split image/video processing for a XR service, SEALDD server support data delivery for the XR service
AIMLE Server Assists Split AI/ML Operations
  Discovery split nodes - AIMLE server assists VAL server for discovery of split endpoints to take the split tasks on e.g. AI/ML image/video processing
  AI/ML task delivery - AIMLE server provides assistance information to SEALDD server for supporting the data delivery
    Time point/time window for data delivery with QoS requirement.
    Achievable QoS with current configuration of session between UE and AF (e.g. the consumer).
    Suggestion of QoS values for each flow of the session in order to satisfy application requirement.

## Slide 7: AIML Capability for XR Services
The assistance information from the AIMLE server can be used by the SEALDD server
  Time point/time window for data delivery with QoS requirement
    Can be used to decide the time for data delivery/distribution and satisfy QoS requirement.
  Achievable QoS with current configuration of session between UE and AF (e.g. the consumer)
    Can be used to decide whether update of the current configuration is needed or not.
  Suggestion of QoS values for each flow of the session in order to satisfy application requirement
    Can be used to decide the configuration of each flow of the session.
The assistance information can be used separately or jointly depends on need at the SEALDD server.

## Slide 8: AIML Capability for XR Services
The SEALDD server may decide to interact with AIMLE server for assistance information, if such assistance information is needed and not contained in the request message from the consumer.
The benefits that the SEALDD server get the assistance information directly from the AIMLE server include
  Receive assistance directly from AIMLE server with relevant low delay.
  Support fast update of configuration with the updated assistance information directly from the AIMLE server.
  Allow flexible request of assistance information for data delivery purposes (e.g. achievable QoS, suggestion of QoS), as the SEALDD server can adjust its request to the AIMLE server based on need.

## Slide 9: Available 5G Network Information for XR Services
Consumer (e.g. VAL server, VAL client via SEALDD/XRApp client) requests SEALDD server for real-time data delivery
Available 5GC information for real-time data delivery
  NWDAF: E2E data volume transfer time analytics
    The predictions of E2E data volume transfer time for uplink/downlink given data volume can be used by the SEALDD/XRApp server to set the individual QoS parameters (e.g. Requested 5GS Delay) and data volume.
  NWDAF: UE mobility analytics:
    The prediction of UE location can be used to set the requirement on QoS monitoring (e.g. area of interest).
  Services provided by NEF:
    Set up AF session with required QoS for XR data delivery
    QoS monitoring

## Slide 10: Data Size in Service Request
In the request from the consumer to SEALDD server, assume that data size of the data to be delivered is contained.
  Data size of the data to be delivered is available or can be estimated by the consumer.
Split point | Approximate output data size (MByte) | Required UL data rate (Mbit/s)
Candidate split point 0 (Cloud-based inference) | 0.15 | 36
Candidate split point 1 (after pool1 layer) | 0.27 | 65
Candidate split point 2 (after pool2 layer) | 0.17 | 41
Candidate split point 3 (after pool5 layer) | 0.02 | 4.8
Candidate split point 4 (Device-based inference) | N/A | N/A
Table 5.1-1 (in TR 22.876): Required UL data rate for different split points of AlexNet model for video recognition @30FPS (Frame Per Second)
Example that data size is available: Split AI/ML image recognition introduced in clause 5.1 of TR 22.876 (Table 5.1-1), etc.
Consumer can estimate the data size according to its previous applications with the same XR service.
If such information is not contained in the request, the SEALDD server rejects the service request from the consumer.

## Slide 11: Proposed Solution
Following changes to FS_XRApp TR 23.700-23:
  For the study aspect in key issue #4
    Whether and how the identified application enablement capabilities could be utilized to jointly support the XR service.
    Add solution on application enablement layer AIML capabilities for supporting XR services
  For the study aspect in key issue #7
    What available information from 5G network can be used by enable layer to optimize the real-time XR service requirements.
    Add solution on support real-time XR service with available 5G network information
The proposed changes provide solutions to address the study aspects in clauses 4.4 and 4.7 of TR 23.700-23, complete the study of corresponding key issues for FS_XRApp.

## Slide 12: Summary
This discussion paper proposes solutions to
  Address the study aspects of key issues #4 and #7 in clauses 4.4 and 4.7 of TR 23.700-23 v1.1.0.
  Complete the study of corresponding key issues for FS_XRApp.
  It is proposed to discuss and agree on pCRs S6-243206 and S6-243207 that provide implementation of the solutions described in the discussion paper.