## Slide 1: MCVideo enhancement with 5G network capabilities
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
History track
New 5G network capabilities for media streaming service
How MCVideo service can benefit from 5G network capabilities

## Slide 3: History track
SA6 sent LS-S6-241323 to SA4 discuss about how to use the 5G new network capabilities (e.g., L4S feature) to improve the MCVideo service.
SA4 sent the LS back in S6-243009/S4-241334, indicating that SA4 only focuses on stage 3 for MCVideo
  “SA4 is maintaining the Stage 3 for MCVideo in TS 26.281, following the Stage 2 from SA6. SA4 can start amending TS 26.281 with the needed media plane protocol functions, once the corresponding Stage 2 is finalized, following the normal SA4 work procedures. It is currently assumed, that the amendments to TS 26.281 are minor and can be done within Rel-19.”
Now it is time to start the stage 2 work from SA6!

## Slide 4
New 5G network capabilities for media streaming service also can be used for MCVideo
Category | Exposure information from Network |  | Network entity being involved and related NBI APIs
Network layer connectivity information exposure （SA2） | UL/DL congestion (QoS monitoring) |  | NBI API Nnef_AFsessionWithQoS_Sub/Noti or Npcf_PolicyAuthorization_Sub/Noti (w/o NEF) Nnef_EventExposure_Sub/Noti or Nupf_EventExposure (w/o NEF)
 | UL/DL Data rate |  | 
 | UL/DL/RT delay |  | 
 | Estimated bandwidth |  | NBI API Nnef_AnalyticsExposure_Sub/Noti or Nnwdaf_AnalyticsSubscription_Sub/Noti (w/o NEF)
 | UL/DL congestion (L4S feedback) |  | NBI API Nnef_AFsessionWithQoS (to set the L4S indication) ECN marking for L4S at UPF or RAN towards UE, then to AS
Application layer information exposure （SA4） | QoE metrics UE data |  | Data collection AF Naf_EventExposure_Notify Nnwdaf_AnalyticsSubscription_Sub/Noti (w/o NEF)
NOTE: Other capabilities for media streaming not listed in above table are not applicable for MCVideo, e.g., multi-model service ID, data collection for consumption reporting

## Slide 5
How MCVideo can benefit from such capabilities
Network exposure information | MCVideo service work flow | SA6 standard impact
1. UL/CL congestion (QoS monitoring notification) or UL/CL congestion (L4S feedback) | MCVideo server and MCVideo client negotiate L4S capability. MCVideo server obtains the network UL/DL congestion information via the (a) QoS monitoring or (b) RTCP feedback report (per RFC 6679, RFC 8888); MCVideo servers may adapt the RTP packet sending rate | L4S capability negotiation between MCVideo server and MCVideo client Subscribe the QoS monitoring from 5GC/request L4S ECN marking MCVideo client sends the RTCP with L4S feedback report MCVideo behavior general descriptions
2. UL/DL Data rate | MCVideo server subscribes DL/DL data rate from the 5GC MCVideo server triggers the may adapt the RTP packet sending rate | Subscribe the QoS monitoring from 5GC General MCVideo behavior descriptions
3. UL/DL/RT delay | MCVideo server subscribes RT delay from the 5GC MCVideo server may initiate adapt the RTP packet sending rate | Subscribe the QoS monitoring from 5GC General MCVideo behavior descriptions
4. Estimated bandwidth | MCVideo server subscribes Estimated bandwidth from the 5GC MCVideo server adapt the RTP packet sending rate | Subscribe the QoS monitoring from 5GC General MCVideo behavior descriptions
5. QoE metrics UE data | MCVideo subscribe the QoE metrics UE data MCVideo server may adapt the RTP packet sending rate | Subscribe the QoE metrics data from 5GC/Data Collection AF General MCVideo behavior descriptions
Example: Video Push
Application and signaling
Transmission control
MCVideo server
5GC
NG-RAN
MCVideo UE
RTP pkt
Modem
Application and signaling
Media distribution
Media mixer
Transmission control
SIP messages
Transmission control messages
❶ Network exposure information Sub/Noti
❹ DL RTP sending rate control
❷ L4S capability negotiation
❸ UL L4S feedback
Media control messages
Media control
Media control

## Slide 6
Proposals
Agree the corresponding CR S6-24xxxx (CR xxxx)