## Slide 1: Discussion on 5G-SAT (LEO) backhaul QoS for MC applications
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: Content
ESN use case with 5G SAT
Limitations in LEO backhaul provision
MC QoS requirements with LEO backhaul

## Slide 3: ESN use case
ESN will require the limited backhaul capability provided by LEO satellite constellations in certain scenarios
  These will be ad-hoc MC deployments in remote areas, where terrestrial BH is not available.
  ESN (or other MC network) will have an agreement with the LEO SAT provider for a 5G slice for backhaul provision for the duration of the emergency event.
  The LEO network will configure the 5G temporary backhaul slice, to agreed QoS levels for these MC services.
The QoS levels that can be technically achievable will depend on certain factors.
  The LEO constellation and how many satellites are visible to the ad-hoc MC eNB/gNB.
  The location of the ad-hoc MC eNB/gNB on ground, in relation to the path of LEO constellation.

## Slide 4: Limitations in LEO backhaul
The LEO satellites move w.r.t. earth. Coverage from one satellite to a given point on earth (within coverage footprint) is transient.
  Handovers are needed from one LEO satellite to another along the time axis (diagram).
  In terms of signal strength, there are high and low points between handovers. The backhaul capacity and the QoS that can be provided also varies accordingly.
As the LEO constellation is fixed, these signal strength (and capacity, QoS) variations can be predicted to a high degree of accuracy.
* Enric Juan, Mads Lauridsen, Jeroen Wigard, Preben Mogensen, “Handover Solutions for 5G Low-Earth Orbit
Satellite Networks”, IEEE Access, Vol. 10, 2022.

## Slide 5: MC QoS requirements
When the LEO backhaul is enacted, a mix of MC services (MC PTT, MC data and MC video) with different QoS levels will be provided.
But this service mix and the QoS will need to be mapped to the signal strength and capacity variation of LEO backhaul.
  Some services will have high priority, so they can operate both at high and low capacity points, with some guaranteed QoS.
What information can be provided to the Application layer for QoS and priority management of the service mix?