## Slide 1: Requesting specific location information of MC service user on-demand or periodic via Subscription
Kiran Kapale (kiran.kapale@samsung.com)
Samsung

## Slide 2: Outline
Background
Problem Overview
Option #1 solution description and call flow
Option #2 solution description and call flow
Conclusions

## Slide 3: Background – Location information obtaining
TS 23.280 clause 10.9.3.5 - Location information subscription procedure
TS 23.280 clause 10.9.2.5 - Location information subscription request
TS 23.280 clause 10.9.3.6.2 - On-demand usage of location information procedure
TS 23.280 clause 10.9.2.3 - Location information request
TS 23.280 clause 10.9.3.3 - Client-triggered location reporting procedure
TS 23.280 clause 10.9.2.4 - Location reporting trigger

## Slide 4: Problem Overview – What location information ?
The MC service user can obtain the location information of other MC service user using on-demand request or Periodic via Subscription.
In case of on-demand request:
  The on-demand request is sent to another MC service user and the target MC service user is not configured with Location reporting configuration for what location information is to be reported in emergency or/and non-emergency case – How and what location information is reported ?
  The on-demand request is sent to another MC service user and the target MC service user is configured with Location reporting configuration for what location information is to be reported in emergency or/and non-emergency case – How the desired location information is indicated if the configured location reporting is not meeting the expected location information ?
In case of Periodic via Subscription request:
  The Subscription request is sent to LMS to obtain the location information of another MC service user and the target MC service user is not configured with Location reporting configuration for what location information is to be reported in emergency or/and non-emergency case – How and what location information is reported ?
  The Subscription request is sent to LMS to obtain the location information of another MC service user and the target MC service user is configured with Location reporting configuration for what location information is to be reported in emergency or/and non-emergency case – How the desired location information is indicated if the configured location reporting is not meeting the expected location information ?

## Slide 5: Option #1: Solution description
In case of on-demand request: Location reporting configuration is (not)configured at targeted MC service user
  The MC service user who is requesting can optionally include the desired location information from targeted MC service user.
  Location management server,
    Uses an initial location reporting configuration to the targeted location management clients of MC service users if (not)configured, if requesting MC service user has not indicated any desired location information from targeted MC service user.
    Uses an desired location reporting configuration to the targeted location management clients of MC service users, if requesting MC service user has indicated any desired location information from targeted MC service user.
In case of Periodic via Subscription request: Location reporting (not)configuration is not configured at targeted MC service user
  The MC service user who is subscribing can optionally include the desired location information from targeted MC service user.
  Location management server,
    Provides an initial (if not configured) or update (if configured) location reporting configuration to the targeted location management clients of MC service users, if subscribing MC service user has not indicated any desired location information from targeted MC service user.
    Uses configured or provides an initial (if not configured) or update (if configured) with desired location reporting configuration to the targeted location management clients of MC service users, if subscribing MC service user has indicated any desired location information from targeted MC service user.
In case of Client-triggered location reporting procedure: Above changes are also applicable.

## Slide 6
Option #1: Solution call flow
10.9.2.3 Location information request
10.9.2.5 Location information subscription request
The procedures steps are updated to indicate that location reporting configuration is provided based on the Location information request and added NOTE for further clarification.
The procedures steps are updated to indicate that location reporting configuration is provided based on the Location information request and added NOTE for further clarification.
The detailed updates are captured in the CR 0581

## Slide 7: Option #2: Solution description
In case of on-demand request: Location reporting configuration is configured at targeted MC service user
  The MC service user who is requesting can optionally include the desired location information from targeted MC service user.
  Location management server,
    A pre-condition is added that location reporting configuration to the targeted location management clients of MC service users is already configured.
    Uses initial location reporting configuration to the targeted location management clients of MC service users, if requesting MC service user has not indicated any desired location information from targeted MC service user.
    Uses an desired location reporting configuration(if required) to the targeted location management clients of MC service users, if requesting MC service user has indicated any desired location information from targeted MC service user.
In case of Periodic via Subscription request: Location reporting configuration is configured at targeted MC service user
  The MC service user who is subscribing can optionally include the desired location information from targeted MC service user.
  Location management server,
    A pre-condition is added that location reporting configuration to the targeted location management clients of MC service users is already configured.
    Does not update or provide any location reporting configuration to the targeted location management clients of MC service users, if requesting MC service user has not indicated any desired location information from targeted MC service user.
    Provides an updated (if required) location reporting configuration with desired location reporting configuration to the targeted location management clients of MC service users, if requesting MC service user has indicated any desired location information from targeted MC service user.
In case of Client-triggered location reporting procedure: Above changes are also applicable

## Slide 8
Option #2: Solution call flow
10.9.2.3 Location information request
10.9.2.5 Location information subscription request
The pre-condition, procedures steps are updated to indicate that location reporting configuration is provided based on the Location information request and added NOTE for further clarification.
The pre-condition, procedures steps are updated to indicate that location reporting configuration is provided based on the Location information request and added NOTE for further clarification.
The detailed updates are captured in the CR 0582

## Slide 9: Conclusions
Option 1:
  The LMS will dynamically take action of sending location reporting configuration.
Option 2:
  It is assumed that location reporting configuration already provided.
Option 1 looks better as LMS can decide dynamically instead of pre-condition.
Looking for groups opinion on way forward.

## Slide 10: Thank You!