## Slide 1: Obtain location information from the PLMN operator (core network)
Ericsson
Rana.Alhalaseh@ericsson.com

## Slide 2: Location information from the core network
Stage 1 requirement:
  [R-6.12-002] The MCX Service shall support conveyance of Location information provided by 3GPP location services.
LCS services feature
  TS 23.271 for EPS
  TS 23.273 for 5GS
Notification from PCRF/PCF as part of the PCC mechanism
  TS 23.203 for EPS
  TS 23.503 for 5GS

## Slide 3: Advantages of location reporting from core
GPS in the MC client is the only source to report location information (longitude, latitude) of a user
  GPS is (un-)intentionally disabled, e.g., data security concerns (secretive/high level agents), or simply by mistake
  GPS is not working properly, e.g., out of satellite coverage, user is in a tunnel
  UE is off during the time when a certain trigger should be sent, hence LMC has missed sending location information as the trigger is missed
Advantage Nr. 1: The MC server is always aware of the location of all its MC users, irrespective of possible unforeseen events that may cause limitations/ issues

## Slide 4: Advantages of location reporting from core
Location dependent operations require decisions done by MC server once the LMC has already sent location info properly and correctly
  Possible mistrust of LMC information due to bad configuration/ implementation of LMC (e.g., report when entering but not leaving an area)
  Operations depend on the availability and correctness of location info, as
    Automatic functional alias activation upon entering a predefined area (e.g., cell, TA ID)
    MCPTT private call/ call forward when the target user is identified by functional alias
    Implicit (de-)affiliation to a certain group based on predefined area, e.g., area dependent group communication/ emergency alert/ ad hoc group communication
    Commencement mode group configuration: Geographical area where acknowledgement of all affiliated group members is required before start of audio transmission.
Advantage Nr. 2: The MC server is independent from LMC (including its configuration) for its operations and decision making.
TA: Tracking Area

## Slide 5: Advantages of location reporting from core
The location information is currently sent between the MC system and the MC service client
It is sent irrespective of the network status, e.g., congestion
Advantage 3: location information obtained from the core network can be considered as means to offload radio interface and maintain network resources, especially during network congestion.

## Slide 6: Why location info from core network?
Location information | MC mechanism via LMS-LMC | 3GPP core mechanisms
Type of request | Event triggered and on-demand | Same as in LMS-LMC
Type of events to trigger location reporting | TS 24.379 has defined different events; including, cell/PLMN/SA change, geographical location change | Same as in LMS-LMC. Additionally: UE availability after temporarily unavailable Satellite access/TN change
Geographical location representation | Longitude, latitude, speed | Same as in LMS-LMC. Additionally: Local coordination system Country code (e.g., 1 for USA) Name of area (e.g., London)
Employed mechanism to obtain location information | GPS for geographical location SIB signaling for 3GPP related parameters (e.g., cell ID) | GPS, and non-GPS mechanisms (TS 36.445, TS3 8.455): Cell ID (approx. location based on cell tower location) Cell ID + measurements as Timing Advance, Enhanced Observed Time Difference, beamforming Enhanced cell ID (RSRP, RSRQ, ToA) Advanced 5G measurements (UTDOA, DTDOA, OTDOA)
RSRP: Reference Signal Received Power
RSRQ: Reference Signal Received Quality
ToA: Time of Arrival
UTDOA: Uplink Time Difference of Arrival
DTDOA: Downlink Time Difference of Arrival
OTDOA: Observed Time Difference of Arrival
Notes: Uplink Time Difference of Arrival (UTDOA): Measures the time it takes for a signal to travel from the UE to multiple base stations.
Downlink Time Difference of Arrival (DTDOA): Measures the time difference for a signal to reach the UE from multiple base stations.
Observed Time Difference of Arrival (OTDOA): Involves measuring the time difference of arrival of signals from multiple cells.

## Slide 7: Thank You!