## Slide 1: CAPIF application backend
Walter Featherstone
Apple

## Slide 2: Outline
Highlight the SA3 feedback on solution 1 of TR 23.700-22
Provide motivation for consideration of a backend architecture
Highlight the need to expose a user identifier for resource owner authorization

## Slide 3: SA3 feedback
S3-244340: Reply LS on CAPIF phase 3 security considerations
  SA6 Q6: Solution #1: Whether SA3 would consider supporting the BFF patten in Rel-19?
  SA3 response: BFF patten issue is not captured in the scope of TR 33.700-22 v.0.1.0. If SA3 decides to study it in the scope of TR 33.700-22, SA3 will inform SA6.
SP-240654: Study on security aspects of CAPIF Phase 3
  The objective is to study security enhancement of CAPIF for 3GPP northbound APIs.
  WT: To investigate the security impacts and study potential solutions for the Rel-19 CAPIF enhancement studied in SA6 (Study on CAPIF Phase 3).
  NOTE: SA3 study depends on SA6 study progress.

## Slide 4: TS 33.122
6.5.3.3 Authorization using authorization code (optional PKCE) flow
If authorization code flow, optionally with PKCE, is used by the AEF for authorization of the API invoker, the procedures in RFC 6749 [4] and optionally RFC 7636 [11] shall be followed, with the following profile:
- The authorization token and/or authorization request may include the resource owner ID.
NOTE: If the API invoker is on a UE, the CCF obtains its GPSI during authentication.
Editor's note: the mapping of API Invoker ID and GPSI is left for stage 3.
- The resource owner dynamically authorizes the API invoker to access the resource owner's resources as described in RFC 6749 [4] and optionally RFC 7636 [11].
- If the API invoker is on a UE, the CCF shall check that the UE is accessing its own resources. The access token shall contain the resource owner ID (i.e. GPSI) and the API invoker ID. If the API invoker is an AF not on a UE, the check is omitted.
As an aside, it not clear under what circumstances the OAuth “client credentials” flow of 6.5.3.3 applies for a UE hosted API invoker, since such an invoker appears as an OAuth classified “public” client

## Slide 5: Frontend only solution vulnerabilities
Implicit Flow
  Token Transmission via URL
  Lack of Refresh Token Support
  Persistent Token Theft
  Acquisition and Extraction of New Tokens Proxying Requests via the User's Browser
Authorization Code Flow with PKCE
  Token Transmission via URL
  Lack of Refresh Token Support
  Persistent Token Theft
  Acquisition and Extraction of New Tokens Proxying Requests via the User's Browser

## Slide 6: Backend solutions
OAuth responsibilities are handled by a backend component, e.g.,
  Backend For Frontend: Frontend requests are proxied through the the backend component and
  Token-Mediating Backend: Frontend requests are made directly to the resource server
SA3 TR 33.700-22: Study on security aspects of CAPIF Phase3
  Solution #25: Backend based solution for UE-deployed API invoker accessing resources not owned by that UE: In the real word application deployments, it is very common practice to have a backend server in addition to the ACs running/installed on end point devices such as mobile phones.
    States that the backend server handles the resource owner authorization in the application layer
    CAPIF-8 has been specified in 23.222 where its capabilities include “providing authorization for resource access”.
    A resource owner could be expected to be provided with a user identifier before granting authorization for resource access

## Slide 7: Vulnerabilities addressed by backend solution
Authorization Code Flow with Token-Mediating Backend
  Code Interception Attack
  Persistent Token Theft
  Proxying Requests via the User's Browser
Authorization Code Flow with Token-Mediating Backend and PKCE
  Code Interception Attack
  Persistent Token Theft
  Proxying Requests via the User's Browser
Authorization Code Flow with PKCE and BFF
  Code Interception Attack
  Persistent Token Theft
  Proxying Requests via the User's Browser

## Slide 8: Backend for frontend
Solution 1 of 23.700-22 provides a representation of the CAPIF architecture that includes a backend component
  The API invoker in considered to comprise of a frontend and backend, where the backend takes responsibility for the OAuth responsibilities
  It is proposed to capture such an architectural deployment into the CAPIF, i.e., into TS 23.222

## Slide 9: Summary / highlights
LS response from SA3
OAuth flows specified by SA3
Security limitations with frontend only based solutions
Overview of introducing a backend component
  Potential requirement for the backend component to expose a user identity to the authorization function, but that’s considered in scope of SA3
Vulnerabilities addressed by backend solution
Architecture of the backend solution
  It is proposed to capture that variant in TS 23.222