| 3GPP TSG-T3 (USIM) Meeting #13 Tokyo, Japan, 21 - 24 February, 2000 | Tdoc T3-000063 |
| --- | --- |
| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | TS 31.101 | CR | xxx | Current Version: | V3.0.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submission to TSG | T # 7 | for approval | x | (only one box should |
| list TSG meeting no. here ( | For information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM | x | ME |  | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Schlumberger | Date: | 04/02/00 |
| Subject: | Indication of the UMTS application state to the USIM (initialised, terminated) |
| 3G Work item: |  |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature | X |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | The states of the UICC and of the ME need to be synchronized, so that both entities can allocate the USIM resources in the critical phase like the initialization, start all the linked processes or terminate them and free all the allocated resources. For USIM application initialization the steps are : start of USIM initialization procedure : ME informs the card by sending the APDU command Select AID with USIM AID end of USIM initialization procedure : This CR proposes that the ME sends the APDU command Status with P1 value. The USIM/UICC needs to be informed of the closure of UMTS application so that all allocated resources can be freed and associated process informed of this closure. As the use of these synchronization steps can be used by other application develop on the top of the UICC it is proposed to extend the definition of the Status APDU. |
| Clauses affected: | 11.2 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

## 11.2	STATUS

### 11.2.1	Functional description

This function indicates to the selected application its state in the Terminal and returns information concerning the current directory.

## Input:

-	Current/selected application state in the ME.

## Output:

- ID of the current directory, total memory space available, PIN enabled/disabled indicator, PIN status and other system specific data (identical to SELECT).

### 11.2.2	Command parameters

| Code | Value |
| --- | --- |
| CLA | As specified in 10.1.1 |
| INS | As specified in 10.1.2 |
| P1 | Current application state, see Table 11.x |
| P2 | 00 |
| Le | Empty, '00', or maximum length of data expected in response |

# Table 11.x: Coding of P1

| b8 | b7 | b6 | b5 | b4 | b3 | B2 | b1 | Meaning |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | No change |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | Current application is initialised in the ME |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | Current application is terminated in the ME |

Response parameters and data are identical to the response parameters and data of the SELECT command in case of MF or DF.