## Slide 1: LTE evolution
Asbjörn Grövlen
Ericsson

## Slide 2: Overview
LTE is submitted as part of the SRIT to IMT-2020
What has happened in LTE since the IMT-Advanced submission?
  Lots!

## Slide 3: Coordinated Multi-Point Operation
Introduced coordination across antenna points
  Reducing inter-cell interference, improving coverage
Many coordination schemes require fast backhaul
Rel-11→
Intra-site coordination only (Rel-11)
coordination
coordination
coordination
Inter-site coordination (Rel-12)
coordination
Coordination
different resources scheduled
Dynamic Point Blanking
Coordination
Null forming
Coordinated Beamforming
Simultaneous transmission
Joint transmission
Dynamic switching
Dynamic Point Selection
Coordinated Link Adaptation
Coordination

## Slide 4: Enhanced downlink control channel
PDCCH is
  always full bandwidth
  using common reference signal (CRS)
EPDCCH introduced to support
  increased control channel capacity
  frequency-domain ICIC
  improved spatial reuse of control channel resource
  beamforming and/or diversity
The EPDCCH can
  be transmitted multiplexed with PDSCH
  coexist with legacy UEs on the same carrier
DMRS are used for demodulation
Rel-11→

## Slide 5: Dual connectivity
Control and user plane separation
  DL (Rel-12)
  UL (Rel-13)
Benefits
  Increased mobility robustness
  Minimize UE context transfer
  Minimize re-establishment failures
Split bearer
  Data is split on the PDCP layer
  Transparent to higher layer protocols
  Service specific offloading
Rel-12→

## Slide 6: Small cells
Dynamic TDD (eIMTA)
  Certain subframes within the radio frame can be dynamically switch between UL and DL
256QAM
  1024 QAM also supported in DL
Allow small cells to be turned on/off with low latency
  Discovery signal
Radio interface based inter-cell synchronization
Rel-11→

## Slide 7: Proximity services (ProSe) and vehicle-to-everything (V2X)
The introduction of the sidelink interface enables direct UE-to-UE communications
The cellular interface was enhanced to handle efficiently unicast and broadcast traffic
Use cases
  Mission critical push-to-talk for first responders (ProSe, Rels. 12-13)
  Discovery (ProSe, Rels. 12-13)
  Vehicular day-1 safety services such as CAM and DENM (V2X, Rel. 14)
  Truck platooning, advanced driving, vehicle sensor sharing (V2X, Rel. 15)
Rel-12→
Features
  UE-autonomous resource allocation and NW-managed resource allocation for sidelink
  Distributed synchronization for operation outside network coverage
  New physical layer format for high mobility scenarios (V2X)
  Aggregation of multiple sidelink carriers
  New cellular multicast periodicities for reduced latency

## Slide 8: Licensed-Assisted Access
Rel-13 Licensed assisted access
  Enable gigabit throughput LTE via carrier aggregation framework
  Downlink only access to 5 GHz unlicensed bands
Rel-14 Enhanced LAA
  Introduce scheduled uplink access to unlicensed bands
Rel-15 Further enhanced LAA
  Enhance uplink access throughput and latency with configured grants (aka “autonomous UL”)
UL
DL
Primary Carrier Licensed Spectrum
Secondary Carrier Unlicensed Spectrum
Rel-13→

## Slide 9: Elevation Beamforming/ Full-Dimension MIMO
With the introduction of advance antenna systems with more antenna elements, exploiting all three dimensions for MIMO becomes possible
A 3D channel model was developed
Feature components
  Increased number CSI-RS ports to 12 and 16
  Beam selection
  SRS enhancements for low delay spread channels
  DMRS enhancements to increase the number of co-scheduled UEs
- UE height: 1.5-22.5m
- eNodeB height: 25m
- ISD 500m
3GPP 3D UMa
3GPP 3D UMi
- UE height: 1.5-22.5m
- eNodeB height: 10m
- ISD 200m
Rel-13→

## Slide 10: Shortened TTI and processing time
Shortened TTI and processing time for LTE introduces the possibility for subslot- (2 or 3 symbols long) and slot-based transmission, each associated with a short processing time.
A shortened processing time of n+3 (compared to n+4) has also been introduced for subframe-based transmissions
DL and UL control channels have been redesigned (SPDCCH and SPUCCH for UL and DL respectively) ensuring backwards compatibility with existing LTE operation
Higher layer improvements to latency have also been introduced
Rel-15

## Slide 11: Summary
Continuous enhancements have improved LTE meeting the IMT-2020 requirements of a component RIT