3GPP TSG-RAN4 Meeting #111 R4-2410333 Fukuoka, Japan, May 20 – 24, 2024 CR-Form-v12.2 CHANGE REQUEST 38.133 CR draft rev Current version: 18.5.0 For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests.

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | [draftCR IR2] CR for inter-RAT EUTRAN measurements case b-1 without gap |
| --- | --- |
| Source to WG: | Xiaomi |
| Source to TSG: | R4 |
| Work item code: | NR_MG_enh2-Perf |  | Date: | 2024-5-22 |
| Category: | B |  | Release: | Rel-18 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | According to the agreed WF R4-2403543, a test case for inter-RAT EUTRAN measurements case b-1 with MG but no DRX configuration is needed (IR2) |
| Summary of change: | Define a test case for inter-RAT EUTRAN measurements case b-1 with MG but no DRX configuration. |
| Consequences if not approved: | The RRM requirements cannot be verified in realistic environment. |
| Clauses affected: | A.6.6.x |
|  | Y | N |  |  |
| Other specs |  |  | Other core specifications | TS/TR ... CR ... |
| affected: | X |  | Test specifications | TS 38.533 |
| (show related CRs) |  |  | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

| This CR's revision history: |  |
| --- | --- |

--------------START OF CHANGES #1--------------

#### A.6.6.x.y	SA NR - E-UTRAN event-triggered reporting without gap under non-DRX in FR1

##### A.6.6.x.y.1	Test Purpose and Environment

The purpose of this set of tests is to verify that the UE makes correct event-triggered reporting of inter-RAT E-UTRAN measurements without gap as there are vacant RF chains available for UE measurements when operating in standalone (SA) operation with PCell in FR1. This test shall partly verify the cell search and measurement requirements in Clauses 9.4.8, and also verify the scheduling availability during inter-RAT measurement without gap in clause 9.4.8.3.5.

The serving frequency and the target frequency should be selected such that UE reports no-gap-no-interruption via NeedForInterruptionInfoNR-r18’ for the target frequency given the serving frequency and ‘[32-6 to supportEMWconifugation]’.

##### A.6.6.x.y.2	Test parameters

In each test there are two cells: Cell 1 and Cell 2. Cell 1 is the NR PCell and Cell 2 is an inter-RAT E-UTRAN inter-RAT neighbour cell. In the measurement control information from the PCell it is indictated to the UE that event-triggered reporting with Event B2 (PCell becomes worse than threshold1 and inter RAT neighbour becomes better than threshold2) is to be used. Each test consists of two consecutive time periods, with durations T1 and T2, respectively. Prior to the start of time duration T1, the UE shall be fully synchronized to Cell 1. During T1, the UE shall not have any information on Cell 2.

Supported test configurations are give in table Table A.6.6.3.2.1-1 [and additional parameters for EMW configuration in table Table A.6.6.x.y.2-1] . General test parameters are provided in Table Table A.6.6.3.2.1-1. Test parameters for Cell 1 and Cell 2, valid for both time duration T1 and T2, are provided in Tables Table A.6.6.3.2.1-3 and Table A.6.6.3.2.1-4, respectively.

Table A.6.6.x.y.2-1: Additional PCell specific test parameters for SA inter-RAT E-UTRA without gap event triggered reporting in non-DRX with PCell in FR1

| Parameter | Unit | Configuration | Cell 1 |
| --- | --- | --- | --- |
|  |  |  | T1 | T2 |
| [EMW configuration] |  | 1, 2, 3, 4, 5, 6 | [EMW configuration #1 |

##### A.6.6.x.y.3	Test Requirements

The actual overall measurement delay requiremetns can refere to the requirements in A.6.6.3.1.2. And during T1 and T2, UE shall send HARQ ACK/NACK for the corresponding PDSCH scheduled in PCell based on the requirements defined in 9.4.8.3.5.

----------------END OF CHANGES #1--------------

# Comments

shceulding restriction depending on different EMW