3GPP TSG-RAN WG4 Meeting #111	R4-2409906
Fukuoka City, Fukuoka, Japan, 20th – 24th May, 2024

Title:	Reply LS on 3GPP NR TRP TRS OTA requirements

Response to:		R4-2407017/CAG-24-217r3

Release:	Rel-18, Rel-19

Work Item:	NR_FR1_TRP_TRS_enh, TRP_TRS_MIMO_OTA_Ph3

Source:	3GPP RAN4

To:	GCF CAG

Cc:	3GPP RAN Plenary, 3GPP RAN5, ETSI MSG TFES, GCF PAG, CTIA OTA WG, GSMA TSG-AP, NGMN Alliance, PTCRB, CCSA TC9 WG1

Contact person:	Ruixin Wang

ruixin.wang@vivo.com

Anatoliy Ioffe

anatoliy.ioffe@apple.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

# 1	Overall description

3GPP RAN4 would like to thank GCF CAG for their LS in R4-2407017/CAG-24-217r3 on requirements work for 5G NR FR1 TRP TRS OTA.

In Rel-18 WI, RAN4 has already concluded some requirements work on following scope [1][2]:

- Requirements to BHH (Beside Head and Hand)

- TRP for devices with Power Class 3

- Some bands listed in GCF LS, i.e., n1, n28

Meanwhile, 3GPP also approved a new Rel-19 Work Item as TRP_TRS_MIMO_OTA_Ph3 in RAN#103 meeting, March 2024 [3], targets enhanced OTA test methodologies and more requirements for NR OTA, the FR1 TRP TRS requirements working scope can be summarized as:

- More bands for BHH and Hand only, e.g., n3, n5, n7, n8, n77, n79

- Requirements for device narrower than 72mm is also considered in Rel-19

- TRP TRS requirements for UE configured with 2Tx non-coherent UL-MIMO at bands n41 and n78

- 2Tx coherent UL-MIMO requirements are not precluded if commercial devices and corresponding phantom are available

RAN4 recommends 3GPP RAN to discuss including bands n38, n20 into the scope of the currently ongoing Rel-19 work item.

3GPP RAN4 would like to keep collaboration with GCF CAG on FR1 TRP TRS OTA work.

# 2	Actions

To GCF CAG:

ACTION: 	3GPP RAN4 respectfully asks GCF CAG to take the above feedback into account when developing 5G NR FR1 OTA antenna conformance testing.

# 3	Dates of next TSG-RAN WG4 meetings

TSG-RAN WG4 Meeting #112                           	 19-23 August, 2024    		     Maastricht , NL

TSG-RAN WG4 Meeting #112bis	 14-18 Oct, 2024 				     China

# 4	References

- R4-2409907, CR to TS 38.161 on FR1 TRP TRS requirements, vivo, RAN4#111, May 2024.

- R4-2409905, CR to TS38.161 on PC3 scaling of the TRP requirement, Apple, RAN4#111, May 2024

- RP-240841, New WID: WI on TRP (Total Radiated Power), TRS (Total Radiated Sensitivity) and MIMO OTA (Over the Air) testing enhancement Phase 3, vivo, CAICT, RAN#103, March 18-21, 2024