## Slide 1: xxx
xxx

## Slide 2: Background:SA WG2/SA WG5 Energy Efficiency
3.3 | - | - | - |  | - | - | - | Docs:=7
3.3 | SP-240718 | DISCUSSION | Agreement | Way Forward for SA WG2 EnergySys | Samsung, Lenovo, CATT, China Mobile, ETRI, Hisillicon, Huawei, Intel, InterDigital, KPN, KT Corp., LG Uplus, MediaTek, NEC, NTT DOCOMO, OPPO, ORANGE, Rakuten Mobile, SK Telecom, Toyota, Vivo, ZTE | Rel-19 |  | 
3.3 | SP-240890 | DISCUSSION | Approval | Work split between SA WG2 and SA WG5 for the Energy Efficiency topic | Qualcomm Incorporated | Rel-19 | FS_EnergySys | 
3.3 | SP-240899 | DISCUSSION | Agreement | Discussion on Working Scope Separation for Energy as Service Criteria between SA WG2 and SA WG5 | Lenovo, KDDI | Rel-19 |  | 
3.3 | SP-240918 | DISCUSSION | Agreement | Analysis of Status of SA WG2 study FS_EnergySys & Proposed Way Forward | Ericsson | Rel-19 | FS_EnergySys | 
3.3 | SP-240719 | WID NEW | Approval | WID on Energy Efficiency and Energy Saving | Samsung, Lenovo, CATT, China Mobile, ETRI, Hisilicon, Huawei, Intel, InterDigital, KPN, KT Corp., LG Uplus, MediaTek, NEC, NTT DOCOMO, OPPO, ORANGE, Rakuten Mobile, SK Telecom, Toyota, vivo, ZTE | Rel-19 |  | 
3.3 | SP-240910 | WID NEW | Approval | New WID on Energy Efficiency and Energy Saving | Nokia | Rel-19 |  | Related to SP-240719
3.3 | SP-240612 | DRAFT TR | Approval | Presentation of TR 23.700-66 to TSG SA for approval | SA WG2 | Rel-19 | FS_EnergySys | 

## Slide 3: Options on the table
3 different way forward proposals
  SP-240718 by Majority
    Follow majority view in SA2 and approval the WID (new functionality to be defined in SA2)
  SP-240918 by Ericsson
    TSG SA can ask to reuse SA5 defined functionality as applicable or alternatively ask SA2 to avoid developing
  SP-240890 by QC
    First discuss the Work split between SA2 and SA5

## Slide 4: WT#1
collection and calculation of energy consumption
exposure of energy consumption
Different granularity | SA2 | SA5
NF |  | √(OAM, existing)
Network slice |  | √(OAM, existing)
UE based on data volume | √(new) | √(new)
per-UE-per-QoS flow(including per application) based on data volume | √(new) | √(new)
Renewable energy info (applies to all granularities above) | √(new) | √(new)
Different granularity | SA2 | SA5
Network slice |  | √(OAM, existing)
UE | √(new) | √(new)
per-UE-per-QoS flow(only internal exposure to 5GC NF) | √(new) | √(new)
Renewable energy info (applies to all granularities above) | √(new) | √(new)

## Slide 5: WT#2
WT #2. The objective of this WT is to specify the enhancements for subscription and policy control to enable network energy savings as service criteria based in WT#1. The following enhancements will be specified:
  The definition of energy saving subscription information per UE that is stored as part of the subscription data in the UDM/UDR, to assist the network to perform energy saving strategies for the UE
  The detailed procedures for the PCF to receive UE subscription data and notification related to the energy related information to trigger making policy decisions (reusing the existing parameters)
  NOTE 9: Further details and what energy related information can be taken into account for policy control will be defined during the normative work.
  NOTE 10: Detailed parameters and associated policy procedures will be discussed during the normative work.
  NOTE 11: The interaction for PCF with CHF for policy control and charging (e.g. how the PCC rules are determined based on energy criteria) will be considered in the normative phase, based on collaboration with SA5.

## Slide 6: WT#3
WT #3. The objective of this WT is to specify the 5GS enhancements to support network energy saving and efficiency based on WT#1. The following enhancements will be specified:
  Enhancements of NF discovery and (re-)selection based on energy related information
  New energy related information and/or existing NF profile parameters in the NF Profile to allow an operator to influence NF discovery and selection based on their energy strategy
  NOTE 12: Which energy related information is included in the NF profile is to be further discussed in the normative phase. Only parameters captured in existing solutions will be considered. Coordinated with SA WG5 may be needed.
  NOTE 13: The information within NF profile is expected not to change frequently, e.g., constantly reflecting changes in energy consumption. The procedure for updating the information will be addressed in normative phase.
  Enhancement on NF discovery and (re-)selection to consider the energy related information from the NF profiles and/or discovery request from the NF consumer
  Enhancements on existing operations and procedures for energy saving and energy efficiency: The optional UP path adjustment for a PDU session(s) will be specified.
  NOTE 14: Whether other existing procedures and operations are enhanced for energy saving and energy efficiency will be decided in the normative phase.
  NOTE 15: The energy related decision will also consider operator’s policy.

## Slide 7: Way Forward
Joint SA2+SA5 CC ahead of the next WG meeting
  Well organize the agenda and the questions to be discussed during the CC