## Slide 1: SoH Questions for R19 FS_AIML_CN
vivo (Rapporteur) MediaTek Inc. (Rapporteur)

## Slide 2: SoH for KI#1: Enhancements to LCS to support Direct AI/ML based Positioning
Q1: Which entity is enhanced to perform model training?
  Option A: LMF is enhanced to perform model training. LMF supports UE positioning based on AIML model trained with RAN and UE data. The trigger for data collection and for model training in LMF is up to implementation.
    Yes:
    No:
  Option B: MTLF is enhanced to perform model training
    Yes:
    No:
  Option C: Option A + Option B
    Yes:
    No:
Way forward: go with Option C
Result: Option C selected for normative work (no objections raised).
Q2: Which entity is to perform ML-based UE positioning?
  Option A: enhanced LMF is to perform Location Calculation based on the ML model
  Option B: LMF(collocated with enhanced AnLF) is to perform Location Calculation based on the ML model
  Way forward: enhanced LMF is to perform location calculation based on the ML model. The interaction between LMF and MTLF is only for model provisioning and possibly, based on coordination with RAN WGs, for data collection for training.
  Result: Option A selected for normative work (no objections raised).

## Slide 3: SoH for KI#3: NWDAF-assisted policy control and QoS enhancement
Q0: Which of the following options shall we support with respect to the relation between the candidate QoS parameters and input QoS parameters provided by the PCF, if available?
  Option A: the candidate QoS parameters are ONLY from the input QoS parameters provided by the PCF (i.e., NWDAF does NOT provide recommendations). (2 objections: Huawei, CATT)
    Yes: 12
    No: 2
  Option B: the candidate QoS parameters can be different from the input QoS parameters provided by the PCF (i.e., NWDAF does provide recommendations). (4 objections: Nokia, MediaTek, Ericsson, Qualcomm)
    Yes: 8
    No: 8
Way forward: work on Option A when updating pCR
Q1: Which of the following options shall we support with respect to NWDAF providing candidate QoS parameters?
  Option A: NWDAF provides candidate QoS parameters with a new service (2 objections: Nokia, Ericsson)
    Yes: 10
    No: 3
  Option B: NWDAF provides candidate QoS parameters with a new Analytic ID supported by existing services (1 objection: Huawei)
    Yes: 12
    No: 2

## Slide 4: BACKUP