## Slide 1: SoH questions on FS_NG_RTC_Ph2 Conclusions
China Mobile (Rapporteur)

## Slide 2: KI#1: Event subscription and notification
It has been discussed in drafting session whether non-subscriber specific events are in the scope and companies are OK to keep in in the conclusions; it is also agreed that the subscription of non-subscriber events is directly from the consumer to all the possible producers
This remaining issue is about subscriber specific events on how the event consumer, i.e. DC AS, subscribes events from the event producer, i.e. IMS AS, inlcuding how the consumer discovers producer and how the event is subscribed.
The alternative options for event producer discovery are as follows:
  Option 1: HSS based
    the event producer registers itself in HSS and the consumer queries HSS to discover event producer
  Option 2: NRF based
    the event producer registers itself in NRF and the consumer queries NRF to discover event producer
  Option 3: implicit subscription with no discovery needed
    the event is implicitly subscribed to event producer through subscription data in HSS, so no need for event consumer to discover event producer

## Slide 3: KI#1: Event subscription and notification (Cont’)
The alternative options for event subscription are as follows:
  Option 1: HSS based
    The consumer subscribes subscriber related events via HSS and non-subscriber evnets directly to event producer
  Option 2: directly
    The consumer subscribes event directly from event producer
  Option 3: subcription data based
    no need to subscribe event. Instead the event producer discover the subscribed events based on the event subscription data

## Slide 4: KI#1: Event subscription and notification
SoH question on event producer discovery are as follows:
  Option 1: HSS based solution is supported
    Yes:
    No:
  Option 2: NRF based solution is supported
    Yes:
    No:
  Option 3: implicit subscription solution is supported
    Yes:
    No:
SoH question on event subscription are as follows:
  Option 1: HSS based solution is supported
    Yes:
    No:
  Option 2: Direct subscription solution is supported
    Yes:
    No:
  Option 3: implicit subscription solution is supported
    Yes:
    No:

## Slide 5: KI#2: IMS capability exposure
Q1: Shall the IMS session management request from the DC AS be sent to the IMS AS via DCSF?
  Yes:
  No:
Q2: Shall the IMS session management request from the DC AS be sent to the IMS AS directly?
  Yes:
  No:

## Slide 6: KI#6: Standalone Data Channel
Q1: Shall capability negotiation for standalone data channel be supported?
  Yes
  No
Q2: How to avoid long lasting sessions?
  Option 1: by user
    Yes:
    No:
  Option 2: using session timer mechanism
    Yes:
    No:
Q3: Is Standalone DC a new service or part of MMTel?
  New service
    Yes:
    No:
  Part of MMTel
    Yes:
    No:
Q4: how terminating UE behaves in case of combination of standalone BDC and standalone ADC, when the terminating UE has not downloaded the DC App
  Option 1: answers to accept BDC first then downloads that DC App
  Option 2: downloads that DC App first then answers to accept both BDC and ADC together
  Option 3: operates Option 1 or Option 2 based on terminating side local configuration

## Slide 7: KI#8: Avatar communication
In the draft session discussion, it is agreed to support rendering at the UE which does not own avatar representation for remote UE
It is also agreed that avatar ID list is downloaded by DCSF via bootstrap DC
This remaining issues is which NF connects directly with DAR to download the avatar representation
SoH question: which network function the DAR need to be connected to provide the avatar representation?
  Option 1: DC AS connects to DAR
    Yes:
    No:
  Option 2: DCSF connects to DAR
    Yes:
    No:
  Option 3: MF connects to DAR
    Yes:
    No:

## Slide 8: KI#5: PS data off for data channel
Q1: Shall application level PS Data Off management be supported?
  Yes:
  No:

## Slide 9: KI#3: Data Channel Interworking
Q1: Shall the scenario of MTSI UE accessing DC application via hyperlink provided in SMS be supported?
  Yes:
  No:
Q2: Shall interworking of MTSI UE initiating a session to DCMTSI UE be supported?
  Yes:
  No:

## Slide 10
Thanks!