## Slide 1: SoH questions on FS_NG_RTC_Ph2 Conclusions
China Mobile (Rapporteur)

## Slide 2: KI#1: Event subscription and notification
It has been discussed in drafting session whether non-subscriber specific events are in the scope and companies are OK to keep in in the conclusions; it is also agreed that the subscription of non-subscriber events is directly from the consumer to all the possible producers
This remaining issue is about subscriber specific events on how the event consumer, i.e. DC AS, subscribes events from the event producer, i.e. IMS AS, inlcuding how the consumer discovers producer and how the event is subscribed.
The alternative options for event producer discovery are as follows:
  Option 1: HSS based
    the event producer registers itself in HSS and the consumer queries HSS to discover event producer
  Option 2: NRF based
    the event producer registers itself in NRF and the consumer queries NRF to discover event producer
  Option 3: implicit subscription with no discovery needed
    the event is implicitly subscribed to event producer through subscription data in HSS, so no need for event consumer to discover event producer

## Slide 3: KI#1: Event subscription and notification (Cont’)
The alternative options for event subscription are as follows:
  Option 1: HSS based
    The consumer subscribes subscriber related events via HSS and non-subscriber evnets directly to event producer
  Option 2: directly
    The consumer subscribes event directly from event producer
  Option 3: subcription data based
    no need to subscribe event. Instead the event producer discover the subscribed events based on the event subscription data

## Slide 4: KI#1: Event subscription and notification
SoH question on event producer discovery are as follows:
  Option 1: HSS based solution is supported
    Yes:
    No:
  Option 2: NRF based solution is supported
    Yes:
    No:
  Option 3: implicit subscription solution is supported
    Yes:
    No:
SoH question on event subscription are as follows:
  Option 1: HSS based solution is supported
    Yes:
    No:
  Option 2: Direct subscription solution is supported
    Yes:
    No:
  Option 3: implicit subscription solution is supported
    Yes:
    No:

## Slide 5: KI1 Questions for SoH (1 of 2)
Question 1. The alternative options for event producer discovery are as follows. Which option(s) shall be supported?
  Option 1: HSS based (the event producer registers itself in HSS and the consumer queries HSS to discover event producer)
    Yes: 4
    No: 2
  Option 2: NRF based (the event producer registers itself in NRF and the consumer queries NRF to discover event producer
    Yes: 1
    No: 5
  Option 3: implicit subscription with no discovery needed (the event is implicitly subscribed to event producer through subscription data in HSS, so no need for event consumer to discover event producer)
    Yes: 3
    No: 4
Option 1 taken as basis for pCR update

## Slide 6: KI1 Questions for SoH (2 of 2)
Question 2. The alternative options for event subscription are as follows. Which option(s) shall be supported?
  Option 1: HSS based (The consumer subscribes subscriber related events via HSS and non-subscriber events directly to event producer)
    Yes: 3
    No: 5  3 objections (Huawei, Samsung, ZTE)
  Option 2: direct subscription (The consumer subscribes event directly from event producer)
    Yes: 4
    No: 4  3 objections (Nokia, Ericsson, Huawei)
  Option 3: subscription data based (no need to subscribe event. Instead, the event producer discover the subscribed events based on the event subscription data)
    Yes: 3
    No: 4  4 objections (Samsung, Qualcomm, Ericsson, Nokia)

## Slide 7: KI#2: IMS capability exposure: not asked
Q1: Shall the IMS session management request from the DC AS be sent to the IMS AS via DCSF?
  Yes:
  No:
Q2: Shall the IMS session management request from the DC AS be sent to the IMS AS directly?
  Yes:
  No:

## Slide 8: KI#6: Standalone Data Channel: only first one asked
Q1: Shall capability negotiation for standalone data channel be supported?
  Yes: 3
  No: 5
Q2: How to avoid long lasting sessions?
  Option 1: wait for user to terminate session
    Yes:
    No:
  Option 2: using session timer mechanism
    Yes:
    No:
Q3: Is Standalone DC a new service or part of MMTel?
  New service
  Part of MMTel
Q4: How does a terminating UE behave in case of combination of standalone Bootstrap DC and standalone Application DC when the terminating UE has not downloaded the DC App?
  Option 1: answers to accept BDC first then downloads that DC App
  Option 2: downloads that DC App first then answers to accept both BDC and ADC together
  Option 3: operates Option 1 or Option 2 based on terminating side local configuration
No need for capability indication taken as basis for pCR update

## Slide 9: KI#8: Avatar communication: asked
In the draft session discussion, it is agreed to support rendering at the UE which does not own avatar representation for remote UE
It is also agreed that avatar ID list is downloaded by DCSF via bootstrap DC
This remaining issue is about which NF connects directly with DAR to download the avatar representation
Question 1: in case the avatar representation needs to be downloaded to the MF, to which network function the DAR needs to be connected to provide the avatar representation to the MF?
  Option 1: DC AS connects directly to DAR (3 objections by Samsung, ZTE and Qualcomm)
    Yes: 2
    No: 3
  Option 2: DCSF connects directly to DAR (3 objections by Nokia, Ericsson and Qualcomm)
    Yes: 4
    No: 3
  Option 3: MF connects directly to DAR (2 objections by Samsung and Ericsson)
    Yes: 4
    No: 3

## Slide 10: KI#5: PS data off for data channel: not asked
Q1: Shall application level PS Data Off management be supported?
  Yes:
  No:

## Slide 11: KI#3: Data Channel Interworking: asked
Q1: Shall the scenario of MTSI UE accessing DC application via hyperlink provided in SMS be supported?
  Yes: 2
  No: 5
Q2: Shall interworking of MTSI UE initiating a session to DCMTSI UE be supported?
  Yes:4
  No:4

## Slide 12
Thanks!