SA WG2 Meeting #163	S2-2406143

# Jeju, South Korea, 27 - 31 May 2024

Source:	OPPO

Title:	KI#1, Conclusion on KI#1

Spec:	3GPP TR 23.700-06

Agenda item:	19.6

Work Item / Release:	FS_VMR_Ph2 / Rel-19

Document for:	Approval

Abstract of the contribution: This contribution is to provide the conclusion on KI#1.

1. Introduction

In the architecture assumption part,

-	the MWAB may connect to an NG-RAN of a PLMN or an SNPN;

-	the MWAB-gNB may broadcast a PLMN ID that is different to the PLMN ID of the PLMN that the MWAB-UE is connected to;

Then it is possible that the PLMN ID the MWAB-gNB broadcasts is not in the set of the PLMN IDs the gNB broadcasts.  For example, the NG-RAN broadcasts MCC, MNC. If the MWAB-UE’s PLMN does not have control the broadcast info of the MWAB-gNB, the MWAB-gNB can even broadcast MCC+MNC in a different country. The UE may perform the PLMN selection to those MWAB-gNB’s PLMN, especially for those roaming UEs. This may not be aligned with the relagutory requirement.

Since the MWAB-gNB is using BH PDU session in the PLMN ID of MWAB- UE, the PLMN of the MWAB-UE should be aware of the broadcast info. of the MWAB-gNB and can control the broadcast info. of the MWAB-gNB. This is to ensure that the broadcast info. (e.g. MCC, MNC) is allowed in the located country.

The above is also linked to the question#28-3 in the NWM discussion:

Question 28: Can we add the following to the principles for KI#1?

1. OAM server address is assumed to be configured on MWAB-gNB.

2. The AMF address is assumed to be configured by the OAM server to the MWAB-gNB.

3. MWAB-UE’s PLMN should NOT be assumed to have control of MWAB-gNB’s configurations (as it can be serving a different PLMN).

4. MOCAN should be supported by MWAB-gNB.

Please also provide further explanations on why you suggest/not support the principles.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-06.

* * * * First Change * * * *

## 8.1	KI#1 Conclusion

It is proposed to proceed normatively based on these principles.

-	the MWAB-UE may connect to an NG-RAN of a PLMN or an SNPN:

a)	if the MWAB-UE is connected to an NG-RAN of PLMN, the MWAB-gNB may broadcast a PLMN ID that is different to the PLMN ID of the PLMN that the MWAB-UE is connected to. The PLMN that the MWAB-UE is connected to have control of MWAB-gNB’s configurations to ensure the PLMN ID is broadcasted by the MWAB-gNB in the location;

b)	if the MWAB-UE is connected to an NG-RAN of PLMN, the MWAB-gNB may broadcast a SNPN ID where the PLMN ID in the SNPN ID may be different to the PLMN ID of the PLMN that the MWAB-UE is connected to.

c)	if the MWAB-UE is connected to an NG-RAN of SNPN, the MWAB-gNB may broadcast a SNPN ID that is different to the SNPN ID that the MWAB-UE is connected to.

d)	a dedicated SNPN ID or GIN ID as defined in the existing mechanism can be used to control the UE to access the MWAB-gNB if only the type of MWAB-gNB are within the SNPN or the GIN network.

e)	Validity information as defined in the localized service in Rel-18 can be used to control the UE to access the MWAB-gNB if both marco gNB and MWAB are deployed in a SNPN network or GIN network.

* * * * End of Changes * * * *