## Slide 1: SoH Questions for FS_UIA_ARC
Mike Starsinic (Rapporteur)
InterDigital

## Slide 2: Proposed Way Forward
  For each key issue, revise one baseline conclusion paper based on the following SoH questions.

## Slide 3: KI#1 - Activating a User Identity (1/2)
  Background
    In round 1 of the NWM, Q-1.11 asked: “How does a linked user become active with a subscription?”.
      15 companies responded.
      12 companies indicated that the user identifier is provided in NAS signaling.
        3 of these companies expressed a clear preference for the user identifier being provided during PDU Session Establishment.
        4 of these companies expressed a preference for the user identifier being provided during registration.
      2 companies indicated that an application layer procedure may be used.
    In round 2 of the NWM, Q-1.29 asked: “Is the user identifier provided in an NAS-MM (e.g. registration) or a NAS-SM (e.g. PDU Session Establishment)? Which NAS message(s)”.
      17 Companies responded.
      7 companies answered, “NAS-MM”.
      4 companies answered, “NAS-SM”.
      4 companies prefer no NAS impact, 3 of the 4 prefer NAS-SM if there is impact.
      1 company indicated that both NAS-MM and NAS-SM may need to be supported.
      1 company prefers more discussion but comments that NAS-SM seems not appropriate.
  SoH Questions
    Q1a1: Should NAS signaling support to initiate the activation procedure by sending the user identity to the network (i.e. without credentials) (S2-2306251, 6012, 6371, 6480, 6616)?
      Yes: 10
      No: 3 (2 objections)
    Q1a2: Should NAS signaling support to initiate and perform the authentication to activate the user identity in the network (S2-2305929, 6040, 6480, 6616, 6816)?
      Yes: 12
      No: 4 (2 objections)
    Q1b: Should an application layer signaling support to initiate and perform the authentication to activate the user identity (S2-2306391)?
      Yes: 5
      No: 11 (10 objections)

## Slide 4: KI#1 - Activating a User Identity (2/2)
  SoH Questions
    Q2a: If NAS Signaling is used, is NAS-MM (e.g. registration, S2-2406039) preferred?
      Yes: 10
      No: 4 (2 objection)
    Q2b: If NAS Signaling is used, is NAS-SM (e.g. PDU Session Establishment, S2-2406480) preferred?
      Yes: 6
      No: 6 (4 objection)
    Q2c: If NAS Signaling is used, is both NAS-MM (e.g. registration) and NAS-SM (e.g. PDU Session Establishment) preferred (e.g. S2-2406703)?
      Yes: 3
      No: 9 (9 objection)

## Slide 5: KI#1 – Where is the UIP Stored?
  Background
    In round 1 of the NWM, Q-1.3 asked: “Where is the User Identity Profile Stored”.
      18 Companies responded.
      14 companies indicated that the User Identity Profile should be stored in the UDR.
      2 Companies indicated that the User Identity Profile should be stored outside of the 5GC (i.e. UIP or an AF).
      1 company was neutral.
      Another company indicated that it should not be stored in the UDR.
  SoH Questions
    Q4: Should the User Identity Profile be stored as a data set in the UDR (i.e., the user identifier is used as a data key) (e.g. S2-2406251, 5929, 6012, 6040, 6371, 6480, 6545, 6616, 6816).
      Yes: 14
      No: 3 (2 objections)

## Slide 6: KI#1 – URSP Rules
  SoH Questions
    Q6a: Should user identities be considered by the PCF when generating URSP Rules (S2-2406048)?
      Yes: 11
      No: 3 (2 objections)
    Q6b: Should a new parameter for user identifiers be included in URSP Rules (S2-2406048)?
      Yes: 5
      No: 4 (4 objections)

## Slide 7: KI#1 - SMS
  Background
    Generally, 3 options for handling SMS have been discussed.
      The SMS Service is not impacted when the user becomes active (i.e. delivery of the SMS service continues based on the subscription).
      The SMS Service is disabled when the user becomes active (i.e. delivery of the SMS service continues based on the subscription).
      The SMS Service is provided based on a GPSI in the User Identity Profile when the user becomes active (i.e. delivery of the SMS service continues based on the subscription).
    Round 1 and Round 2 of the NWM point to option 1 above. That is, when a user is active with a subscription, the SMS service is not impacted. (Questions 1.9, 1.19 1.30, 1.31)
  SoH Questions
    Proposal from the drafting session: Assume no normative impact and send an LS to SA1. The response may trigger work in this release or a future release.
    Q7a: When a user id is active, should there be 5GC impact in order to provide the SMS service?
      Yes (e.g. S2-2406264 , S2-2406371):
      No (e.g. S2-2406251, S2-2406816):
    Q7b: If the answer to Q7 is yes, should it be possible for the SMS Service disabled based on the active user?
      Yes (S2-2406371):
      No:
    Q7c: If the answer to Q7 is yes, should delivery of the SMS Service continue based on information from the UIP of the active user?
      Yes (S2-2406264 ):
      No:
    Q8: Should SA2 send an LS to SA1 to let them know that the 3 options above have been discussed and ask them for their opinion?
      Yes:
      No:

## Slide 8: KI#1 - IMS
  Background
    Generally, 3 options for handling IMS have been discussed.
      The IMS Service is not impacted when the user becomes active (i.e. delivery of the IMS service continues based on the subscription).
      The IMS Service is disabled when the user becomes active (i.e. delivery of the IMS service continues based on the subscription).
      The IMS Service is provided based on a information in the User Identity Profile when the user becomes active (i.e. delivery of the IMS service continues based on the subscription).
    Round 1 and Round 2 of the NWM point to option 1 above. That is, when a user is active with a subscription, the IMS service is not impacted. (Questions 1.10, 1.18, 1.32, 1.33)
  SoH Questions
    Proposal from the drafting session: Send an LS to SA1. The response may trigger work in this release or a future release.
    Q9: When a user id is active, should there be 5GS impact in order to provide the IMS service?
      Yes (e.g. S2-2406264):
      No (e.g. S2-2406251, S2-2406816):
    Q9a: If the answer to Q9 is yes, should it be possible for the IMS Service disabled based on the active user?
      Yes:
      No:
    Q9b: If the answer to Q9 is yes, should delivery of the IMS Service continue based on information from the UIP of the active user?
      Yes (S2-2406264 ):
      No:
    Q10: Should SA2 send an LS to SA1 to let them know that the 3 options above have been discussed and ask them for their opinion?
      Yes:
      No:

## Slide 9: KI#4 (1/3)
  Background
    In round 2 of the NWM, Q-4.9 asked: “Is it necessary to specify a procedure where the user identifier is bound to a non-3GPP device? If yes, who does the binding (e.g. the 5GC or 5G-RG/UE)? If yes, who is aware of the binding (e.g. the 5GC, 5G-RG/UE, or both)”.
      17 Companies responded.
      12 companies indicated binding is needed. At least 7 companies indicated that both the 5G-RG/UE and 5GC should be aware of the binding. 4 companies indicated that only the 5G-RG/UE needs to know the binding.
      2 companies indicated binding is not needed.
      3 companies indicated binding requires further discussion.
  SoH Questions
    Q15: Is it necessary to specify a procedure to associate the traffic from an individual non-3GPP with a device identifier (S2-2406813)?
      Yes:
      No:
    Q16: If yes, is the 5GC aware of the association of the traffic from the individual non-3GPP with a device identifier (S2-2406813)?
      Yes:
      No:

## Slide 10: KI#4 (2/3)
  Background
    In round 2 of the NWM, Q-4.8 asked: “Does the 5GC identify the traffic from the individual non-3GPP devices by a user identifier or an IP Address/MAC Address when obtaining service requirements (e.g. QoS)?”.
      19 Companies responded.
      12 companies indicated user identifier.
      2 companies commented that the question needs clarification.
      3 companies indicated IP Address
      1 company indicated both.
      1 company disagreed with the assumptions behind the question.
  SoH Questions
    Q17: Should the 5GC be able to use the device identifier of an individual non-3GPP device to obtain service requirements (e.g. QoS) for the traffic of the non-3GPP device (S2-2406813)?
      Yes:
      No:

## Slide 11: KI#4 (3/3)
  Background
    In round 1 of the NWM, Q-4.2 asked: “Is it necessary to specify a procedure to facilitate authentication via the 5GC of the user identifier associated with each individual non-3GPP device(s) connecting behind the UE or 5G-RG (i.e. to enable service differentiation and charging)?”.
      18 companies responded.
      8 companies responded yes.
      6 companies responded no.
      2 companies responded that it can be left to SA3.
  SoH Questions
    Q18: Is whether and how to authenticate/authorize a non-3GPP device is a SA WG3 decision (S2-2406813)?
      Yes:
      No:

## Slide 12: KI#3 - Exposure
  Background
    Question Q-3.4 of the NWM asked “Should it be possible to expose authentication results, via an NEF API?”
      15 Companies responded., 9 companies responded yes, 6 companies responded no.
    Question Q-3.5 of the NWM asked “Should it be possible to expose, to an authorized AF, whether a user is active, via an NEF API?”
      14 Companies responded., 7 companies responded no., 6 companies responded yes., 1 companies requires further discussion.
    Question Q-3.6 of the NWM asked “Should it be possible to expose, to an authorized AF, the identities of the subscriptions that are linked to a user identity, via an NEF API?”
      15 Companies responded., 9 companies responded no., 5 companies responded yes., 1 company is open to discussing.
    Question Q-3.7 of the NWM asked “Should it be possible to expose, to an authorized AF, the identities of the subscriptions that are linked to a user identity, via an NEF API?”
      13 Companies responded., 5 companies responded no., 5 companies responded that some information can be read., 3 companies questioned the use case.
  SoH Questions
    Q11: Should it be possible to expose authentication results, via an NEF API?
      Yes (e.g. S2-2406618, 6683):
      No (e.g. S2-2406587):
    Q12: Should it be possible to expose, to an authorized AF, whether a user is active, via an NEF API?
      Yes (e.g. S2-2406618):
      No (e.g. S2-2406587):
    Q13: Should it be possible to expose, to an authorized AF, the identities of the subscriptions that are linked to a user identity, via an NEF API?
      Yes (e.g. S2-2406618, 5931, 6814):
      No (e.g. S2-2406587):
    Q14: Should it be possible to expose, to an authorized AF, the user identities that are linked to a user subscription, via an NEF API?
      Yes (e.g. S2-2406618):
      No (e.g. S2-2406587):

## Slide 13: KI#1 - One or More User Identities in a UIP
  Background
    In round 1 of the NWM, Q-1.4 asked: “There is an editor’s note in the conclusion that says that whether more than one User Identity can be in the User Identity Profile is FFS. Should it be possible for more than one User Identity to be in a User Identity Profile? If yes, then what is the use case?”.
      16 companies responded.
      8 companies expressed a preference that there should only one user identity in the User Identity Profile.
      6 companies expressed a preference that it should be possible for more than one user identity to be in the User Identity Profile.
      2 companies were neutral or indicated that the question is out of scope.
  SoH Questions
    Q5: Should it be possible to include more than one User Identities in the User Identity Profile (S2-2406014)?
      Yes:
      No: