3GPP TSG-SA3 Meeting #116	S3-242418-r1 merges S3-241713 and S3-242034

Jeju, South Korea,  20th - 24th May 2024

# Source:	Lenovo, Motorola Mobility, Johns Hopkins University APL

# Title:	Resolve EN in Use case 1

# Document for:	Approval

Agenda Item:	5.1

# 1	Decision/action requested

This contribution provides clarifications and resolves the EN in TR 33.794 Clause 5.1.1 on Malformed Message.

# 2	References

[1]	3GPP TR 33.794, 'Study on enablers for Zero Trust Security', (Release 19).

# 3	Rationale

TR 33.794 [1], Clause 5.1.1.3, has the following EN.

Editor’s Note: Additional evaluation if any is FFS.

As it is clearly provided in the guidance EN of clause 5.1, ‘this clause covers the security analysis to identify potential threat(s) and attack(s) on 5G SBA layer intended to identify which data may be relevant for threats and attack detection.’. Inline to this goal, usecase 1 clarified the potential malformed message scenario specific threats/attacks on 5G SBA layer and related event data to be considered for threat/attack detection. Also the collection of this event data can also be determined based on the operator’s policy and so it is not mandatory by default. Additionally, further details (if any) are left to the solution discussions as clarified in NOTE 1 and 2, therefore the EN is resolved.

This contribution additionally fixes, minor editorials in usecase 1 description.

# 4	Detailed proposal

SA3 is kindly requested to agree the pCR below to TR 33.794.

*****Start of Change 1 *****

# 4	Security Assumptions

This section describes the potential security assumptions to be considered for the study specific to the objectives [2]. The security aspects identified with respect to the zero trust security tenets in the context of the 5GC SBA in TR 33.894 [3] are still relevant and applicable for this study.

Assumption #1: Based on Objective 1 (i.e., Data exposure for security evaluation and monitoring) the operator has deployed a Security Function.

- 	The Security function that performs the security evaluation and monitoring resides in the operator’s domain (i.e., external to the 3GPP network) and it is considered as a trusted entity. This Security function and its application logic are upto the operator’s implementation, and it is outside the scope of 3GPP in the present document.

For security related data or logs, care must be taken when logging or triggering notification for such events. Some guidelines and measures on data collection, and secure handling is described e.g., [x].

Assumption #2: For Objective 2 (i.e., Security mechanism for dynamic policy enforcement), the dynamic security policy enforcement is configured and controlled by the operator based on operator’s policy.

Exposing the security data in a structured manner can help automated continuous security monitoring. In order to do this, classification of security data and defining a structure can help.

In relation to data exposure for security evaluation and monitoring, it is important to understand the relevant security risks associated with SBA. Accordingly, symptoms required to assess the possibility of exploiting any such risks can be considered for data exposure. For this study, it is assumed that following attacks may be applicable to SBA layer, which can be implemented using microservices or virtual network functions:

1. Network level attacks

2. Service-level attacks

3. API security risks

4. Infrastructure related attacks: These attacks can be considered out of scope for 3GPP. However, operators may want to define specific security data to be exposed for such attacks. The present document does not consider defining data exposure for these attacks.

*****End of Change 1 *****

*****Start of Change 2 *****

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TR 33.894, 2023 September, V18.0.0: "Study on applicability of the zero trust security principles in mobile networks", Release 18.

[3]	3GPP SP-231784, "New Study on enablers for Zero Trust Security".

[4]	3GPP TS 33.501: "Security architecture and procedures for 5G System".

[5]	RFC 6749, "The OAuth 2.0 Authorization Framework".

[6]	3GPP TS 33.310: "Network Domain Security (NDS); Authentication Framework (AF)".

[7]	3GPP TR 33.894, 2023 September, V18.0.0: "Study on applicability of the zero trust security principles in mobile networks", Release 18.

[8]	NIST Special Publication 800-207: "Zero Trust Architecture".

[9]	3GPP TR 33.738: "Study on security aspects of enablers for network automation for the 5G system phase 3".

[10]	3GPP TS 29.500: "5G System; Technical Realization of Service Based Architecture; Stage 3".

[11]	3GPP TS 23.502: "Procedures for the 5G System (5GS); Stage 2".

[12]	3GPP TS 29.501: "5G System; Principles and Guidelines for Services Definition; Stage 3".

[13]	3GPP TS 23.288: "Architecture enhancements for 5G System (5GS) to support network data analytics services".

[14]	IETF RFC 9113: "HTTP/2".

[15]	3GPP TS 33.117: "Catalogue of general security assurance requirements"

[16]	3GPP TR 33.926: "Security Assurance Specification (SCAS) threats and critical assets in 3GPP network product classes

[17]	https://owasp.org/www-community/Threat_Modeling_Process

[18]	3GPP TS 23.501: " System architecture for the 5G System (5GS)".

[x]	NIST SP-800-92 "Guide to Computer Security Log Management".

*****End of Change 2 *****

*****Start of Change 3*****

### 5.1.1	Use case #1: Information on Malformed Message

#### 5.1.1.1	Description

Malformed messages (i.e., SBI message violations) may be received by a NF over an SBI from another NF (e.g., due to malicious intentions or due to mere error). The malformed message(s) sent with malicious intentions have the potential to cause failure/malfunction of NF(s). In various other cases there are requirements to handle such malformed message(s) (such as in TS 33.501 [4], Clause 5.9.3.2, states, ‘The SEPP shall discard malformed N32 signaling messages’, and Clause 5.9.3.4, states, ‘The IPUPS shall discard malformed GTP-U messages’). In the case of SBA, simply dropping a malformed message cannot help to identify the threat surface and its context i.e., which NF sends the malformed message and why does it send such a malformed message, which services it is targeting, etc. Identifying the potential threat rather than dropping the malformed message(s) can prevent further attacks on the rest of the network (e.g., another NF). 3GPP specified service-based interface message inputs and outputs described in TS 23.502 clause 5.2 [11] and TS 29.500 [10] can be considered as normal messages. If a Service based interface message violates the specified input or output (i.e., SBI message violation), that message can be considered as malformed message and the related event data can be collected, logged, and exposed (based on operator policy) to the Operator’s security function residing external to the 3GPP network to enable security evaluation and monitoring. Additionally, clause 6.2 of TS 29.501 [12] provides guidelines on which service-based messages can be considered malformed.

#### 5.1.1.2	Relevant data

The data relevant to be exposed includes event data on the received malformed message (using a related event name or identifier), and the NF identification information (i.e., NF ID) of the sender of the malformed message.

NOTE: Management aspects of relevant security data about malformed messages need to be coordinated with SA5.

#### 5.1.1.3	Evaluation of the identified data

Based on Operator’s policy, malformed message related event data (e.g., the NF identification information and the malformed message event information) can be logged for security evaluation and monitoring purposes. If such logs are available, it is notified to the Operator’s Security Function to enable necessary security evaluation and monitoring to aid in timely threat detection.

NOTE 1: For this malformed message scenario, the relevant data and if the malformed message itself or any other additional information related to this event need to be sent to the Operator’s Security Function will be discussed as part of solutions and the decisions will be made in the conclusion clause 7 below (later in the study).

NOTE 2: Further if the event related data should only be logged or also need to be notified to Operator’s security functions will be discussed as part of the solution details.

*****End of Change 3*****

# Comments

Added new change 2 and 3 clause to cover the reference added. And is related citations