## Slide 1: Moderator Summary on introduction of IoT-NTN TDD mode
RAN1 Vice-Chair (Huawei)
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
RP-242411

## Slide 2: Proposed approach for the WID on introduction of IoT-NTN TDD mode
Define a new NB-IoT TDD mode for NTN based on minimum necessary changes to the NB-IoT NTN FDD frame structure and procedures for the NB-IoT operation in targeted unpaired MSS allocated band (TN deployment is not expected in this band).
The new NB-IoT NTN TDD mode is based on the configuration of a periodic pattern consisting of non-overlapping set of usable contiguous UL subframes and set of usable contiguous DL subframes, which is periodic every N radio frames, with N=9 as baseline. No blind detection is assumed at the UE side. The value of N and the configuration of the periodic pattern are fixed per band.
The feature is not intended to be applicable to existing 3GPP bands.
The WI includes a one-quarter study phase in RAN1 (checkpoint in RAN#106) and RAN4 (start from Nov’24) to investigate the impact due to the periodic pattern at least on UE DL synchronization, and TBD other aspects.
Create a new band for the new TDD mode as example band in the WID, which is the 1616-1626.5 MHz MSS allocated band
  Reuse the existing RAN4 requirements as much as possible (no intention to have any relaxation of the requirements)
  Start of the work in RAN4 in 2025/Q1 with 0.5 TU in RF
  No NTN-NTN coexistence study needed. Leverage existing work as much as possible for TN-NTN coexistence of adjacent channels/bands.
Expected TU: 0.5 TU in RAN1 from Q4, 0.5 TU in RAN2 from 2025/Q1, starting from 0.25 TU for RRM in 2025/Q1, performance part to start after 2025/Q3 with 0.25 TU.
A corresponding draft WID is provided in RP-24XXXX.