## Slide 1: On Rel-19 Multi-carrier enhancements
3GPP TSG RAN Meeting #105
Melbourne, Australia, Sep. 9-12, 2024
RP-242336
Agenda Item: 9.1.1
Source: Lenovo, CMCC, China Telecom, China Unicom, NTT DOCOMO, Verizon, Huawei, HiSilicon, Nokia, Nokia Shanghai Bell, ZTE, Sanechips, CATT, Apple, OPPO, vivo, Spreadtrum, xiaomi, Motorola Mobility, NEC, HONOR, Cybercore, TCL, Transsion, New H3C, ASR, Baicells, Tencent, Telstra, Qualcomm
Document for: Discussion and decision
(Revision of RP-242122)

## Slide 2: Background: Rel-18 Standardization outcome
Main standardization outcome
DCI format design:
  At most one PDSCH or PUSCH per scheduled cell
  New DCI formats, DCI 0_3 & DCI 1_3, introduced
  Up to 4 cells can be co-scheduled by one DCI 0_3/1_3
  DCI 0_3/1_3 can be used for single cell scheduling
  DCI 0_3/1_3 and DCI 0_0/1_0/0_1/1_1/0_2/1_2 can be monitored simultaneously from a same scheduling cell.
Basic framework
Supported cases:
  Only same SCS among co-scheduled cells is supported
  Only same carrier types (licensed/unlicensed, FR1/FR2/FR2-2) among co-scheduled cells is supported
  Only a single scheduling cell for each scheduled cell
  Only single PDSCH or PUSCH scheduled per scheduled cell
  Only TB-based transmission supported per scheduled cell
Up to 4 cells scheduled by one DCI format 1_3
Up to 4 cells scheduled by one DCI format 0_3

## Slide 3: Motivation for Rel-19 Multi-carrier enhancements
Multi-carrier operation is very important for 5G commercial networks by aggregating various spectrum resources for providing high data rate and low latency communication.
Due to quite limited TU for Rel-18 Multi-carrier enhancements, some important use cases have been excluded from Rel-18, e.g., different SCS among co-scheduled cells, different carrier types among co-scheduled cells. Co-scheduling carriers with different SCS is of high commercial needs for operators, e.g., 3.5GHz TDD + Sub-3GHz FDD, FR1 + FR2.
Furthermore, two new DCI formats are introduced in Rel-18, DCI format 0_3 and 1_3. Each DCI format 0_3 or 1_3 can schedule up to 4 cells with limitation of a single PUSCH or PDSCH per scheduled cell. In Rel-17, for FR2 with high SCS, multi-PDSCH/PUSCH scheduling is introduced, i.e., up to 8 PUSCHs or PDSCHs on a single serving cell can be scheduled by a single DCI format 0_1 or 1_1, in order to save UE power consumption and reduce PDCCH overhead.
Hence, it is straightforward to combine multi-cell scheduling and multi-PDSCH/PUSCH scheduling in Rel-19 to fully exploit the gain of power saving and PDCCH overhead reduction so that one DCI format 0_3 or 1_3 can schedule multiple cells with one or multiple PUSCHs/PDSCHs per scheduled cell. This is especially useful when scheduling cell in FR1 with a lower SCS schedules multiple cells in FR2 with higher SCS.

## Slide 4: Objective for Rel-19 Multi-carrier enhancements
Specify a solution for multi-cell PUSCH/PDSCH scheduling with a single DCI [RAN1]
  Different SCS/carrier type among co-scheduled cells by DCI format 0_3/1_3 is supported
  One or multiple PUSCHs/PDSCHs per scheduled cell is supported by a single DCI
      The maximum number of PUSCHs/PDSCHs per scheduled cell is [4 or 8]
      Note: Type-1 HARQ-ACK codebook is not enhanced for Rel-19 multi-cell scheduling.
      Note: The maximum number of sub-codebooks for Type-2 HARQ-ACK codebook is not increased for Rel-19 multi-cell scheduling.
      Note: UE does not expect to be configured with both single-cell multi-PUSCH/PDSCH scheduling and multi-cell multi-PUSCH/PDSCH scheduling on the same or different cells within a same PUCCH group.
  Note: No new DCI format is introduced.