## Slide 1: WF for NTN NB-IoT inband operation
Ericsson, [...]

## Slide 2: Background
NTN NB-IoT standalone operation is introduced from Rel-17
NTN NB-IoT inband operation has not been introduced in specification till now.

## Slide 3: Open issue
Inband or guard band operation at network for NR NTN
  Option 1: inband
  Option 2: inband and guardband
In-band/guard band operation should be mandatory or optional feature
  Option 1: mandatory
  Option 2: optional
From which release the in-band/guard band operation mode should be mandatory supported by NTN NB-IoT UE
  Option 1: Rel-18
  Option 2: Rel-19
From which release the in-band/guard band operation mode should be optional supported by NTN NB-IoT UE
  Option 1: Rel-18
  Option 2: other release

## Slide 4: Open issue
Signaling aspect and other potential cross group impact
  Issue 1: When configured with non-anchor carrier, NTN NB IoT UE needs to apply 0.5 offset for M_DL for standalone mode, while no offset for M_DL in inband mode, hence NTN NB-IoT needs to know which deployment mode the configured anchor carrier is:
    Further check if the NTN NB-IoT UE can use the MIB IE below to identify the In-band/guard band and standalone mode.
  MasterInformationBlock-NB field descriptions
  operationModeInfo
    Deployment scenario (in-band/guard-band/standalone) and related information. See TS 36.211 [21] and TS 36.213 [23].
    Inband-SamePCI indicates an in-band deployment and that the NB-IoT and LTE cell share the same physical cell id and have the same number of NRS and CRS ports.
    Inband-DifferentPCI indicates an in-band deployment and that the NB-IoT and LTE cell have different physical cell id.
    guardband indicates a guard-band deployment.
    standalone indicates a standalone deployment.

## Slide 5: Open issue
Signaling aspect
  Issue 2: whether to define the UE capability for in-band operation
    Option 1: Yes
    Option 2: No

## Slide 6: Open issue
Which CR category should be used for TEI CR?
Option 1: Category C
Category | Meaning | Remarks
A | Corresponds to a change to an earlier Release | Used to reflect functionally equivalent changes made to an earlier Release of the same Specification. NOTE: The proposed change to the later Release of the Specification need not be absolutely identical to the proposed change to the earlier Release, since it is possible that, due to earlier change requests, the affected text is not identical in each Release. Category A should be used when the functional objective of the proposed changes is equivalent in the earlier and later Releases.
B | Addition or deletion of feature | The new feature is to be added to the Release; the reference is not to the Specification itself. This will normally correspond to an identified Work Item. This category shall not be used for a frozen Release, except for alignment CRs as described in clause 4.7.
C | Functional modification of feature | Any functional modification shall correspond to an identified Work Item. However backward compatibility shall be ensured when the issue has an impact on the UE. This category shall not be used for a frozen Release, except for alignment CRs as described in clause 4.7.
D | Editorial modification | Editorial modifications shall have no impact on an implementation. An editorial modification CR to a frozen Release shall not be permitted.
E | (not used) | 
F | Correction | Used: 1 to correct an error in the specification (i.e. a clear instruction in the specification which leads to incorrect operation of the system); or 2 to correct an ambiguity in the specification which could lead to different implementations which cannot inter-operate; or 3 (void); or 4 to remedy the incorrect implementation of a previously approved CR; or 5 to correct a misalignment between the specifications (stage 1, stage 2 & stage 3) for a feature or service when not introducing a new function or functional change.
Table 4A: Categories of Change Requests

## Slide 7: Open issue
Which wording for the draftCR adding the F_DL for in-band/guard band operation:
  Option 1: Adding the same F_DL forumular with in TS 36.101
    i.e option 1 in draftCR R4-2416114
  Option 2: keep the same formular in TS 36.102 and modifying the M_DL offset in a note for inband operation.
  Option 3: other option not excluded

## Slide 8: Open issue
SAN TS 38.108 impact
  Evaluating NTN NB-IoT in-band operation RF specificaiton in next meeting
SAN TS 36.108 impact
  EARFCN to adopt the same with 36.102
SAN TS 38.181 impact
  Declaration of the NTN NB-IoT operation
  Related test for core requirement in TS 38.108
How to split the work between companies?
  [3+ of meetings to finalize the network specification]

## Slide 9: Reference
R4-2415461, On inband deployment of NTN NB-IoT in NR carrier, Ericsson
R4-2416114, (TEI18) Draft CR to 36.102 In-band NB-IoT NTN deployment with NR, MTK