## Slide 1: SoH Questions for NG_RTC_Ph2 way forward
China Mobile (Rapporteur)

## Slide 2: KI#1: Extensible IMS mechanism supporting IMS events in the context of DC communication
This key issue enhances IMS architectural and procedures to support an extensible mechanism that enables trusted and untrusted applications to subscribe to and receive reports about IMS events related to IMS services in the context of Data Channel communication.
The controversial issue is how to enahnce IMS AS service to support subscription and notification of events to AF
  Option A: define a new IMS AS service specific for event exposure to AF (S2-2409982)
  Option B: update existing IMS AS service Nimsas_SessionEventControl to also support event exposure to AF (S2-2410446)

## Slide 3: SoH for KI#1: Extensible IMS mechanism supporting IMS events in the context of DC communication
Q1: how to enahnce IMS AS service to support subscription and notification of events to AF
  Option A: Define new service
    Yes:
    No:
  Option B: Update existing service
    Yes:
    No:

## Slide 4: KI#8: Support of IMS Avatar Communication
This key issue aims to study enhancements of IMS architecture, interfaces, and procedures to support IMS based Avatar communication
The controversial issues are related to the architecture of MF retrieving Avatar representation from BAR
  Issue 1: where the Avatar ID list is stored
    Option 1.1: the Avatar ID list is stored in HSS (S2-2410354)
    Option 1.2: the Avatar ID list is stored in BAR (S2-2410217)
    Option 1.3: the Avatar ID list is local available in the UE before initiating the IMS Session (S2-2410524)
  Issue 2: How the UE got authorized when UE request to use certain avatar representation.
    Option 2.1: UE send request to DC AS through ADC, and DC AS will authorize the download. (S2-2410354)
    Option 2.2: UE send request to the DCSF through SDP, and DCSF will authorize the download, (S2-2410217)
  Issue 3: whether direct interface between UE and BAR is supported for user management of avatar representation
    Option 3.1: supported (S2-2410524)
    Option 3.2: not supported

## Slide 5: SoH for KI#8: Support of IMS Avatar Communication
Q1: where the Avatar ID list is stored
  Option 1.1: the Avatar ID list is stored in HSS
    Yes:
    No:
  Option 1.2: the Avatar ID list is stored in BAR
    Yes:
    No:
  Option 1.3: the Avatar ID list is local available in the UE before initiating the IMS Session
    Yes:
    No:
Q2: How the UE got authorized when UE request to use certain avatar representation
  Option 2.1: MF retrieves avatar representation directly from BAR over “control plane”, or from BAR via DCAS over “control plane” (S2-2410354)
    Yes:
    No:
  Option 2.2: MF retrieves avatar representation directly from BAR over “media plane” (S2-2410217)
    Yes:
    No:
Q3: whether direct interface between UE and BAR is supported for user management of avatar representation
  Option 3.1: supported
    Yes:
    No:
  Option 2.2: not supported
    Yes:
    No:

## Slide 6: KI#4: Extensible IMS framework to support authorization and authentication of third-party identities in IMS sessions
This key issue is to study how to enhance the IMS architecture and procedures to support third party identities in IMS sessions
It is concluded in the TR that either S-CSCF or IMS AS supports authorization of usage of third party identities. However some issues need to be discussed and decided during normative phase
  Issue 1: whether the authorization information should be stored in transparent data or service profile
    Option 1.1: If IMS AS authorizes the subscriber, the authorization information should be stored as transparent data in HSS and not standardized
    Option 1.2: If S-CSCF authorizes the subscriber, the authorization information should be stored as service profile and be standardized over Cx/N70
    If both options are supported, whether supporting co-existence of both option in one network need to be considered
It is concluded in the TR that RCD information may be provisioned in the HSS repository data via the NEF, however it seems there is different proposals
  Issue 2: how to support provisioning of RCD information
    option 2.1: RCD information is provisioned via OAM, thus provisiong of RCD information via NEF is not supported (S2-2410189)
    Option 2.2: Provisioning of RCD information via NEF is supported (S2-2410511)

## Slide 7: SoH for KI#4: Extensible IMS framework to support authorization and authentication of third-party identities in IMS sessions
Q1: whether the authorization information should be stored in transparent data or service profile
  only Option 1.1 is supported:
    Yes:
    No:
  only Option 1.2 is supported
    Yes:
    No:
  Both option 1.1 and 1.2 are supported
    Yes:
    No:
Q2: whether supporting co-existence of both option 1.1 and 1.2 in one network
    Yes:
    No:
Q3: how to support provisioning of RCD information
  Option 2.1: via OAM
    Yes:
    No:
  Option 2.2: via NEF
    Yes:
    No:

## Slide 8: BACKUP