## Slide 1: eEDGE_5GC_Ph3 Tuesday Q0 drafting session
Dario S. Tonesi

## Slide 2: Tentative agenda
KI#1: I-SMF based EAS discovery
  Discovery and insertion of I-SMF: AMF-based vs. SMF-based
  Local offload policy (generation of N4 rules by I-SMF)
KI#2: PSA UPF discovery based on N6 delay
  Reporting of N6 delay: SBI vs. non-SBI

## Slide 3: KI#1: I-SMF based EAS discovery: Discovery and insertion of I-SMF
Options:
S2-2409762, Huawei et al.
  AMF selects and inserts I-SMF during PDU session establishment based on subscription info (local offload allowed indication, DNN/S-NSSAI).
S2-2410604, Nokia.
  AMF selects and inserts I-SMF during PDU session establishment based on information from SMF (target DNAI)

## Slide 4: KI#1: I-SMF based EAS discovery: Local offload policy (generation of N4 rules by I-SMF))
Options
S2-2410249, Huawei.
  I-SMF generates N4 rules based on direct input from PCF (requires I-SMF<>PCF interface)
S2-24XXXX?, Nokia.
  I-SMF generates N4 rules based on input from SMF (no I-SMF<>PCF interface required)

## Slide 5: KI#2: PSA UPF discovery based on N6 delay Reporting of N6 delay: SBI vs. non-SBI
Options for reporting N6 delay measurements by UPF to SMF
S2-2409770, Huawei.
  Via N4 interface (non-SBI)
S2-2410598, Nokia.
  Via Service Based Interface (SBI). NOTE: configuration via N4

## Slide 6: Thank you

## Slide 7: SoH question template
Do you support Option 1?
  Yes
  No
Do you support Option 2?
  Yes
  No