## Slide 1: Qualcomm’s view on SA2 release 19
Source: Qualcomm Incorporated

## Slide 2: Outline
Release 19 timelines
Principles for 5G Advanced evolution
Overall view on Release 19 content (top 10 priorities)
Other priorities
Topics proposed not to evolve in release 19

## Slide 3: Release 19 timeline (SA2 view)
Expected timeline agreed in SA#99 views the completion of stage-2 in Dec. 2024
This timeline will be very constrained for study/work items that will be approved in Dec.
We should be open to certain WIs getting completed in Mar. 2024 without impacting the overall release cycle (with nominal 6mo CT work)
R18 SA2
R18 Maint
R19
Workshop
(June 13-14)
R19 in SA2 starts
2022
Q1
Q2
Q3
Q4
2023
Q1
Q2
Q3
Q4
2024
Q1
Q2
Q3
Q4
R19
1st pkg
(SA#101)
Sep. 23
R19
2nd pkg
(SA#102)
Dec. 23
R19
Stage-2 freeze

## Slide 4: Principles for 5G evolution
Balance the needs of the increasing number of actors participating in 3GPP and/or committed to the 3GPP ecosystem
Avoid auto-pilot continuation projects
  For some items we should consider “taking a break” to ensure that the market can “absorb” the R16+17+18 content
Resist standards getting too far ahead of product roadmaps

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | Dual Steer (See slides 19-23 and SWS-230049 for more details) | The objective of this study item is to study how to enhance the 5G system architecture to address how an MA PDU Session can simultaneously support two 3GPP access paths. The two 3GPP access paths can be in the same PLMN or in different 3GPP networks. In case of different 3GPP networks, the MA PDU Session has one 3GPP access path via a certain PLMN and the other 3GPP access path via another PLMN or SNPN, and the UE registers with the first PLMN and with the other PLMN/SNPN using the same 3GPP subscription credentials. Key Work Tasks includes defining - How to select the second PLMN or SNPN in case of different 3GPP networks after an initial PLMN was selected for the UE. How to enhance registration and session management procedures. How to support mobility between a PDU Session with single 3GPP access and a MA PDU Session with dual 3GPP access as well as between MA PDU Sessions with dual 3GPP accesses. How to route the traffic of the MA PDU Session towards the PSA UPF. How to extend policies, steering functionalities and steering modes. | Yes, Study on upper layer traffic steering, switching and split over dual 3GPP access | SA2 | Don’t know | SA3 for security, SA5 for charging

## Slide 6: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
2. | VMR phase 2 (See slide 24-27 for more details | The aim of this study work is to investigate and identify potential architecture and system level enhancements to further evolve the functionalities of base station relays mounted on vehicles. Specifically, the objectives include: - WT#1: Identify gaps for supporting the architecture with a full gNB/CU onboard of a relay and the use of a PDU session for the wireless backhauling of the N2/N3 interfaces. - WT#2: Enable mobility for a full gNB/CU onboard of a relay using a PDU session for the wireless backhauling of the N2/N3 interfaces. - WT#3: Specify architecture enhancements for the selected option(s) to enable authorization of relay - WT#4: Specify architecture enhancements for the selected option(s) to enable QoS support over the backhaul -WT#5: Specify architecture enhancements for the selected option(s) to enable Cell ID/TAC management - WT#6: Specify architecture enhancements for the selected option(s) to enable support for UE location services and emergency services - WT#7: Specify architecture enhancements for the selected option(s) to enable NTN backhaul for VMR - WT#8: Specify architecture enhancements for the access to onboard services/edge computing - WT#9: Specify architecture enhancements for the selected option(s) to extend UAV functionality to VMR | No | SA2 | Yes, major | SA3 for Security aspects, SA5 for charging aspects, RAN3 for RAN aspects

## Slide 7: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3. | Generalized framework of data collection from UE (See slide 28-31 and SWS-230056 for more details) | AI/ML for NR Air Interface is being discussed in RAN1 and RAN2 in Rel-18 RAN2 is leading the discussion about data collection from UE for ML model training and ML model transfer / delivery to UE. Several solutions which include EVEX-enhanced solution were proposed in RAN2. The work should require SA expertise as it goes beyond RAN’s scope for the following reasons: RAN can not track a UE between RRC connections. ML model training maybe performed by the UE vendor, while the data is available at the operator. We need a standard way to transfer the data out of the operator’s network that is visible and controlled by the operators. The SA teams should be involved in designing the architecture for data collection and data storage for RAN AI/ML purposes. “UE data collection from UEs” are being discussing in different WGs, including SA2, SA4, SA6 and RAN1/2. It is desired to have a common framework that meets all the requirements among different WGs. SA2 is the natural WG that defines common system frameworks. It is proposed to approve the following proposal as objectives in the SID regarding 5G AI/ML in Rel-19 in SA2: A general framework of data collection from UEs | No | SA2 | Yes, minor | SA3 for Security aspects, SA5 for charging aspects, RAN2 and RAN3 for RAN aspects

## Slide 8: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
4. | Architecture Enhancements for Advanced Air Mobility in Cellular Environment (See slide 32-38 for more details) | The aim of this study work is to investigate and identify potential architecture and system level enhancements to further evolve the functionalities for the AAM aerial vehicles ecosystem. Specifically, the objectives include: - WT#1: Enhance NEF services to support data services (e.g. service exposure) between MNOs and UTM functions to support intelligent pre-mission flight planning, in-mission flight monitoring, interfacing with UTM infrastructure (e.g. supporting multiple USS serving different geographical areas), and QoE estimation and planning - WT#2: Enable network-assisted/ground-based DAA solutions that leverage information collected and generated in the 5GS (e.g. input from sensing and other potential "sensors" in RAN and UEs), and leverage service exposure and edge computing to provide aerial UEs and UTM with tactical deconfliction solutions. The solution shall co-exist with and leverage, to the extent possible, Direct DAA solutions considered in Release 18. - WT#3: study enhancements to multi-PLMN connectivity for connectivity redundancy to improve connection reliability based on SA1 requirements. The work will build upon ATSSS features in previous releases and leverage Release 19 work on ATSSS. - WT#4: Study support of the C2CSP model, considering existing 3GPP solutions and potentially extensions (e.g. IMS DC and IMS framework). - WT#5: study architectural enhancements for support of UTM configuration in UAV and mobile networks of different aerial flight zones where UAV application settings and communication QoS may be different, and to provide network and UAV with means to identify those flight zones. | Yes, Further Architecture Enhancement for UAV and UAM | SA2 | Yes, minor | SA3 for Security aspects, SA5 for charging aspects, RAN2 and RAN3 for RAN aspects

## Slide 9: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5. | Further enhancements for XR services (See slide 39-43 for more details) | It is important to extend the framework to address: • Awareness of Application Layer Forward Error Correction (AL-FEC) at RAN can assist detection of PDU-set errors and allow scheduler optimization in delivery of PDU-sets • For certain types of XR flows, PSDB/PDB does not fully represent the actual latency requirements because applications care about the absolute delivery time of display. • Better adaptability of 5GS QoS level for XR traffic. Specifically, the objectives include: - Extend PDU Set based QoS handling to address scenarios with Application-level Forward Error Correction (AL-FEC) • Split XR solutions implement AL-FEC to achieve high reliability at low latencies without retransmissions • Further refinement of QoS framework to address latency requirements • PDU-set latency requirement is a deadline in time for display as opposed to a latency bound between packet arrival and packet departure: promote Nominal PSDB to address this type of applications. • Extend mechanism to adapt 5GS QoS level for XR traffic • Alternative QoS Profile applied to PDU Set based QoS handling | No | SA2 | Yes, major | RAN2 and RAN3 for RAN aspects

## Slide 10: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
6. | Lightweight Access Aggregation and Steering of Wi-Fi in 5GC (See slide 43-46 for more details) | The Rel-16 to Rel-18 Access Traffic Steering, Switch and Splitting feature enables simultaneous communication between UE and UPF over multiple paths. By leveraging the simultaneous communication over multiple paths, the 5G system can provide services with improved user experience, can distribute the traffic across multiple accesses in a policy-based fashion, can provide new high-data-rate services, etc. However currently the Access Traffic Steering, Switch and Splitting feature requires that MA PDU Sessions require integrated trusted or untrusted non-3GPP accesses. This means that to enable ATSSS either a TNGF (Trusted Non-3GPP Gateway Function) or an N3IWF (Non-3GPP InterWorking Function) is deployed in the PLMN. At the same time, many network deployments do not have such nodes and it is therefore beneficial to study how to support a limited set of access traffic aggregation and steering features applicable to non-integrated Wi-Fi networks (which do not require the deployment of TNGFs/N3IWFs). The objectives are to study how to enhance the 5G system architecture to address the following aspects: 1) Define a new architecture for Lightweight Access Aggregation and Steering of non-integrated Wi-Fi in 5GC not based on TNGF/N3IWF. 2) Introduce the concept of Non-Integrated Aggregated (NIA) PDU Session based on the re-use of IETF RFC protocols (e.g., MPQUIC/MPTCP) and related functions in the UE and in the PSA UPF. A) How to establish and modify NIA PDU Sessions B) How to extend the usage of rules for UE and UPF to coordinate the aggregation and steering of traffic within a NIA PDU Session, including how to configure the MPTCP/MPQUIC proxy functionality in the UPF NOTE: It is assumed that the Lightweight Access Aggregation and Steering functionality applies to non-GBR traffic type only. | No | SA2 | No | SA3 for security aspects

## Slide 11: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
7. | Timing as a Service and Timing Resiliency for NB-IoT and eMTC (See slide 47-50 for more details) | Rel-17 specified support for timing as a service, which refers to providing timing information to UEs as a monetizable operator service. Rel-18 added support for subscription control for timing delivery to individual UEs and also support for providing quality information about the 5GS clock to UEs. Clock quality information enables UEs to determine if the 5G clock quality is sufficient or enables UEs to compare the 5G clock quality against other available time sources and to select the best available clock source based on this. Timing as a service enhances timing resiliency as it enables use of 5GS as yet another reliable time source. However, as of now timing as a service is only supported for NR. This limits commercial opportunities for MNOs since NR coverage (with NR connected to 5GC) can be expected to not be available in many areas for quite some time. NB-IoT and eMTC (both terrestrial and non-terrestrial) offer a significantly larger global coverage. However, NB-IoT and eMTC do not support timing as a service. Specifically, NB-IoT/eMTC do not support providing reference time selectively to UEs based on subscription information and do not support providing clock quality information to UEs. The objectives of this study are as follows: • WT#1: Study how to enable selective reference time and clock quality information delivery based on subscription for NB-IoT and eMTC (terrestrial and non-terrestrial) • Subscription enhancements in HSS for control of reference time delivery and control of clock quality delivery to the UE • MME enhancements to inform eNBs about need for reference time delivery and clock quality information delivery for individual UEs • eNB support for delivery of reference time and clock quality information for individual UEs NOTE: The solution defined in Rel-18 for selective reference time and clock quality information delivery based on subscription in 5GS can be taken as a baseline. • WT#2: Study how to support propagation delay compensation for NB-IoT and eMTC | No | SA2 | Yes, minor | SA3 for security aspects. RAN2 and RAN3 for the RAN aspects

## Slide 12: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
8. | Enhancements in handling of Radio Capabilities (See slide 51-55 for more details) | The aim of this study work is to investigate and identify potential architecture and system level enhancements to further evolve the handling of radio capabilities in 5GS and EPS. Specifically, the objectives include: - WT#1: Identify how to prevent a UE to access a specific RAT/system in which it does not have subscription and therefore will be rejected. How to indicate to UE to disable certain radio capabilities in order to avoid attempting to register to this RAT/system and be rejected. How to define exceptions for emergency services. - WT#2: How an AF (internal or external to the network) know in advance before initiating a session for a particular application that there is “alignment” of radio features that would be required in order to support this application or the specific function is required. - WT#3: How to transfer the radio capability container or UE Radio Capability ID between AMF and MME (and vice versa) in order to avoid retrieval of radio capabilities from the UE (if possible) from the target system. The work will be based on following deployment options: 1) RACS support in UE and NW, 2) No RACS in UE, but support of RACS in NW, 3) No RACS support. | No | SA2 | Yes, minor | SA3 for security aspects. RAN3 for the RAN aspects

## Slide 13: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
9. | Integrated Sensing and Communication | The study should focus on providing sensing services over 5G systems, using NR-based sensing (most probably not in rel.19), as well as non-3GPP type of sensors. Sensing information may be collected by RAN entities(e.g. gNB), UE, or with collaboration of RAN and UE(s) following the SA1 Assumption that sensing target does not actively participate in the sensing operation. SA2 objectives include: Define the system architecture supporting sensing services. Reuse/extend Location Service/Positioning architecture Defining procedures and management functions for sensing services (e.g. a Sensing Management Func.) Defining signaling and service exposure functions for collaborative sensing, for both NR-sensing and non-3GPP sensing. | Yes, SA1 Rel-19 study on Integrated Sensing and Communication (TR 22.837) | SA2 | Yes, major | SA3 for security aspects. RAN1,2,3 for the RAN aspects

## Slide 14: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
10. | Energy Efficiency as a Service | Energy efficiency in communication networks has increased in interest from operators and even gubernatorial bodies, particularly in 6G context. In that context, 3GPP – starting in SA1 – is studying how to offer energy efficiency as a service to application functions and subscribers, and how to cap the emergency consumed for specific services to a certain energy consumption rate in the network. Further aspects include charging based on energy consumption, e.g. increased pricing above a certain energy consumption rate, and definition of energy efficiency modes. Based on potential service requirements to the 5G system arising from SA1 study we can anticipate the following objectives in SA2: Introduction of maximum energy credit limit as policy per service. Framework for Energy consumption reports from 5GC Network Functions and RAN per slice / PDU session / QoS flow. Introduction of energy consumption information in CDRs (charging) Introduction of energy efficiency modes in policy information. Notes: Network only feature, no impact to UE Scope to only provide energy consumption information exchange framework. How NFs and RAN compute energy consumption per slice/PDU session/QoS flow is out of scope of SA2. | Yes, SA1 Rel-19 study on Energy Efficiency as a service (TR 22.882 | SA2 | Yes, minor | SA3 for security aspects, RAN3 for the RAN aspects, SA5 for charging

## Slide 15: Other priorities
ProSe (relay aspects)
  Further ProSe Relay enhancement for multi-hop support for U2U Relay and U2N Relays (L2 & L3)
  Multi-path aggregation enhancement with multiple Relay links
  Support ProSe Relay architecture over non-3GPP link
  Support MBS service over UE-to-Network ProSe Relays
Sidelink Positioning
  Support of joint Sidelink and Uu positioning
  Support of the cross-PLMN operation of the Network assisted Sidelink Positioning/Ranging

## Slide 16: Other priorities
NTN enhancements
  Support for architecture with regenerative payload (RAN node on board the satellite)  Requires major support from RAN3
  For NTN access without a feeder link, enable store and forward communication for all services which can function in this mode
  Support real time communication between UEs accessing the same satellite without going through a land based PLMN
Ambient IoT
  Study system support for A-IoT devices including potentially two streams:
    Support for devices capable of autonomous transmission, for which the focus shall be on further enhancements of IoT features to enable reduced power operation
    Support for devices not capable of autonomous transmission including reachability / mobility management, security and charging aspects
  Views
    Both device types cannot be covered in rel-19
    Consider if support for devices with autonomous transmission offers any commercial values, otherwise do study only in rel-19
    Ambient IoT solutions shall be considered within the current 5GS architecture, this work excludes considering completely new end-to-end system.

## Slide 17: Topics not to evolve in release 19
The standards work done on the following should be considered mature for commercial deployment and therefore it is proposed to not evolve any further in SA2 in release 19:
  NR RedCap
  Network Slicing
  Non-Public Networks
    caveat: any new functionality defined in rel-19 should also consider NPN support
  IIOT/TSN
  Wireless Wireline convergence
  Edge computing
  Location services

## Slide 18: Annex
Further details on the motivation for the high priority topics

## Slide 19: Dual Steer

## Slide 20: Example use cases
Single PLMN
Terrestrial (TN) + Satellite access (NTN)
  NTN used to extend TN capacity/Throughput, or vice versa
  Can be temporary dual RAT coverage (e.g., UEs in a train/cruise-ship/plane, at a stopover)
Other examples: NR + LTE (e.g., if/where Multi Radio Dual Connectivity (option 4) is not available)
Dual PLMN or PLMN + SNPN
Local dual-NW connectivity, e.g., in a stadium
  Using local SNPN/PLMN2 RAT for extra PLMN1 capacity, or vice versa. Can be temporary / on-demand
  Other similar scenarios: campus, enterprise, factory…
Other examples: Terrestrial + Satellite 3GPP access, or dual SAT access (E.g., partnership by PLMN1 with SAT MNO, or b/w 2 SAT MNO)

## Slide 21: Limitations of ATSSS
Currently one 3GPP access and (at least) one integrated non-3GPP access are required to support ATSSS
In certain use cases, non-3GPP access(es) are not ideal to improve capacity, coverage, reliability and QoE, e.g. (see slide #4):
  stadium with SNPN or local PLMN deployment
  3GPP terrestrial combined with 3GPP non-terrestrial access
ATSSS requires (at least) one integrated non-3GPP access to work

## Slide 22: Limitations of other existing solutions
Dual Connectivity (DC) and Carrier Aggregation (CA) have limitations
  PLMN + SNPN and PLMN TN + PLMN NTN when SNPN and PLMN NTN belong to different administrative domains than main PLMN
  DC or CA require RAN sharing arrangements between PLMNs or PLMN+SNPN which are often complex to deploy and have security implications
  DC or CA are cumbersome to deploy in cross- infra vendor deployments
Ultimately, in case of multiple PLMNs or of PLMN + SNPN, currently there is no viable alternative to DualSteer to do aggregation/steering between 3GPP accesses with home operator control

## Slide 23: Proposition for Dual Steer
Enable additional 5GS tools, under MNO control/policy, to improve access/NW resources utilization, capacity, coverage, reliability and QoE, using dual 3GPP access
Provide flexible user plane traffic aggregation, steering & switching at 3GPP layer

## Slide 24: VMR phase 2

## Slide 25: Gaps of VMR defined in Rel-18
The scope of the Rel-18 SA2 work on VMR was restricted to the IAB architecture
This may not be able to support some of the deployment requirements, e.g. when there is no IAB support in RAN, or local traffic switching is required, or more flexible relationships between PLMNs
In summary, other architectures such as the “Velcro” architecture are possible and may fit certain deployment scenarios better
Velcro architecture
IAB architecture

## Slide 26: Additional scenarios for VMR deployment
NTN backhauling, to provide coverage e.g on vessels, aircrafts and in other areas without TN coverage
  Based on work done on NTN backhaul WI of rel.18 to support “mobile relay”
MEC in the relay for support of onboard/local services
  The “Velcro architecture” is better suited for this use case than the IAB architecture

## Slide 27: Additional scenarios for VMR deployment (‘cont)
Extension of UAV functionality to relay to provide service to non-UAV-capable UEs in helicopter or drones

## Slide 28: Generalized framework of data collection from UE

## Slide 29: UE data collection standard status – SA2
Rel-17
  SA2 approved UE data collection solution by using EVEX architecture in clause 6.2.8 in TS 23.288 since Rel-17.
    It is allowed to collect UE application layer data from UE to 5GC
    Both direct data collection ( UE->DCAF->NWDAF) and indirect data collection (UE->DCAF->AF->NWDAF) are supported
    Both 3GPP and non-3GPP defined information is supported

## Slide 30: UE data collection standard status – SA6
SA6 is also discussing UE data collection and exposure between UE and 5GC in Rel-18 in ADAES and eSEALs.
The LS S6-231059 was sent from SA6 to SA4 to express the following requirements for EVEX architecture:
  The ASP shall be able to retrieve/pull collected data on-demand (i.e. without need for setting up session) from the UE Application through a request/response mechanism.
  The UE Application shall be able to send/push collected data on-demand (i.e. without need for setting up session) to ASP through a request/response mechanism.
  The ASP shall be able retrieve collected data from the UE Application through a subscribe/notify mechanism.
  The ASP shall be able to configure the subscription for the UE Application including the specific information to be reported, the triggering criteria and reporting configuration.

## Slide 31: UE data collection standard status –RAN1 & RAN2
AI/ML for NR Air Interface is being discussed in RAN1 and RAN2 in Rel-18
RAN2 is leading the discussion about data collection from UE for ML model training and ML model transfer / delivery to UE.
Several solutions which include EVEX-enhanced solution were proposed in RAN2.
The work should require SA expertise as it goes beyond RAN’s scope for the following reasons:
  RAN can not track a UE between RRC connections.
  ML model training maybe performed by the UE vendor, while the data is available at the operator. We need a standard way to transfer the data out of the operator’s network that is visible and controlled by the operators.
  The SA teams should be involved in designing the architecture for data collection and data storage for RAN AI/ML purposes.
More details can be found in SWS-230056

## Slide 32: Advanced Air Mobility

## Slide 33: SA1 Release 19 Work
SA1 has introduced new requirements for Release 19
  (SA1 Objective 1) Provide additional information to the UAV operator/USS to execute pre-flight preparations and inflight operation (e.g, flight mission application, flight path recommendation, flight monitoring and control)
  (SA1 Objective 2) Use 5G system to support enhancing the UAV flight/route management based on network capacity and QoS information along the planned route
  (SA1 Objective 3) Use 5G system to further enhance the safety and security of drone operations, e.g. supporting UTM in UAV detection and DAA (Detect and Avoid) with network-based solutions
  (SA1 Objective 4) Identify potential new requirements related to redundancy and reliability of command and control (C2) traffic for UAV.

## Slide 34: Advanced Air Mobility
With the rapid growth in aerial vehicles (UAVs, urban transport, EVTOLs, etc.), a large number of activities (ICAO, RTCA, EASA, EUROCAE, FAA, and many other Civil Aviation Agencies) is focusing on ensuring a complete framework for Advanced Air Mobility is being defined
AAM includes UAM (aimed at congested urban areas) and beyond, including rural areas
  Focus is on small UAVs, medium/large goods transport, and people carriers (“aerotaxis”) flying at low and medium altitude
  High altitude aircraft and traditional crewed aircraft are not part of this

## Slide 35: Proposed Objectives for Release 19 Work in SA2
Enhance NEF services to support MNO-UTM data services for intelligent flight planning, flight monitoring, interfacing with UTM infrastructure (e.g. multiple USS), and QoE estimation and planning​
  This corresponds to (SA1 objective 1) and (SA2 objective 2)
  In addition, several recommendation from aviation industry have been introduced (e.g. GSMA and ACJA) for such enhancements to service exposure
  Ensuring a complete set of service exposure by an MNO to entities in the aviation industry (UAS operators, UTM, C2CSPs, etc.) enables a valuable service proposition by MNOs to the aviation industry, and enable cellular networks to be the safe and reliable communication backbone for the aviation vertical

## Slide 36: Proposed Objectives for Release 19 Work in SA2
Enable network-assisted/ground-based DAA solutions leveraging input from sensing and other "sensors" in RAN and UEs, and leverage NEF and edge computing to provide the ground component of a complete DAA solution​
  This corresponds to (SA1 objective 3)
  There is a clear need in the aviation industry for a network-assisted/ground-based solution to enhance current aircraft-to-aircraft solutions to create a comprehensive safety solution for AAM​.
    Work in various aviation groups (RTCA, EUROCAE, EASA, ACJA, etc.) has identified the need for such network-based solutions
    Network-based solutions enable MNOs to provide valuable value-added services to the aviation vertical

## Slide 37: Proposed Objectives for Release 19 Work in SA2
Enhance multi-PLMN connectivity for redundancy ​
  SA1 has been studying requirements for multi-PLMN connectivity for aerial vehicles to provide improved reliability
    The simultaneous connectivity to multiple PLMN, where one is actively used and the other is standby, gives the unique benefit of maximizing reliability in areas where the coverage of a PLMN may not be optimal
    Architectural enhancements need to be studied and gaps identified to enable such scenarios, building on the features already defined by 3GPP
  This relates to some objectives of DualSteer SI, but focuses on some different aspects such as multi-subscription and different PLMNs

## Slide 38: Proposed Objectives for Release 19 Work in SA2
Study support of C2CSP model, potentially via extensions of IMS DC solution and IMS framework.​
  ICAO and RTCA are defining the model for C2 Connectivity Service Providers to leverage cellular networks
  3GPP has defined several tools that enable the C2CSP framework, including the introduction of the IMS Data Channel which is perfect fit for C2 traffic
  The aim is at identifying the building blocks and architectural enhancements to enable the support of the C2CSP model(s) being defined by the aviation industry (ICAO, RTCA, ACJA, GUTMA)

## Slide 39: XR enhancements

## Slide 40: Limitations of Rel-18 XRM
Rel-18 XRM made significant progress on XR awareness in 5G by introducing the PDU Set based QoS handling framework.
However, due to time constraints, some important features were left out of the Rel-18 XRM work item
It is important to extend the framework to address:
  Awareness of Application Layer Forward Error Correction (AL-FEC) at RAN can assist detection of PDU-set errors and allow scheduler optimization in delivery of PDU-sets
  For certain types of XR flows, PSDB/PDB does not fully represent the actual latency requirements because applications care about the absolute delivery time of display.
  Better adaptability of 5GS QoS level for XR traffic

## Slide 41: Application Layer Forward Error Correction
There are requirements for XR application protocols to use Forward Error Correction (AL-FEC), see, e.g., RFC 8854 for WebRTC, RFC 8627 for RTP
If RAN scheduler aware of AL-FEC details, it can improve scheduling, e.g.:
  If content ratio = 75%, one out of four PDUs of the PDU Set can be dropped and the PDU Set is still considered successfully delivered;
  Can decide to stop transmission when UE receives sufficient PDUs.
RAN to AF indication useful as well, e.g.:
  RAN can ask to enable/disable FEC
UPF
RAN
UE
SMF
PCF
FEC content ratio = 75%
4
3
2
1
4
2
1
PDU set w/ 4 PDUs

## Slide 42: Better adapt 5GS QoS level for XR traffic
As of today, the concept of Alternative QoS Profile (to enable AF/AS to adapt to changed radio conditions) applies only to PDUs
  AQP = {PDB, PER, GFRB, (MDBV)}
In order to enable better adaptability also for PDU Set based traffic, it is useful to study how to extended the AQP concept to PDU Sets
  E.g., AQP = {PSDB, PSER, GFBR, (MDBV)}
UPF
RAN
SMF
PCF
1) PSDB, PSER
AQP1 = PSDB1, PSER1, GFBR1
AQP2 = PSDB2, PSER2, GFBR2
AQP3 = PSDB3, PSER3, GFBR3
2)
3) Established QoS Flow with PSDB, PSER
UPF
RAN
SMF
PCF
1) QNC: AQP1
2) QNC: AQP1

## Slide 43: Lightweight Access Aggregation and Steering of Wi-Fi in 5GC

## Slide 44: Limitations of current ATSSS architecture
Requires support for (un)trusted connectivity of integrated Wi-Fi to 5GC
Commercial deployments of TNGF/N3IWF are very limited
Value of N3IWF beyond support for voice over Wi-Fi (e.g., for general internet access) is questionable
  this would effectively be an ePDG connected to 5G core
  it would face hardware capacity issues due to large increase of traffic volume (from, e.g., 20-50 Kbps per UE for VoWiFi to possible 100s of Mbps for internet traffic) with questionable RoI
ATSSS requires either N3IWF or TNGF to work

## Slide 45: Motivation for a different architecture
Hence the need for supporting a solution for non-integrated Wi-Fi-based traffic aggregation/steering/switching that…
  does not require N3IWF support
  achieves some targets of ATSSS (e.g., traffic aggregation)
  enables initial deployment with limited CAPEX

## Slide 46: Example architecture
Proxy works via N3 and Nx
MASQUE H3 proxy (UDP over H3)
No control plane (N1/N2) for Wi-Fi access
Non-integrated aggregated PDU Session

## Slide 47: Timing as a service over NB-IoT/eMTC

## Slide 48: Background on Timing Resiliency work
Timing as a service refers to providing timing information to UEs​ as a monetizable operator service
  Rel-18 enabled
    subscription control for timing delivery to individual UEs​
    providing quality information about the 5GS clock to UEs
  Clock quality information enables UEs to
    determine if the 5G clock quality is sufficient,
    compare the 5G clock quality against other available time sources
    select the best available clock source​
Timing as a service enhances timing resiliency as it enables use of 5GS as another reliable time source.

## Slide 49: Motivation for enhancements
Timing as a service is only supported for NR
NR coverage is still quite limited and may not be available in many areas for quite some time and cost of the UE can be problematic for certain use cases
Other RATs (terrestrial and non-terrestrial NB-IoT and eMTC) do not support timing as a service
  NB-IoT/eMTC do not support providing time selectively to UEs based on subscription information and
  NB-IoT/eMTC do not support providing clock quality information to UEs.​
  Note: For NB-IoT/eMTC over NTN, timing as a service is useful if GNSS is not supported or temporarily not available.​

## Slide 50: Proposal to extend support on NB-IoT/eMTC
Enable timing as a service for NB-IoT/eMTC (terrestrial and NTN) connected to EPC to maximize monetization potential for operators
  Enable selective reference time delivery for NB-IoT/eMTC based on subscription information
  Enable delivery of clock quality information to UEs for NB-IoT/eMTC (terrestrial and over NTN)​
  Support propagation delay compensation (specifically relevant for NB-IoT/eMTC over NTN for UEs without GNSS)

## Slide 51: Enhancements in handling of radio capabilities

## Slide 52: Problem statement (#1)
Issue #1: Disabling RATs the UE radio capability does not need to support due to UEs subscription
  It is possible that certain UEs due to their subscription are only allowed in 5GS and not in LTE/EPS e.g. "CAG only" UEs, UEs with no NTN subscription etc.
  Nevertheless since the UE (modem) has radio capability to access LTE/EPS in certain cases it will attempt to do idle mode reselection to LTE and as a result be rejected.
  This procedure wastes battery power for the UE and network resources for the network. It is therefore proposed that the network indicates to the UE that due to its subscription it needs to disable its radio capabilities for specific RATs and as a result the UE does not need to perform inter-RAT measurements and mobility.

## Slide 53: Problem statement (#2)
Issue #2: Exposure of support/no support of specific UE radio capability by NEF
  In certain deployments the viability of a particular application and the actions that an Application Function (AF) will take depend on the “alignment” of radio features deployed in network and UE.
  Network (PLMN and SNPN) may deploy a sub-set of the available radio features. UE operating in such network may or may not support the radio capabilities to operate such features.
  How an AF (internal or external to the network) know in advance before initiating a session for a particular application that there is “alignment” of radio features that would be required in order to support this application or the specific function is required.
  Examples use cases: Timing resiliency service (delay compensation), XR (RedCap vs full scope NR), QoS sustainability

## Slide 54: Problem statement (#3)
Issue #3: Transfer of radio capability container from AMF to MME (and vice versa)
  When UE moves frequently between EPS and 5GS (in idle mode) a new retrieval of radio capability is needed from target system when the UE moves to connected mode.
  This procedure would be optimised if like inside 5GS there is transfer of the radio capability container from AMF to MME and vice versa in similar fashion that is transferred between AMFs inside 5GS.

## Slide 55: Proposed work
For issue #1: Identify how to prevent a UE to access a specific RAT/system in which it does not have subscription and therefore will be rejected. How to indicate to UE to disable certain radio capabilities in order to avoid attempting to register to this RAT/system and be rejected. How to define exceptions for emergency services.
For Issue #2: How an AF (internal or external to the network) know in advance before initiating a session for a particular application that there is “alignment” of radio features that would be required in order to support this application or the specific function is required.
For issue #3: How to transfer the radio capability container or UE Radio Capability ID between AMF and MME (and vice versa) in order to avoid retrieval of radio capabilities from the UE (if possible) from the target system.
The work will be based on following deployment options: 1) RACS support in UE and NW, 2) No RACS in UE, but support of RACS in NW, 3) No RACS support.