## Slide 1: On High Priorities in Release 19
Wireless Systems Laboratory & Space-Time Standards Laboratory,
National Institute of Information and Communications Technology (NICT), Japan

## Slide 2: Outline
Overall View on Rel-19 Content
Background
  Multiple Network Resources
  Local Reference in Space & Time
Summary

## Slide 3: Overall View on Rel-19 Content
S. NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/ Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | Enhanced support of DualSteer and ATSSS | 5G system support for multipath transmission with more than or equal to two paths composed of TN(s)-NTN(s) and/or PLMN(s)-NPN(s). Key Features includes - Enhanced robustness to high latency path Enhanced efficiency of multipath aggregation Enhanced responsiveness | FS_SOBOT FS_Metaverse FS_DualSteer | SA2 | Yes | Don’t Know
2. | Local reference in space and time | Requirement for the synchronization and positioning becomes more divergent depending on the use cases. Locally available high precision in time and positioning is required, for instance inside or around factory, while the link to global time and space reference is also maintained. Key Features includes – Locally available framework of space and time Link of the local coordinates to the global coordinates such as UTC (time) and ITRF (space) | FS_SOBOT FS_Sensing FS_Metaverse | RAN | Yes, Major | Don’t know

## Slide 4: Multiple Network Resources
NICT studies Human-Robot society based on service robot
  The realization of reliable Human-Robot society by heterogeneous mobile network resources from multiple operators
Expanded activity range and available resources by resources from multiple NWs
Moving/Time
Resource
Requirement
by robot
Case of using resources from multiple NWs
Case of using resources from only PLMN A
NPN A with 3GPP or non-3GPP deployment by local operator
PLMN B
PLMN A
NTN
NPN B
Moving route

## Slide 5: Local reference in space & time
NICT is developing three technologies relevant to synchronization and high accuracy positioning
  Compact atomic clock (CLIFS)
  Carrier-phase based wireless two-way interferometry (Wi-Wi) for synchronization and precise positioning
  Algorithm for cluster clocks
These are integrated to a locally available reference of time and positioning, where at least a single point should be linked to conventional (global) reference.
local space-time synchronization
global space-time synchronization
High precision (mm, ns)
global
local
edge servers in roadside for low latency communications
IoT
sensors
IoT
sensors
Low precision (m, ms)
Compatibility or ability of conversion in local and global system
is worth to be discussed.
CLIFS: Chip Level Integrated Frequency Standard, Wi-Wi: Wireless two-Way interferometry

## Slide 6: Summary
It is proposed:
  To study mechanism and architecture for Human-Robot society based on
    Heterogeneous mobile NW composed of more than or equal to three access paths
      related to DualSteer, ATSSS, NPN, NTN/5GSat, etc…
    with
    Enhanced robustness to high latency path
      c.f., GEO-based NTN with about ms round-trip time
    Enhanced efficiency of multipath aggregation
      c.f., wide NW performance range from various systems and operators
    Enhanced responsiveness
      e.g., how to assist moving UE to quickly determine availability of each network
  To study a compatibility of highly precise local space and time with a global reference, which forms an infrastructure in non-human communications such as M2M, V2X, etc.
Contact info: std_stsl@ml.nict.go.jp, std@ml.nict.go.jp