## Slide 1
Views on IoT in 6G
6GWS-250189
Notes: 1

## Slide 2
Sea
Port
Land
3GPP - a Global solution
For a vertical, 3GPP is a ecosystem – expectation to have generic devices working with MNOs, NPN and NTN globally

## Slide 3
IoT/Verticals – Lifecycle of IoT devices
From Standard
to implementation
Adoption
/ validation of Technology
Roll out/
deployment of devices/
Exploitation
Duration of life of the device
Decommissioning
Use of a technology
3 to 5+ years
3 to 10 years
5 to 20 years
5 to 20 years
3 to 10 years
15+ to 40/50+ years

## Slide 4
Consumer market and vertical markets have different expectations in terms of lifecycles and deployments
  Expectations for Private mMTC (NB-IoT / eMTC) network => likely to be remaining for more than 30 years / 40+ years in some verticals
  Expectations of exploitation of 5G services by verticals depending on the duration of life of their equipment
    Duration of life of a plane ± 25 years
    Duration of life of a Train ± 40 years
    Duration of life of a smart meter ± 25 years
=> Verticals expect to keep mMTC solutions and/or 5G solutions for the next 20 to 50 years
IoT/Verticals – Different perspective than consumer

## Slide 5
IoT/Verticals – what is needed by when
 | 2025 | 2030 | 2035 | 2040+
Private Network/vertical demand | Mostly Deployment of PN for IoT (4GC) | Some PN for IoT on 4GC + Need to support IoT On 5GC | Still some PN for IoT on 4GC + Increase demand to support IoT On 5GC + First need to support IoT on 6GC | IoT On 5GC + IoT on 6GC
Satellite operator | IoT NTN on 4G only (LEO/GEO) | Several constellations IoT on 4GC + Need to support IoT NTN On 5GC (for GEO) | Still several constellations IoT on 4GC + New NR based constellations need to support IoT (on 5GC) | Most NR based constellations to support IoT + new 6G based constellations with need to support IoT
MNO | IoT on 4G only | Unclear | Unclear | Unclear
Requires to be part
of standard in Rel-20
Requires to be part
of 6G from the beginning

## Slide 6
There is an expectation/need from verticals to keep NB-IoT and eMTC at least for the next 30 to 40 years
Expectations from verticals in 6G :
  NO new standard / no new LPWA to address the use cases of NB-IoT/eMTC
  Allow a path to have NB-IoT/eMTC supported by 5GC then by 6GC to maintain technology at least for 30/40 years
The future of mMTC in 6G