## Slide 1
Views on 6G RAN Requirements and Key Technologies
China Unicom
3GPP workshop on 6G
Incheon, Korea, March 10-11, 2025
Agenda item: 4
6GWS-250190

## Slide 2
1. General Views on Rel-20
The Real Commercial needs of 5G-A are very strong from operator side.
  Low Altitude Economy：China Unicom has very strong needs to to build an intelligent integration network of TN and NTN and formed a service model that is based on data services and runs through the industrial chain capabilities of drones, providing a comprehensive platform for urban governance. It has been widely applied and practiced at the national and urban governance levels.
  Ambient IoT：Expand billions of IoT connections and explore the new business applications.
6G is planned for a sufficient duration to study 6G system design and key technologies for a new generation system.
  Learn the lessons from 5G first release, NSA vs SA, Complex system design.
  New challenges to consolidates the common needs/interest from diverse regions.
  Good pace of standardization on the common parts features of 5G-A/6G, e.g. ISAC, A-IoT, AI/ML.
  New area studies for industries, e.g. NTN for broadband service, V2X for Intelligent Connected Vehicles.
  Good balance of Rel-20 TU allocation between 5G-A and 6G is critical for seizing market opportunity and exploring the new commercial use cases. (50%, 50%)

## Slide 3
2. Views on Rel-20 6G
6G needs a sufficient duration to study 6G system design and key technologies for a new generation system.
  Before start with 6G Rel-20, the requirement input from operators, vendors, service provides are crucial to consolidate the common views of 6G.
Innovation is the greatest driving force of 3GPP.
Network architecture evolution: New 6G core vs. 5GC, SA vs. NSA parallel with SA.
Ensure well design of universal features and avoid over-design add-on features as 5G.
Protocol flexibility adaptive for various types of services, e.g. Ubiquitous connectivity, HRLLC.
Day-1 Commercial feature list, e.g. AI/ML, ISAC, 6G NTN for broadband service, IoT, HRLLC, V2X, etc.
Coordination btw different working groups of RAN and SA.
Notes: Boost revenue and cut cost.

## Slide 4
3. Views on 6G Services
6G Services
  Ubiquitous connectivity: Cellular-based connection with even larger bandwidth and higher data rate, i.e. 2C service, 6G NTN, V2X.
  Integrated Sensing and Communication: Drone/UAV, Vehicle.
  AI and Communication: AI as a Service, AI-native features, AI agent network service, AI agent application, AI-enable/AI Agent Robotic.
  Immersive Communication: XR, XR-like service, MR.
  Massive Communication: Unified air interface for all categories providing from higher data rate to lower date rate.
  HRLLC: Vertical industry service, automatic driving and intelligent connected vehicles, Power grid.
    HRLLC service always has diverse requirements on data rate, latency. 6G shall consider the flexible design on HRLLC features.

## Slide 5
4 Views on 6G System Design
6G System Design
  6G Spectrum: low frequency (e.g. 900MHz), C-band(e.g. 3.5GHz), U6G, 26GHz.
  Single Carrier BW: 200MHz/300MHz/400MHz for FR1, 400MHz/800MHz for FR2.
  Waveform: reusing OFDMA design and open for the adaption of new waveforms.
  SCS: prefer to support a limited number of configuration set.
  Coding & Modulation: open for new design.
  ELAA: Support 2048/4096 or more AEs for U6G and 6G spectrum.
  AI-Native function: support in RF, PHY, MAC, RRC for NW side and UE side.
  New service capability: service-aware/content-aware, latency-aware, automatic NW mngm, SLA enh for new business(vertical application), etc.

## Slide 6
5. Views on 6G RAN Network Architecture
Motivation
  The option of 6G RAN Network architecture is always a hot topic at the beginning of new generation.
    Operators focus on the evolution and migration path from 5G to 6G: New 6G vs. 5G-evolution, SA-only vs. NSA parallel with SA, align with Core network architecture.
    Support the split architecture for RAN node and the tight coordination with core network.
Views
  Open to discuss the new architecture and interfaces for 6G RAN node.
    Prefer SA mode and new 6G core.
    RAN node to core network, 6G-NG interface.
    Need to decide whether to support CU/DU split as F1 interface.
    No need to specify fronthaul interface in 3GPP, i.e. reuse eCPRI protocol.
6G NEW CORE
6G RAN Node
Base band
6G NG
6G RAN Node
Radio part
6G RAN Node
RF part
Fiber fronthaul
Cable connection

## Slide 7
6. 6G RAN candidate features
6G
New Capability
ISAC
AI-native for Network
new 6G IoT
01
Service Assurance
Service quality assurance for XR, AI, ISAC, etc.
Protocol adaptation for vertical service, HRLLC etc.
05
Functionality evolution
eMIMO/ELAA, MRSS, MBSC
Unified mobility framework
low-cost Coverage, poisitioning
04
Green and Sustainable
Collaborative energy saving and power saving for UE&NW.
02
Ubiquitous connectivity
6G NTN for broadband service, 6G IoT NTN evolution.
V2X for intelligent connected vehicles
03

## Slide 8
6. 6G candidate feature of ISAC
Motivation
  New waveform and signal design shall be studied for 6G ISAC to fulfill higher performance requirement.
  Support higher precision and larger range for UAV and smart transportation/eVTOL, and new scenarios, i.e. smart factory, smart healthcare, public safety.
  Channel modeling is studied from Rel-19.
Potential Objective
  Good split the content of ISAC between 5G-A and 6G.
  5G-A focus on architecture of the high layer to support sensing function.
  6G focus on support all sensing modes and lower layer design, e.g. waveform, subframe, ISAC procedure, signaling, etc.
  Study ISAC scenarios, requirements and functionalities for sensing assisted communication.
UE

## Slide 9
7. 6G candidate feature of AI/ML framework and Use Case
Motivation
  6G AI-Native Network is widely discussed for integration of communication, computing, sensing and intelligence.
  6G AI-native network is an intelligent and efficient system for NW operation, management and optimization.
Potential Objective
  Identify and define the unified AI/ML framework and functionalities in 6G UE/RAN/CN domain in collaborative/non-collaborative manner.
  5G-A AI/ML use cases are considered as the starting point.
  Study and support new 6G AI application scenarios on the basis of 5G use cases, i.e. autonomous driving, AI agent/ AGI service, etc.
  Extensively study AI/ML new use cases and identify the impacts on the design of 6G network architecture, protocol, interworking with existing 5G network, etc.
Local inference and training
6G AI framework（AI for Network）
AI/ML model training and inference
Cloud-based model training
Real-time AI data
Non-real-time AI data
CN/OAM/Server in MNO
Real-time AI data
Non-real-time AI data
AI
AI
AI
AI Model transfer
AI Model transfer
Edge computing resource

## Slide 10
8. 6G candidate feature of M-IoT
Motivation
  New design of Ambient IoT for outdoor scenarios
    An OFDM-based waveform with sufficient output power can be adapted by new type of A-IoT device.
  Massive IoT support for 6G
    Massive IoT should be supported in the first release of 6G and the overall 6G design should support low-end and high-end devices.
    6G massive IoT should cover all use cases and different IoT categories. Ambient IoT could be a parallel track with 6G massive IoT.
    6G NW performance should not be degraded while the massive IoT devices connect to NW and coexist with the normal terminals (e.g. smartphones).
  The coexistence of 4G and 6G IoT deployments
    Ensure the longevity of 4G IoT in the 6G.
Potential Objective
  New scenarios can be studied.
    Power substation inspection, pharmaceuticals tracking, valuables recover.
  Providing all types of 6G IoT service at Day 1 for larger bandwidth and peak data rate.
  Low power consumption, reduce the complexity and cost of IoT devices are mandatory requirement.
Timeline
UE Capability
RedCap/
eRedCap
5G NR
6G
Massive
IoT
LTE-M
NB-IoT
Ambient IoT

## Slide 11
9. 6G candidate feature of HRLLC Vertical
Motivation
  Service requirements: Considering ITU HRLLC scenario requirements and practical vertical needs, it aims for ~1ms E2E latency, high-precision synchronization, and high reliability (99.9999%).
  Optimized design and reduced complexity: 6G HRLLC design should avoid the introduction of excessive options and redundant designs.
  Integration with non-3GPP networks: integrate HRLLC into existing non-3GPP networks, particularly wired networks in industrial scenarios (such as Industrial Ethernet).
    Potential objectives：
  Physical layer: Reuse 6G eMBB basic design, and meets HRLLC requirements via partial PHY design, such as subcarrier spacing and frame structure design, to enable 1ms latency.
  Protocol simplification: For localized networks such as industrial network, the protocol stack should be further simplified to reduce E2E latency and better integrated with wired networks.
6G HRLLC for vertical
Protocol simplification & flexibility

## Slide 12
10. 6G candidate feature of Mobility Framework
Motivation
  5G specs support mobility functions for various scenarios (CA, MR-DC) and RAT (4G, 5G, 5G-A), defining new measurement frameworks (L1/L2/L3) and mobility mechanisms (Legacy L3 handover, CHO, LTM).
  Research on a unified mobility framework to reduce complexity in protocol and end-to-end network implementation, while ensuring a seamless user mobility experience.
  Interworking between 6G and 5G is high priority.
Petontial Objective
  Unified measurement framework for L1/L3 measurement and reporting mechanism.
  Reduce the HO delay as well as guarantee the service experience of UE.
  Support the Mobility enhancement between TN and NTN network,e.g. 5G/4g and NR NTN.
UE
6G mobility

## Slide 13
11. 6G candidate feature of RIS
Motivation
  RIS technology offers a promising solution to improve the coverage by deriving more beams
    Enhancing Spectral Efficiency and Coverage
  RIS acts as the passive device, making 6G more sustainable and cost-effective
    Addressing Energy Efficiency Challenges
  RIS enables a flexible and adaptive network architectures
Petontial Objective
  Study channel modeling for RIS function.
    mmWave band is high priority.
  Study the enhancement of interaction btw 6G base station and RIS.
    Consider NCR in Rel-18 as baseline.
  Study signaling-assisted RIS operation with AI.
    e.g. beam management.

## Slide 14
12. 6G candidate feature of Content Aware Scheduling
Motivation
  Enhance E2E experience, improve NW resource efficiency.
    NW side support the capability to aware type and content of different service to guarantee various service requirements, e.g. E2E delay time, jitter, throughput, quality of service.
    Enhance the network's intelligence resource allocation efficiency for a wide range of scenarios, enabling automated service assurance within network functions.
Potential Objective
  Resource scheduling matching, e.g.
    Attaining latency awareness across various domains in RAN.
    Acquiring the channel quality and the required service rate synchronously.
  Intelligent service matching, e.g.
    The RAN network function can intelligently control and modify according to the feedback received from user.
    Support various types of services, such as XR service, AI service, sensing service, etc., to ensure quality of service to fulfill performance requirements of each service.
OAM domain
UE domain
RAN domain
CN domain
AI service 1
Service identification
QoS-based
scheduling
QoS Monitor & Service control
UE Service quality info
AI service 2
ISAC service
XR and XR-like service
HRLLC service1
Network mngm
Service quality info in RAN
Service quality info in CN

## Slide 15
13. 6G candidate feature of RAN Sharing/Multi-Band Single Carrier
Petontial Objective
  6G RAN sharing is mandatory, taking 4G/5G RAN Sharing commercial features as baseline.
    200MHz/300MHz/400MHz for FR1, 400MHz/800MHz for FR2
  Significant improvement for multi-carrier operation
    Reduction on overhead for sync, reference signal, and support flexible and on-demand configuration.
  Support AI-enable scheduling and resource allocation
    Content-aware and service-oriented E2E solution.
PDCCH-1
CC1
CC2
CCn
……
PDSCH-1
PDSCH-2
PDSCH-n
PDCCH-n
AI-scheduler
……

## Slide 16
Thanks!