## Slide 1: Chair’s summary of the 3GPP workshop on
Puneet Jain (TSG SA Chair)
Ronald Borsato (TSG RAN Vice Chair)
Peter Schmitt (TSG CT Chair)
6GWS-250238
AI# 6
6GWS-250238, 3GPP workshop on 6G, Incheon, Korea, 10 - 11 Mar 2025

## Slide 2: General Disclaimer
The Chairs' summary is based on a compilation of input papers submitted for the 3GPP workshop on 6G.
It is not an exhaustive record of all views expressed, or proposals submitted in the input contributions, nor does it reflect a consensus views among 3GPP members.
This summary does not imply any prioritization or ranking of 6G technical areas.
The scope of work within 3GPP is determined by its established working procedures, and there is no assurance that all the potential technical areas mentioned will be pursued as part of 3GPP studies in Release 20.

## Slide 3: Outline
3GPP Workshop on 6G – Introduction
6G Motivation (Why 6G?)
6G Goals
Lessons Learned from 5G
Potential 6G Technology Areas for 6G study
3GPP 6G Workplan/Timelines
Summary of Next Steps Towards 6G

## Slide 4: 3GPP Workshop on 6G
Workshop Presentations: Link
Opportunity for 3GPP members to present their vision & priorities for next generation radio technology, system architecture, core network and protocols.
𝟭,676 𝗿𝗲𝗴𝗶𝘀𝘁𝗿𝗮𝘁𝗶𝗼𝗻𝘀, 𝟳48 𝗶𝗻-𝗽𝗲𝗿𝘀𝗼𝗻 registrants
𝟮19 input 𝗰𝗼𝗻𝘁𝗿𝗶𝗯𝘂𝘁𝗶𝗼𝗻𝘀 from 𝗼𝗽𝗲𝗿𝗮𝘁𝗼𝗿𝘀, 𝘃𝗲𝗻𝗱𝗼𝗿𝘀, 𝗮𝗰𝗮𝗱𝗲𝗺𝗶𝗮, 𝗮𝗻𝗱 𝗠𝗥𝗣𝘀
Discussions covering 𝗿𝗮𝗱𝗶𝗼, 𝗰𝗼𝗿𝗲 𝗻𝗲𝘁𝘄𝗼𝗿𝗸, 𝗽𝗿𝗼𝘁𝗼𝗰𝗼𝗹𝘀, 𝗮𝗻𝗱 𝗺𝗼𝗿𝗲
Mar 10th to 11th in Incheon, Korea

## Slide 5: 6G Motivation (Why 6G?)
Support for New Services and Use Cases
  Enabling new services and use cases beyond traditional communication, such as integrated sensing and communication (ISAC), XR/immersive communication, and AI-based services – Compute.
Revenue Growth and Monetization
  Creating new revenue streams by monetizing network capabilities and supporting diverse applications across industries.
AI and Automation
  Implementing AI-native networks for automation, optimization, and improved efficiency in network management and resource allocation.
Energy Efficiency and Sustainability
  Reducing energy consumption and promoting environmental sustainability through energy-saving features in network design and AI-driven power management.
Spectrum Efficiency
  Utilizing spectrum efficiently, including dynamic spectrum sharing and exploring new spectrum bands.
Ubiquitous Coverage
  Seamlessly integrating terrestrial and non-terrestrial networks (NTN) for ubiquitous coverage and resilient services.
Total Cost of Ownership (TCO) Reduction
  Reducing capital expenditure (CAPEX) and operational expenditure (OPEX) through simplified network operations and improved energy efficiency.
Improved Service Reliability and Customer Experience
  Enhancing service reliability, resiliency, and insights for improved customer experience.
Network Simplification
  Simplifying network architecture, reducing complexity, and improving operational efficiency.

## Slide 6: 6G Goals
Sustainability
  Focus on environmental, social, and economic sustainability. This includes energy efficiency, reduced resource consumption, and contributing to global emissions targets.
Resilience
  Designing networks that are robust and can withstand various events, including operational errors, heavy traffic, and disasters.
Security
  Increased security, integrity, and privacy are required from day one, incorporating zero trust principles and post-quantum security measures.
Customer Experience
  Improved end-user/customer experience through seamless, ubiquitous connectivity, ensuring reliable, high-quality services delivery. Optimized Quality of Experience (QoE) across diverse devices and network conditions.
Efficiency
  Cost reduction via simplified systems and operations, with AI-driven automation and optimization.
Interoperability
  Promoting open/interoperable interfaces and collaboration to foster innovation and avoid market fragmentation.

## Slide 7: Lessons Learned from 5G
Challenges in Migration
  The transition from 5G Non-Standalone (NSA) to Standalone (SA) proved complex and difficult.
Architectural Complexity
  An excessive number of architectural options, features, and configurations led to high system complexity, impacting UE capabilities and deployment efficiency.
Slow Adoption of Key Capabilities
  Certain 5G features, such as network slicing, experienced slow adoption—necessitating an analysis of underlying causes and potential simplifications in 6G.
Deployment Inefficiencies
  Issues identified during 5G rollouts, including NRF profile inefficiencies and protocol challenges (e.g., HTTP/2 over TCP), should be addressed in 6G.
Optimized Network Functions
  Ensuring efficient Network Function (NF) sizing with clear decoupling, while further exploring stateless architectures.
Functionality Optimization
  6G should focus on a well-dimensioned set of functionalities, minimizing redundant options and excessive configurations to reduce complexity.

## Slide 8: Potential Technical Areas for 6G Study

## Slide 9: 6G System Design Considerations
Focus and Simplicity
  Lean and streamlined standards for 6G, e.g., by dimensioning an appropriate set of functionalities, minimizing the adoption of multiple options for the same functionality, avoiding excessive configurations, etc.
Cloud-Native Architecture
  Designing networks to be cloud-native to enable flexibility, agility, and innovation.
AI-Native Design
  Integrating AI and ML frameworks natively into the network for intelligent automation, optimization, and improved efficiency.
Scalability and Modular Design
  Implementing a scalable and modular design that allows a wide range of features, device types, services, and spectrum bands to be developed and deployed as needed.
Software-Driven Deployment
  Software-driven deployment with needs-based hardware refresh to allow for continuous innovation and agility.
Interoperability
  Designing components with interoperable interfaces and a unified management framework to ensure interoperability and avoid fragmentation.
Enhanced Security
  Ensuring the 6G system is secure by design to provide enhanced security and privacy.
IoT Support
  Designing 6G to support diverse IoT device types and use cases from day one, with a focus on long-term commitments and multi-generational solutions.
Service-Aware
  Enabling a service-aware intelligent network powered by AI-native, programmable, and service-aware 6G RAN.
Ubiquitous Connectivity
  Providing ubiquitous coverage through seamless integration of terrestrial and non-terrestrial networks.

## Slide 10: Radio Access Network for 6G design considerations
  6G Radio interface: Non-backwards compatible (from a UE perspective) to exploit full potential, with certain characteristics (e.g., waveform, modulation and channel coding) based on 5G NR with possible enhancements.
  Study needs to show significant gains to justify 6G Radio.
  Lean and Streamlined 6G, dimension appropriate set of functionalities, minimize adoption of multiple options for the same functionality, avoid excessive configurations
  Superior coverage for 6G radio from Day-1
  Diverse device types with scalable design from Day-1 based on, for example: Bandwidth/data rate, form factor, energy consumption
  Harmonized TN and NTN design
  AI/ML: Extensible AI/ML framework built on 5G-A as appropriate, with native support for AI/ML lifecycle management, (e.g., configuration, performance monitoring, deactivation, and seamless transition to conventional algorithms). And exploring new use cases.

## Slide 11: Core Network for 6G design considerations
A preference for a single 6G Standalone Architecture is noted, with SA mode as a baseline
Core Network for 6G to be designed to cover new 6G requirements regarding AI, connectivity, Security/Privacy/ Resilience with possible reuse of the 5G SBA/SBI framework and investigate enhancement 5G SBA/SBI architecture
Simplification of architecture and streamlining of NFs definitions and interactions/interfaces/protocols
Investigation of new functions based on the SBA architecture to support new 6G Services
Designed to integrate and interoperate with various access technologies, including FWA and Wi-Fi access
A unified network exposure framework for simplifying the 3GPP-wide exposure framework to foster an API economy of scale

## Slide 12: Migration/Architecture Options
6G SA standalone as the primary architecture option. Based on lesson learned from 5G, avoid 6G Non-Standalone (NSA) options if possible.
MRSS (5G+6G spectrum sharing) and 6G-6G carrier aggregation
Other aggregation means were proposed as possible additional migration path, for example -
  5G-6G Dual Connectivity
  5G-6G Dual-stack

## Slide 13: Interworking with legacy 3GPP systems
Seamless interworking with 5G system
  Single registration vs dual registration
Seamless interworking with 4G system?
  General consideration to avoid interworking with 4G
  Scenarios needs to be further discussed
No interworking with 2G and 3G system

## Slide 14: Spectrum Considerations
Support for existing spectrum critical (FR1 & FR2)
  Performance and efficiency enhancements needed
Support for new spectrum in upper mid band critical
  Desire for deployments based on existing mid band cell site grid
  Evolution of MIMO technology with increased number of ports and antenna elements key to deliver performance in this frequency range
Improvements in the support of different spectrum assets
  Reduced overhead and energy consumption, improved delay to access high data rates, reduced complexity in standardisation, implementation and deployment, etc

## Slide 15: 3GPP 6G workplan/timeline
(source: 6GWS-250240)

## Slide 16: Overall 3GPP 6G Workplan
Stage-1 workshop on IMT2030 use cases
First 3GPP TSG-wide 6G Workshop
To discuss vision & priorities for next generation radio technology, system architecture, core networks and protocols.
Studies for 6G
from Release 20
Normative work for 6G
from Release 21
Rotterdam, Netherland, May 8 – 10, 2024
Workshop Summary: SWS-240025
Workshop Presentations: Link
Incheon, S. Korea, March 10 – 11, 2025
WG SA1
TSGs#107
2024
SP-241391 : SA1 6G study item on use cases and service requirements (FS_6G_REQ) approved at TSG SA#105.
    RP‑243327 : The 6G RAN Study (part I: ITU focused) was approved at TSG RAN#106
    See next slide for the 6G studies timelines
Release 21 is expected to produce the 1st set of 3GPP 6G technical specifications and will be the release for IMT-2030 submission before 2030 and is expected to be delivered with a single drop (i.e., a single code freeze).
Rel-21 timeline is to be decided no later than June 2026
However, ASN.1/OpenAPI freeze date is no earlier than March 2029
2030

## Slide 17
2024
#103
Mar.
#111
Mar.
#107
Mar.
#104
Jun.
#108
Jun.
#112
Jun.
#105
Sep.
#109
Sep.
#102
Dec.
#106
Dec.
#110
Dec.
TSGs
Workshop on 6G
Stage 3 6G SID def.
#113
Sep.
#114
Dec.
#115
Mar.
Jun
Workshop IMT-2030 use cases
#116
SA1 6G Study
SA1 6G SID def.
RP IMT-2030 disc.
RP ITU Study
RP 6G Study
RAN1 6G Study(ies)
SA2 6G Study(ies)
Stage 3 6G Study(ies)
2025
2026
2027
SA2 & RAN WGs 6G SID def.
SA3/4/5/6 SID def. and compl. TBD
RAN2/3/4 6G Study(ies)
or
TBD
Release 20: 6G Timeline
Tech proposals
IMT-2030 Technical Performance Requirements
Requirements, evaluation criteria and submission templates
Workshop on technology proposals

## Slide 18
6G Study Items(s) - RAN Plenary
  RAN Plenary (RP) work is split into an ITU-focused SI and General RAN SI
    IMT-2030 discussion is expected in RAN from Sep 2024 to Dec 2024
    RP SI Rel-20 focusing on ITU– IMT-2030: approval Dec 2024 until June 2025
    RP SI Rel-20 focusing on 6G General: approval Mar 2025 (after 6G WS), until June 2026
6G Study Item(s) – RAN WGs
  RAN WGs: 21 months
    RAN WG SI package approval June 2025
    RAN1 SI starts in June 2025 until Mar 2027
    RAN2/3/4 SI start in Sep 2025 until June 2027
Release 20: 6G Study Item (SI)
6G Study Item(s) – TSG SA
  SA SI Approval
    SA1 SI approval: TSG#105 (Sept 2024)
    SA2 SI approval: TSG#108 (Jun 2025)
    Other SA WG (SA3, SA4, SA5, SA6) SI approval: TBD at future TSG meeting
  SA SI completion (18/21 months)
    SA1 6G SI completion: Mar 2026
    SA2 6G SI completion: Dec 2026 or Mar 2027 (To be confirmed at future TSG meeting)
6G Study Item(s) – TSG CT
  CT WGs: at least 9 months
    Discussion on 6G studies will start in Q4 2025 in CT
    CT WG 6G SI is expected to be approved in Mar 2026 (or Dec 2025).

## Slide 19
3GPP Release 20 introduces a unique approach, dividing its focus into two key components: Rel-20_5GA for 5G-Advanced and Rel-20_6G for early 6G studies.
SA1 6G study on use cases and service requirements was approved at TSG SA#105 (SP-241391). The 6G RAN Study (part I: ITU focused) was approved at TSG RAN#106 (RP‑243327)
Technical studies on the 6G radio interface and 6G core network architecture within the RAN and SA Working Group to start in June 2025.
Release 21 will be the official start of normative 6G work and is expected to produce the first formal 6G technical specifications, aligning with IMT-2030 submission requirements.
The Release 21 timeline is expected to be finalized no later than June 2026, with ASN.1/OpenAPI freezes projected no earlier than March 2029.
3GPP is contribution driven and active participation in relevant WGs is necessary to define the scope of 6G studies/work.
Summary of Next Steps Towards 6G

## Slide 20: Thank you!
www.3gpp.org