## Slide 1: [109] R19 NES Paging Enh

## Slide 2: Scope
[AT127][109][NES] (OPPO)
Scope: For each direction (N extension vs PF bundling): 1) List proposed options, 2) Discuss to understand each option better, 3) Down select options, 4) Discuss pros and cons for each direction or down-selected options (with the consideration of UE impacts, system impacts and specification job). F2F offline discussion in Brk3 room.
Intended outcome: Discussion summary in R2-2407598.
Deadline: Comeback in Thursday CB session.

## Slide 3: Q1: Sub-cases for Option-a)
[OPPO] List sub-options for option-a), to check similarity/diff, and see if any chance to down-select
Source | Formula | Comment
Intel, 6471 | (SFN + PF_offset) mod T = G*(UE_ID mod L) | L: the number of consecutive PFs within a PF bundle (i.e., PF bundle size) G: the frame gap between consecutive PFs
Apple, 6671 | (SFN + PF_offset) mod T = (T div N)*(UE_ID SubGroup_ID mod N) | 
Apple, 6671 | (SFN + PF_offset) mod T = (T div N)*(UE_ID Mod N) | 
CATT, 7004 | (SFN + PF_offset) mod T = G*(UE_ID mod N) | G: the frame gap between consecutive PFs.
Vivo, 6243 | (SFN + PF_offset) mod T = SFN [(UE_ID mod N)] | 
Vivo, 6243 | Rel-19 PF = legacy PF +[ (UE_ID mod (N_new/N+factor)) – (factor-1)] | 
Lenovo, 6809 | only one fixed PO is used in a cell specific Paging DRX Cycle | 

## Slide 4: Discussion

## Slide 5: Q2: Pros/Cons for option-a/b
[OPPO] Try to understand each other (performance, impact etc.), no intention to decide now.

## Slide 6: Q2: Pros/Cons for option-a/b
In 38.304
NOTE 1: A PO associated with a PF may start in the PF or after the PF.
NOTE 2: The PDCCH monitoring occasions for a PO can span multiple radio frames. When SearchSpaceId other than 0 is configured for paging-SearchSpace the PDCCH monitoring occasions for a PO can span multiple periods of the paging search space.

## Slide 7: Discussion