## Slide 1: [109] R19 NES Paging Enh

## Slide 2: Scope
[AT127][109][NES] (OPPO)
Scope: For each direction (N extension vs PF bundling): 1) List proposed options, 2) Discuss to understand each option better, 3) Down select options, 4) Discuss pros and cons for each direction or down-selected options (with the consideration of UE impacts, system impacts and specification job). F2F offline discussion in Brk3 room.
Intended outcome: Discussion summary in R2-2407598.
Deadline: Comeback in Thursday CB session.

## Slide 3: Agreement @ 125bis
For adaptation of paging occasions in time domain, RAN2 to study
a) bundle paging frames and
b) extend the values of N to have increased interval between PFs (e.g. T/64, T/128 ...) and compensating decrease in number of PFs by increasing POs per PF.

## Slide 4: Q1: Sub-cases for Option-a)
[OPPO] List sub-options for option-a), to check similarity/diff, and see if any chance to down-select
Source | Formula | Comment
Intel, 6471 | (SFN + PF_offset) mod T = G*(UE_ID mod L) | L: the number of consecutive PFs within a PF bundle (i.e., PF bundle size) G: the frame gap between consecutive PFs
Apple, 6671 | (SFN + PF_offset) mod T = (T div N)*(UE_ID SubGroup_ID mod N) | 
Apple, 6671 | (SFN + PF_offset) mod T = (T div N)*(UE_ID Mod N) | 
CATT, 7004 | (SFN + PF_offset) mod T = G*(UE_ID mod N) | G: the frame gap between consecutive PFs.
Vivo, 6723 | (SFN + PF_offset) mod T = SFN [(UE_ID mod N)] | 
Vivo, 6723 | Rel-19 PF = legacy PF +[ (UE_ID mod (N_new/N+factor)) – (factor-1)] | 
Lenovo, 6809 | only one fixed PO is used in a cell specific Paging DRX Cycle | 

## Slide 5: Discussion
[vivo] Overlapping with legacy? And is it a bundle within R19 PF or with legacy PF? [Apple] indeed there is diff views/def for option-a. our view is it is bundling within R19 PF. Legacy PF relates to the barring scheme. [Samsung] no need to touch legacy PF for now. for R19 PF, anyway there would be some new configuration for both options. Legacy PF is another dimension, and related to network preference on how to handle legacy Ues. [Lenovo] we have a paper with real paging logs, and we proposed a solution merging both options. Agree no need to touch legacy for now. [Nokia] no need to restrict the handling of legacy PF. [NEC] we prefer option-b. [Ericsson] good to understand the diff of the two options first, taking into account of SSB/RACH as well.
=> Option-a) is about the bundling of PF for R19 NES Ues.

## Slide 6: Discussion
[Apple] use intel proposal of the formula as baseline [Nokia] at least it should be possible to configure gap between PFs. [Lenovo, vivo] energy saving comes from consecutive PFs. [CATT] whether we need to change the number of PF within a paging cycle needs to be checked. [Apple] having the gap would be more flexible.
=> For option-a), R2 further discuss whether to allow gaps between bundled PFs

## Slide 7: Q2: Pros/Cons for option-a/b
[OPPO] Try to understand each other (performance, impact etc.), no intention to decide now.

## Slide 8: Q2: Pros/Cons for option-a/b
In 38.304
NOTE 1: A PO associated with a PF may start in the PF or after the PF.
NOTE 2: The PDCCH monitoring occasions for a PO can span multiple radio frames. When SearchSpaceId other than 0 is configured for paging-SearchSpace the PDCCH monitoring occasions for a PO can span multiple periods of the paging search space.

## Slide 9: Discussion
[Samsung] network can configure the PF/PO so that the Pos of the two options are at the same time position. [Ericsson] currently, is the offset of Pos within a same PF the same or can be configured separately [OPPO, Samsung] separately per-PO. [Samsung] two ways: one is to have them consecutively, the other to configure the offset, and the latter one is used to avoid scheduling collision. [Xiaomi] for power saving reason, we should not configure the offset. [Apple] offset configuration is already there, up to network to decide whether to use it or not. [Nokia] the performance diff is also related to other channels (SSB, RACH etc.).
=> R2 observe that the two options can be designed to configure the PO:s at same time position.

## Slide 10: Discussion
[Apple] impact like sync signal (SSB/TRS) and RACH, and scheduling flexibility. [OPPO] what the diff come from if we end up with same PO time position. [Samsung] network configuration can also choose the proper setting [IDCC] is the scheduling restriction mainly about concern of scheduling latency? [OPPO] thought that if we end up with the case where the Pos can be configured sparely as shown, there should not be this concern?