## Slide 1: [Rel-19 NG_RTC_Ph2] Discussion on Enhanced Architecture for Avatar communication
Samsung, []
2024 September

## Slide 2: Summary of discussions in SA2#164
Mainly, three potential architectures were discussed.
  Each architecture has different points in terms of handling ‘Avatar ID List’ and ‘Avatar Representation’ in BAR as following slides.
BAR
DCSF
MF
DCx* (new)
MDC1
MDCx* (new)
* If BAR is co-located in DCAS, DC3/DC4 and MDC2 can be used.
* If BAR is co-located in DCAR, DC5 can be used for control plane (without standardized services), but the media plane between DCAR+BAR has not clarified yet.
[DCSF control based Architecture]
DCAS
BAR
MF
DC6** (new)
DC7** (new)
** Whether to specify DC6/DC7 services or not has not clarified yet. The media plane between BAR and MF has not clarified yet.
** If BAR is co-located in DCAR, the control/media plane between DCAR+BAR and DCAS or MF have not clarified yet.
[DCAS control based Architecture]
DAR
(Digital Asset Repository)
MF
UE
DAR2† (new)
Mb
IMS-AGW
DAR1† (new)
Remote IMS / MF
DAR2† (new)
† DAR1/DAR2 can be used without standardized services.
[Media plane based Architecture]

## Slide 3: Summary of discussions in SA2#164
DCSF control based Architecture
  DCSF retrieves ‘Avatar ID List’ from BAR, and provides it to MF (control plane).
  DCSF interacts with BAR to setup media plane between BAR and the MF.
  DCSF provides information to BAR to allow sending ‘Avatar Representation’ to MF (media plane) when it is requested via established DCs.
  Upon request from MF, BAR provides ‘Avatar Representation’ to MF, and the MF delivers it to the UEs via DCs.
* If BAR is co-located in DCAS, DC3/DC4 and MDC2 can be used.
* If BAR is co-located in DCAR, DC5 can be used for control plane (without standardized services), but the media plane between DCAR+BAR has not clarified yet.
DCSF
BAR
MF
1. Request Avatar ID List (Input: User ID) via DCx(new)
2. Avatar ID List [{Avatar ID#1, config data#1}, {Avatar ID#2, config data#2}, …]
UE
4. Download Avatar ID List via Bootstrap DC
5. Select an Avatar ID
(config data helps displaying thumbnails)
6. Download Avatar Representation (Input: Avatar ID#1)
3. MDCx(new) setup between BAR and MF
(DCSF interacts with BAR, and instructs MF via IMS AS)
Download via MDCx(new)
BAR
DCSF
MF
DCx* (new)
MDC1
MDCx* (new)
IMS AS
HSS/UDM
N72
N71
DC2
DC1
Notes: Based on S2-2407461 (Samsung), S2-2408053 (Vivo), S2-2408194 (ZTE)
BAR+DCAS Collocation (S2-2407461)
BAR+DCAR Collocation (S2-2408053)

## Slide 4: Summary of discussions in SA2#164
DCAS control based Architecture
  DCSF retrieves ‘Avatar ID List’ from HSS/UDM, and provides it to MF (control plane).
  Upon request from MF, DCAS retrieves ‘Avatar Representation’ from BAR (control plane), and the MF delivers it to the UEs via Application DC.
** Whether to specify DC6/DC7 services or not has not clarified yet. The media plane between BAR and MF has not clarified yet.
** If BAR is co-located in DCAR, the control/media plane between DCAR+BAR and DCAS or MF have not clarified yet.
DCAS
BAR
MF
DC6** (new)
DC7** (new)
DCSF
IMS AS
DC2
MDC1
HSS/UDM
N72
N71
MDC3
MDC2
DCSF
BAR
MF
UE
3. Select an Avatar ID
DCAS
1. Retrieve Avatar ID List from HSS/UDM (Input: User ID)
2. Download Avatar ID List via Bootstrap DC
4. Request Avatar Representation (Input: User ID, Avatar ID#1) via Application DC
5. Request via MDC2
(direct request without DCSF involvement is new)
6. Download via DC6(new)
Notes: Based on S2-2408302 (Huawei), S2-2408647 (China Telecom)
BAR+DCAR Collocation (S2-2408302)

## Slide 5: Summary of discussions in SA2#164
Media plane based Architecture
  The Avatar ID to be used in the call is decided by the ‘Scene Description’ provisioned by DCAS through Application DC
  UE/MF directly downloads ‘Avatar Representation’ from DAR.
DCSF
DAR
MF
UE
3. Discover Avatar ID from the Scene Description
DCAS
4. [UE rendering] Request Avatar Representation (Input: Avatar ID#1) via DAR1(new)
† DAR1/DAR2 can be used without standardized services.
DAR
(Digital Asset Repository)
MF
UE
DAR2† (new)
Mb
IMS-AGW
DCAS
DCSF
IMS AS
DC2
HSS/UDM
N72
N71
MDC1
MDC3
DC1
MDC2
DAR1† (new)
2. Provision Scene Description via Application DC
(Scene description data includes Avatar ID(s))
1. Upload Avatar Representation via DAR1(new)
5. [Network rendering] Discover Avatar ID from the Scene Description
(direct operation without DCSF involvement is new)
6. [Network rendering] Request Avatar Representation (Input: Avatar ID#1) via DAR2(new)
Notes: Based on S2-2408071 (Qualcomm)

## Slide 6: Summary of discussions in SA2#164
Summary
Potential Architecture | ‘Avatar ID List’ and ‘Avatar Representation’ handling in BAR | Evaluation
DCSF control based | DCSF gets the ‘Avatar ID List’ from BAR, and transfers it to MF. ‘Avatar ID List’ is composed of Avatar ID and the configuration data which helps displaying the thumbnails of Avatar for user selection DCSF interacts with BAR to setup direct media plane between BAR and MF for Avatar presentation delivery. BAR sends the ‘Avatar Representation’ to MF when the UE requested through Bootstrap DC and/or Application DC. | Avatar ID List and Avatar Representations are managed by BAR. Both static and dynamic storing is possible. Avatar ID List and Avatar Representations are transferred based on control from DCSF. Avatar Representation can be provided via Bootstrap DC and/or Application DC.
DCAS control based | DCSF gets the ‘Avatar ID List’ from HSS/UDM, and transfers it to MF. MF requests ‘Avatar Representation’ to DCAS without DCSF involvement. DCAS gets the ‘Avatar Representation’ from BAR. MF transfers it to the UE through Application DC. | Avatar ID List is managed by HSS/UDM. MF directly request to DCAS without DCSF control. When the DCAS is located in untrusted domain (beyond NEF), the external DCAS retrieves user data from core network (BAR) and delivers it to the core network entity (MF). Avatar Representation can provided only via Application DC.
Media plane based | UE uploads Avatar Representation to DAR. DCAS pushes the ‘Scene Description’ data to MF. MF transfers it to the UE through Application DC. UE discovers ‘Avatar ID’ from ‘Scene Description’, and gets ‘Avatar Representation’ directly from the DAR. In case of network based rendering mode, the MF discovers ‘Avatar ID’ from ‘Scene Description’, and gets ‘Avatar Representation’ directly from the DAR. | Avatar IDs and Avatar Representations are managed by BAR. Both static and dynamic storing is possible. Transmissions of Avatar Representations (upload/download) are performed in SA2 out of scope method.

## Slide 7: Way forward for SA2#165
It is proposed to take architecture as below:
  ‘Avatar ID List’ is stored and managed by HSS/UDM.
  ‘Avatar Representation’ is provided from BAR to UE via MF, based on control from DCSF.
  DCSF interacts with BAR via standardized interfaces by using standardized service operations.
  DCSF interacts with BAR to set up media plane path between the BAR and MF, and to provide information to BAR to allow sending the Avatar Representation to MF when UE/MF request via established DCs.
  Direct interactions ‘between UE and BAR’, or ‘between MF and BAR without DCSF control’ are not specified in SA2.
BAR
DCSF
MF
DCx* (new)
MDC1
MDCx* (new)
IMS AS
HSS/UDM
N72
N71
DC2
DC1
DCSF
BAR
MF
UE
3. Download Avatar ID List via Bootstrap DC
4. Select an Avatar ID
(config data helps displaying thumbnails)
5. Download Avatar Representation (Input: Avatar ID#1)
2. MDCx(new) setup between BAR and MF
(DCSF interacts with BAR, and instructs MF via IMS AS)
Download via MDCx(new)
1. Retrieve Avatar ID List from HSS/UDM (Input: User ID)