## Slide 1: TEI-19 SliceSel Discussion points
KDDI

## Slide 2: Discussion point 1
UDR procedure
  description
    1) The AF sends request to NEF
    2) NEF authorize the AF request and store the application data in the UDR.
    3) The UDR notify the application data to the PCF for the UE, if subscribed to this notifications.
    4) The PCF for the UE may update the URSP rules according to the received application data.
    5) The PCF for the UE may trigger the slice replacement to the AMF.
  Support
  Object

## Slide 3: Discussion point 2
Non supporting UE feature
  description
    The PCF sends an indication whether slice replacement is supported or not for the UE, then the AMF removes the Replaced S-NSSAI from the Allowed NSSAI and includes the Alternative S-NSSAI in the Allowed NSSAI (if not yet present).
  Support
  Object

## Slide 4: Discussion point 3
AF requested indication
  description
    The PCF provide an indication that the slice replacement is due to AF request.
    Nokia proposed it. I would like to know each company’s preferences.
  Support
  Object

## Slide 5: Discussion point 4
Does the SMF register the UDM?(If we support AF indication.)
  Support
  Object

## Slide 6: Proposal overview

## Slide 7: Usecase KDDI assumes
Slice #1
(Default)
RAN
AMF
SMF
PCF
UPF
UE
Replace the default slice to the high priority slice with ticket/time billing
-AF triggers a slice switching to make the user more comfortable with the game app
Slice #2
(eMBB)
RAN
AMF
SMF
PCF
UPF
PDU session
Normal
High
quality
The AF and UE are pre-negotiated, AF is aware of “the S-NSSAI to be replaced”. How to be aware of the S-NSSAI is out of scope of 3GPP.
KDDI assumes an authorized AF on the operator premises.
The AF requests to switch based on ticket/time billing.
Authorized
AF
KDDI premise
The user buys ticket/time billing on operator’s portal site.
KDDI’s portal site/app
Premium
slice ticket