## Slide 1: Comparison of solutions for performance measurement function (PMF) protocol
Significant changes to C1-200313 are marked blue.
Significant changes to C1-202021 are marked green.

## Slide 2: Summary (1)
Alternative solutions for performance measurement function (PMF) protocol
  Ericsson's proposal
    a protocol defined in 3GPP CT1 according to rules specified in TS 24.007
    documented in C1-202621
  Apple's proposal
    a protocol defined in IETF
    documented in C1-202266

## Slide 3: Summary (2)
 | Ericsson's proposal | Apple's proposal
Message size | ✓ at minimum 3 octets | at minimum 44 octets
Extensibility | ✓ can be extended solely in 3GPP, as extensible as NAS protocols | at least interaction with IANA needed, in some cases new IETF RFC needed
Security (if required by SA3) | ✓ can be added solely in 3GPP, based on SA3 requirements, if SA3 specifies any | two separate integrity protection mechanisms, each protecting a part of the message, enabling attacker to modify message content see slide#6, integrity protection of entire PMFP message requires IETF work, confidentiality protection in Ethernet PDU session requires IETF work or a dedicated 3GPP solution
Stateless / stateful protocol | ✓ stateful | 
Use of network-initiated RTT measurement procedure | ✓ optional to use | mandatory to use
Open issues | ✓ comparable | 
Knowledge of the current time | ✓ not required | required

## Slide 4: Detailed comparison of solutions for PMF protocol (1) Message size
Summary:
  Ericsson's proposal is better.
Details:
  Ericsson's proposal: at minimum 3 octets.
  Apple's proposal: at minimum 44 octets.

## Slide 5: Detailed comparison of solutions for PMF protocol (2) Extensibility
Summary:
  Ericsson's proposal is more easily extendable.
Details:
  Ericsson's proposal: as extensible as NAS protocols. No IETF work needed.
  Apple's proposal:
    adding new information element into existing messages requires registration with IANA, with the "First Come First Served" registration policy.
    if a procedure consisting of 3 messages (e.g. a UE sent request, a network sent command, and a UE sent complete) is needed without any additional messages, a new IETF RFC is needed.
    if security features other than:
        partial integrity protection using HMAC field containing output of HMAC-SHA-256 truncated to 128 bits applied on the first 96 octets of the STAMP packet; and
        additional partial integrity protection using HMAC field containing output of HMAC-SHA-256 truncated to 128 bits applied on TLVs of the STAMP packet
      is required, a new IETF work is needed - see slides #5 and #6.

## Slide 6: Detailed comparison of solutions for PMF protocol (3) Security (1)
Summary:
  SA3 has not specified security requirements yet. In Mar 2020 SA3 meeting, there was no consensus whether a new PMF protocol specific security mechanism(s) are needed or the existing security mechanisms are sufficient.
  Given SA3 state, it is difficult to judge what will be needed. Furthermore, new security mechanisms might be forced by inclusion of further IEs in future releases. In general:
    If no new PMF protocol specific security mechanism is required by SA3, no major difference.
    If only a new PMF protocol specific integrity protection is required by SA3:
      if integrity protection of a part of PMF protocol message (i.e. not including the Access Report TLV of the STAMP packet of the Access availability or unavailability report procedure) and additional integrity protection of another part of PMF protocol message (i.e. TLVs including the Access Report TLV of the STAMP packet of the Access availability or unavailability report procedure) is required, no major difference.
        NOTE: The above enables an attacker to modify a content of a PMF-Access-Report message with a content of an PMF-Access-Report message intercepted earlier.
      if integrity protection of entire PMF protocol message is required, Ericsson's proposal is better
      using other mechanism, Ericsson's proposal is better.
    If a new PMF protocol specific confidentiality protection is required by SA3, Ericsson's proposal is better.

## Slide 7: Detailed comparison of solutions for PMF protocol (3) Security (2)
Details:
  If no new PMF protocol specific security mechanism is required by SA3, no major difference.
  if integrity protection of a part of PMF protocol message (i.e. not including the Access Report TLV of the STAMP packet of the Access availability or unavailability report procedure) and additional integrity protection of another part of PMF protocol message (i.e. TLVs including the Access Report TLV of the STAMP packet of the Access availability or unavailability report procedure) is required (as in IETF documents - see NOTE 2 below), no major difference:
    NOTE 1: The above enables an attacker to modify a STAMP packet by replacing TLVs of the STAMP packet with TLVs of an earlier intercepted STAMP packet. E.g. if an attacker intercepts a PMF-Access-Report indicating that non-3GPP access is available, then the attacker can modify any later PMF-Access-Report to indicate that non-3GPP access is available.
    Ericsson's proposal can be extended in 3GPP.
    Apple's proposal supports it.
  If integrity protection of entire PMF protocol message is required by SA3 :
    Ericsson's proposal can be extended in 3GPP (e.g. similarly as in NAS).
    Apple's proposal requires further IETF work (see NOTE 2 below)
  NOTE 2: rfc8762 states "In the Authenticated mode, HMAC covers the first six blocks (96 octets)." and draft-ietf-ippm-stamp-option-tlv-04 adds new TLV fields after the base STAMP packet (i.e. after the first 112 octets) and states "HMAC is calculated as defined in [RFC2104] over text as the concatenation of all preceding TLVs."

## Slide 8: Detailed comparison of solutions for PMF protocol (3) Security (3)
Details:
  If integrity protection of PMF protocol message using other algorithm is required by SA3:
    Ericsson's proposal can be extended in 3GPP (e.g. similarly as in NAS).
    Apple's proposal requires a new IETF RFC.
  If confidentiality protection is required by SA3:
    Ericsson's proposal can be extended in 3GPP (e.g. similarly as in NAS).
    Apple's proposal expects secured transport for the protocol - see rfc8762 section 4.5. Thus, confidentiality protection would either require different solutions for IP based PDU sessions (e.g. IPSec or DTLS based IP solutions) and for Ethernet PDU sessions (solution not clear), or would require a new IETF RFC.

## Slide 9: Detailed comparison of solutions for PMF protocol (4) Stateless / stateful protocol
Summary:
  both solutions are stateful, no major difference.
Details:
  Ericsson's proposal: stateful.
  Apple's proposal: stateful.
    see e.g. C1-200655 subclause 5.3.z.1 last paragraph last sentence or draft-ietf-ippm-stamp-option-tlv-04 section 4.6 3rd paragraph text on retransmission timer.

## Slide 10: Detailed comparison of solutions for PMF protocol (5) Use of network-initiated RTT measurement procedure
Summary:
  Ericsson's proposal is better.
Details:
  Ericsson's proposal: optional use, up to the network implementation.
  Apple's proposal: mandatory use.
    see C1-200655 subclause 5.3.z.2, 1st paragraph.

## Slide 11: Detailed comparison of solutions for PMF protocol (6) Open issues
Summary:
  state of both solution is comparable
Details:
  Ericsson's proposal: size of PTI is left open
  Apple's proposal:
    it is left open how the UE and the UPF obtain the current time, to be indicated in the timestamp field, see slide#10
    it is left open which of the time formats (NTP or PTP) the UE and the UPF use
    it is not specified how the RTT is determined, when several STAMP packets are sent in one RTT measurement procedure
  in both solutions, security is left open as SA3 requirements are not known

## Slide 12: Detailed comparison of solutions for PMF protocol (7) Knowledge of the current time
Summary:
  Ericsson's proposal is better.
Details:
  Ericsson's proposal does not require the UE and the UPF to know the current time. It is enough to measure time difference between sending of a PMF protocol request message and receiving of related PMF protocol response message.
  Apple's proposal requires the UE and the UPF to know the current time as it is indicated in the timestampt field
    rfc8762 states "Timestamp is eight octets long field. STAMP node MUST support Network Time Protocol (NTP) version 4 64-bit timestamp format [RFC5905], the format used in [RFC5357]."
    RFC5357 states "The Session-Sender packet format and content follow the same procedure and guidelines as defined in Section 4.1.2 of OWAMP [RFC4656] (with the exception of the reference to the send schedule)." and "Timestamp and Error Estimate are the Session-Reflector's transmit timestamp and error estimate for the reflected test packet, respectively. The format of all timestamp and error estimate fields follow the definition and formats defined by OWAMP, Section 4.1.2 in [RFC4656]."
    RFC4656 section 4.1.2 states "The format of the timestamp is the same as in [RFC1305] and is as follows: the first 32 bits represent the unsigned integer number of seconds elapsed since 0h on 1 January 1900; the next 32 bits represent the fractional part of a second that has elapsed since then."