## Slide 1: Source: FirstNet Title: Private Call Forwarding Agenda item: x.x Document for: Discussion DRAFT

## Slide 2: Requirements
The MCPTT Service shall provide a mechanism for an MCPTT User to configure forwarding of incoming MCPTT Private Calls (with/without Floor control) to another MCPTT user in the following situations:
  Always (i.e., immediate and CF is configured)
  If the MCPTT User is not reachable (i.e., not logged in and CF is configured)
  If the incoming private call is a call with manual commencement mode and the MCPTT User does not answer within a configured period (i.e., no-answer and CF is configured)
  Based on manual input of the MCPTT User (and CF is authorised)

## Slide 3: Terminology
Forwarded-by-client: The MCPTT client to whom a private call has been placed and who has requested that the private call be forwarded either through settings for immediate call forwarding at its participating MCPTT function or through manual input.
Forwarded-calling-client: The originating MCPTT client who has made a private call attempt that is being forwarded.
Forwarded-to-client: The terminating MCPTT client to whom a private call attempt is being forwarded.

## Slide 4: Databases involved (1/2)
MCPTT user profile:
  Permission to use private call forwarding
  CF no-answer timeout value (how long shall the participating function wait before deciding that there is “no-answer”)
  Conditions allowed for CF
    zero or more of:
      immediate,
      no-answer,
      manual input
  Default static CF target: MCPTT ID or functional alias
    may be overridden by the MCPTT user
    may be unspecified

## Slide 5: Databases involved (2/2)
mcptt-info MIME body (carried within MCPTT signalling)
  This information is created and used within an instance of private call forwarding and as a record of all call forwarding attempts for a private call.
  The MCPTT ID or FA that a private call is being forwarded to in a particular instance of forwarding.
  The list of MCPTT IDs and FAs to which previous call forwarding attempts have been made for this private call. This list includes both URIs and displayable strings (e.g., name – “J Smith”, FA title – “Captain”)
    This list provides both a count of the number of attempted call forwardings and the identity of previous call forwarding targets to allow the MCPTT client/server to avoid a circular list of forwarding targets.
  An indicator to the participating MCPTT function (PF) that a new private call attempt is a call forwarding, to allow the PF to bypass checks of whether the call attempt is allowed to a given target user.
  An indication back to the originating client that the private call is to be forwarded and the new target.
  An indication of the reason for the private call being forwarded (i.e., “immediate”, “no-answer”, “manual input”.
    The originating client can use this information to keep the originating user informed of progress of the private call attempt.

## Slide 6: Originating MCPTT client
Needs to be able to send a SIP message to:
  Initiate a new private call attempt as a result of being informed that the private call should be forwarded.
  Acknowledge a SIP message that a private call should be forwarded.

## Slide 7: Terminating MCPTT client
Needs to be able to send a SIP message to the originating client to:
  Indicate that a private call attempt should be forwarded, including:
    The new target for the private call (MCPTT ID or FA, including displayable string).
      Inclusion of this target MCPTT ID/FA overrides any static private call forwarding target included in the MCPTT user profile.
    The reason for forwarding the private call (“manual input”).
Needs to be able to send a SIP message to its PF to:
  Request that private call forwarding “immediate” be enabled, including:
    The target for private call forwarding (MCPTT ID or FA).
      Inclusion of this target MCPTT ID/FA overrides any static private call forwarding target included in the MCPTT user profile.
    An indication whether private call forwarding should be “immediate” or on “no-answer”.
  Request that private call forwarding be disabled.
  Provide a private call forwarding target. This target will apply to “no-answer”, and will provide a new default target for “immediate” private call forwarding, overriding the user profile.
  Query the status of private call forwarding at the PF.

## Slide 8: Originating participating MCPTT function
Needs to be able to relay a SIP message to the originating client from the terminating MCPTT client to indicate that a private call attempt should be forwarded :
  The PF needs to remember the forwarded-to-client’s MCPTT ID/FA to verify that the subsequent private call attempt that indicates private call forwarding is to the provided forwarded-to-client’s MCPTT ID/FA.
Needs to be able to relay a SIP message from the originating client to the terminating MCPTT client to indicate that a private call attempt forwarding notice was received.
Needs to be able to check a private call attempt from the originating MCPTT client to see if it is a private call forwarding. If so:
  Is the private call forwarding to a remembered forwarded-to-client’s MCPTT ID/FA?
  Have the number of private call forwarding attempts for this private call already reached the limit?
  Is the private call forwarding to an MCPTT ID/FA that has already been attempted?

## Slide 9: Terminating participating MCPTT function
Needs to be able to relay a SIP message to the originating client from the terminating MCPTT client to indicate that a private call attempt should be forwarded.
Needs to be able to relay a SIP message from the originating client to the terminating MCPTT client to indicate that a private call attempt forwarding notice was received.
Needs to be able to receive and reply to a SIP message from its MCPTT client to turn on private call forwarding and to set a new private call forwarding target:
  Is private call forwarding authorized for the MCPTT client?
  Does the request provide a call forwarding target MCPTT ID or FA, or should the default from the user profile be used?
  Is CF to be done for “immediate” or for “no-answer”?
  Needs to be able to receive and reply to a SIP message from its MCPTT client to turn off private call forwarding.
  Needs to be able to receive and reply to a SIP message from its MCPTT client to check the status of immediate private call forwarding.
  If private call forwarding is authorised:
  Needs to be able to time out a private call attempt (“no-answer”) and indicate to the caller the target MCPTT ID/FA to be used.
  Needs to be able to perform immediate private call forwarding