## Slide 1
Encoding Possibilities for PCC related APIs
Thomas Belling
09-11-2017

## Slide 2
Npcf_SMPolicyControl
Service operation name | Description | Initiated by
Npcf_SMPolicyControl_Get | Provides the requested policy to the NF Consumer. | NF consumer (SMF)
Npcf_SMPolicyControl_UpdateNotify | Provides updated policy to the NF Consumer. | PCF
Npcf_SMPolicyControl_Delete | Provides means for the NF Consumer to delete the policy context. | NF consumer (SMF)

## Slide 3
Current encoding Proposal in TR 29.890
Npcf_SMPolicyControl
Resource name | Resource URI | HTTP method | Meaning
SM Policies | {apiRoot}/ npcf_sm_policy_control/ v1/ policies | GET | Read all SM Policies resources at an AS. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given SMF).
Individual SM Subscriber Policy | {apiRoot}/ npcf_sm_policy_control/ v1/ policies/ {supi} | GET | Read the Individual SM Subscriber Policy resources.
 |  | DELETE | Delete the Individual SM Subscriber Policy resource for.
Individual SM PDUSessioPolicy | {apiRoot}/ npcf_sm_policy_control/ v1/ policies/ {supi}/ {sessionID} | PUT (FFS) | Create a new or update an existing Individual SM PDUSession Policy resource.
 |  | PATCH (FFS) | Update an existing Individual SM PDUSession Policy resource.
 |  | GET | Read the Individual SM PDUSession Policy resource.
 |  | DELETE | Delete the Individual SM PDUSession Policy resource.

## Slide 4
Issue: How to enable an effective update of extensive policy information?
Npcf_SMPolicyControl
Stage 2 requires that Policy information can be provided both as response to a GET, and as UpdateNotify request. The information is quite extensive and includes a possibly high number of PCC rules.
Related Issues:
How to achieve maximum communality in the implementation for GET and UpdateNotify?
How to enable an effective update for both cases?
Should we model the policy resource to be located both at PCF and SMF?
Proposal 1 (recommended):
Policies are modeled as resource at the SMF only.
Within the Npcf_SMPolicyControl_Get (HTTP PUT or POST), the SMF provides the root URL for the policy resource.
The PCF does not return policies in the HTTP response to the Npcf_SMPolicyControl_Get. The PCF rather immediately executes an UpateNotify (i.e. sends an HTTP PUT or POST to the designated URL at the SMF), to create or update the policy resource at the SMF (see next slide for resource model and service operations.

## Slide 5
Issue: How to enable an effective update of policy information? (2/2)
Npcf_SMPolicyControl
Proposal 2 (keep current encoding proposal)
Policies are modeled at resource at the PCF only.
Notifications are done in RPC like fashion, providing only deltas
Con: Not fully Restfull.
Con: No efficient encoding for responses to subsequent GET (hardly possible to provide only modifications)
Proposal 3 (policy resources at PCF only. Notifications only as triggers for new Get)
Policies are modeled at resource at the PCF only.
Notifications are done in RPC like fashion, providing only triggers for new Get
Con: No efficient encoding for responses to subsequent GET (hardly possible to provide only modifications)

## Slide 6
Npcf_SMPolicyControl
Proposed subscription resources at the PCF
Resource name | Resource URI | HTTP method | Meaning
SM Policie Subscriptions | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions | GET | Read all SM Policies resources at an AS. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given SMF).
Individual SM Subscriber Policy Subscription | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions/ {supi} | GET | Read the Individual SM Subscriber Policy resources.
 |  | DELETE | Delete the Individual SM Subscriber Policy resource for.
Individual SM PDUSessioPolicy Subscription | {apiRoot}/ npcf-sm-policy-control/ v1/ policy_subscriptions/ {supi}/ {sessionID} | PUT | Create a new or update an existing Individual SM PDUSession Policy resource for a SUPI and sessionID supplied by the SMF. If an Individual SM Subscriber Policy Resource for the SUPI does not yet exist, it is also created.
 |  | PATCH | Update an existing Individual SM PDUSession Policy resource.
 |  | GET | Read the Individual SM PDUSession Policy resource.
 |  | DELETE | Delete the Individual SM PDUSession Policy resource.

## Slide 7
Proposed Policy resources at the SMF
Npcf_SMPolicyControl
Resource name | URI | HTTP method | Meaning
SM Policies | {notificationURI}/ policy | PUT | Install new policies or replace existing SM policies at the service consumer
 |  | PATCH | update existing SM policies at the service consumer
 |  | GET | Read existing SM policies
 |  | DELETE | Delete existing SM policies at the service consumer and request termination of corresponding PDU session
PCC Rules | {notificationURI}/ policy/ pcc-rules | PUT | Install new PCC Rules or replace existing PCC Rules at the service consumer
 |  | PATCH | update existing PCC rules at the service consumer
 |  | GET | Read existing PCC rules
 |  | DELETE | Delete existing PCC rules at the service consumer
Individual PCC Rule | {notificationURI}/ policy/ pcc-rules/ {PCCruleId} | PUT | Install new PCC rule or replace existing PCC rule at the service consumer
 |  | PATCH | update existing PCC rule at the service consumer
 |  | GET | Read existing PCC rule
 |  | DELETE | Delete existing PCC rule at the service consumer

## Slide 8
Npcf_AMPolicyControl
Service operation name | Description | Initiated by
Npcf_AMPolicyControl_Get | Provides the requested policy to the NF Consumer. | NF consumer (AMF)
Npcf_AMPolicyControl_UpdateNotify | Provides updated policy to the NF Consumer. | PCF
Npcf_AMPolicyControl_Delete | Provides means for the NF Consumer to delete the policy context. | NF consumer (AMF)

## Slide 9
Current encoding Proposal in TR 29.890
Npcf_AMPolicyControl
Resource name | Resource URI | HTTP method | Meaning
AM Policies | {apiRoot}/ npcf_am_policy_control/ v1/policies/ | GET | Read all AM Policies resources at an PCF.
Individual AM Policy | {apiRoot} /npcf_am_policy_control/ v1/policies/ {supi} | PUT | Create a new or update an existing Individual AM Policy resource for a SUPI supplied by the AMF.
 |  | PATCH (FFS) | Update an existing Individual AM Policy resource for a SUPI supplied by the AMF.
 |  | GET | Read the Individual AM Policy resource for a SUPI supplied by the AMF.
 |  | DELETE | Delete the Individual AM Policy resource for a SUPI supplied by the AMF.

## Slide 10
Issue: How to enable an effective update of policy information? (1/2)
Npcf_AMPolicyControl
Stage 2 requires that Policy information can be provided both as response to a GET, and as UpdateNotify request. The information is less extensive than for SMF policies. There seem also requirements that the AMFa provides Service Area Restrictions, and/or an RAT Frequency Selection Priority (RFSP) Index (tbc by SA2 experts)
Related Issues:
How to achieve maximum communality in the implementation for GET and UpdateNotify?
How to enable an effective update for both cases?
Should we model the policy resource to be located both at PCF and SMF?
How to handle modification of Service Area Restrictions and RFSP index?
Proposal 1 (similar to SMF service)
Policies are modeled at resource at the AMF only.
Within the GET, the AMF provides the root URL for the resource.
The AMF does not return policies in the HTTP response to a GET. The SMF rather immediately executes an UpateNotify to create or update the policy resource at the SMF (see next slide for resource model and service operations.
Con: Requirement 4 is not addressed well, resources to describe Service Area Restrictions and RFSP index seem still required at AMF

## Slide 11
Issue: How to enable an effective update of policy information? (2/2)
Npcf_AMPolicyControl
Proposal 1b (similar to SMF service) recommended !!!
Policies are modeled at resource at the AMF only.
Within the Npcf_AMPolicyControl_Get (HTTP PUT or POST), the AMF provides the root URL for the resource.
The Service Area Restrictions, and/or an RAT Frequency Selection Priority (RFSP) Index do already exist at the AMF at that point. The AMF may include a representation in the GET. Alternatively the PCF uses an HTTP GET to read out the existing resource.
The AMF does not return policies in the HTTP response to the Npcf_AMPolicyControl_Get. The SMF rather immediately executes an UpateNotify (i.e. sends to the designated URL an HTTP PUT, PATCH to update the existing resources at the SMF or a POST to create new policy resource at the SMF.
For the policy resource structure at the SMF, see subsequent slide
Addresses Requirement 4 but avoids that resources to describe Service Area Restrictions and RFSP index are required at the PCF

## Slide 12
Issue: How to enable an effective update of policy information? (2/2)
Npcf_AMPolicyControl
Proposal 2 (keep current encoding proposal)
Policies are modeled at resource at the PCF only.
Notifications are done in RPC like fashion, providing only deltas
Pro: Requirement 4 addressed well
Con: Not fully Restfull.
Con: No efficient encoding for responses to subsequent GET (hardly possible to provide only modifications)
Proposal 3 (policy resources at PCF only. Notifications only as triggers for new Get)
Policies are modeled at resource at the PCF only.
Notifications are done in RPC like fashion, providing only triggers for new Get
Pro: Requirement 4 addressed well
Con: No efficient encoding for responses to subsequent GET (hardly possible to provide only modifications)

## Slide 13
Npcf_AMPolicyControl
Proposed subscription resources at the PCF
Resource name | Resource URI | HTTP method | Meaning
AM Policies | {apiRoot}/ npcf-am-policy-control/ v1/subscriptions/ | GET | Read all AM Policies resources at an PCF. Query parameters are FFS and can contain the NotificationURI (to identify all resources related to a given AMF).
Individual AM Policy Subscription | {apiRoot} /npcf-am-policy-control/ v1/subscriptions/ {supi} | PUT | Create a new or update an existing Individual AM Policy resource for a SUPI supplied by the AMF.
 |  | PATCH (FFS) | Update an existing Individual AM Policy resource for a SUPI supplied by the AMF.
 |  | GET | Read the Individual AM Policy resource for a SUPI supplied by the AMF.
 |  | DELETE | Delete the Individual AM Policy resource for a SUPI supplied by the AMF.

## Slide 14
Proposed Policy resources at the AMF
Npcf_SMPolicyControl
Resource name | URI | HTTP method | Meaning
AM Policy | {notificationURI}/ policy | PUT | Install new AM policy or replace existing AM policy at the service consumer
 |  | PATCH | update existing AM policiy at the service consumer
 |  | GET | Read existing AM policy
 |  | DELETE | Delete existing AM policyat the service consumer
UE Policy | {notificationURI}/ policy/ ue-policy | PUT | Install new UE policy or replace existing UE policy at the service consumer
 |  | PATCH | update existing UE policy at the service consumer
 |  | GET | Read existing UE policy
 |  | DELETE | Delete existing UE policyat the service consumer
URSP Rules | {notificationURI}/ policy/ ue-policy/ ursp-rules | PUT | Install new URSP Rules or replace existing URSP Rules at the service consumer
 |  | PATCH | update existing URSP rules at the service consumer
 |  | GET | Read existing URSP rules
 |  | DELETE | Delete existing URSP rules at the service consumer
Individual URSP Rule | {notificationURI}/ policy/ ue-policy/ ursp-rules/ {urspRuleId} | PUT | Install new URSP rule or replace existing URSP rule at the service consumer
 |  | PATCH | update existing URSP rule at the service consumer
 |  | GET | Read existing URSP rule
 |  | DELETE | Delete existing URSP rule at the service consumer
AMF Access and Mobility ManagementControl Policy | {notificationURI}/ amf-policy | PUT | Install new or replace existing AMF Access and Mobility ManagementControl Policy at the service consumer
 |  | PATCH | update existing AMF Access and Mobility ManagementControl Policy at the service consumer
 |  | GET | Read existing AMF Access and Mobility ManagementControl Policy
 |  | DELETE | Delete existing AMF Access and Mobility ManagementControl Policy at the service consumer

## Slide 15
Npcf_PolicyAuthorization service
Service Operation Name | Description | Initiated by
Npcf_PolicyAuthorization_Create | Determines and installs the policy according to the service information provided by an authorized NF service consumer. | AF, NEF
Npcf_PolicyAuthorization_Update | Determines and updates the policy according to the modified service information provided by an authorized NF service consumer | AF, NEF
Npcf_PolicyAuthorization_Delete | Provides means to delete the application session context of the NF service consumer | AF, NEF
Npcf_PolicyAuthorization_Notify | Notifies NF service consumer of the subscribed events | PCF
Npcf_PolicyAuthorization_Subscribe | Allows NF service consumers to subscribe to the notification of events | AF, NEF
Npcf_PolicyAuthorization_Unsubscribe | Allows NF service consumers to unsubscribe to the notification of events | AF, NEF

## Slide 16
Issue: Are event exposure and service information provisioning related?
Npcf_PolicyAuthorization service
Related considerations:
Desire to be able to use only event exposure or only service information provisioning, or both in combination.
Some events may be related to an application (e.g. start and stop of application traffic)
Stage indicates that Subscribe depends on Create, but service information within Create is optional
Procedures: | Input (required) | Input (optional)
Npcf_PolicyAuthorization_Create | IP address of the UE, application session context identifier | SUPI if available, DNN if available, Media type, Media format, bandwidth requirements, sponsored data connectivity if applicable, flow description, AF application identifier, AF Communication Service Identifier, AF Record Identifier, Flow status, Priority indicator, emergency indicator, Application service provider, resource allocation outcome
Npcf_PolicyAuthorization_Subscribe | List of events, application session context identifier, Notification URI | none