## Slide 1
The access from 5GS to the MC service environment takes place via the Data Network (DN) in accordance with 3GPP TS 23.501 [7]. A Data Network Name (DNN) as part of the 5GS user profile allows access to the Data Network with up to 8 connectivity sessions (PDU sessions) each with up to 64 communication flows (QoS flows). Different data networks require different DNNs.
4.2.2 Requirements
For MC service UEs who only utilize 5GS, a single DNN may be used for:
- for the SIP-1 reference point;
- for the HTTP-1 reference point; and
- for the CSC-1 reference point.
The DNN shall be made available to the MC service UE either via UE (pre)configuration or via initial UE configuration on a per HPLMN and optionally also per VPLMN basis. {DNNs should be organized per PLMN}
NOTE 1: The Data Network access can also be shared with the "IMS" access taking into account the communication flow limits.
The MC service UE may exploit secondary authentication/authorization by a DN-AAA server during the establishment of session connectivity as specified in 3GPP TS 23.501 [7] using the Extensible Authentication Protocol (EAP) to access the DN identified by the MC service DNN. If required, DN access credentials shall be made available to the MC service UE via initial MC service UE configuration on a per DNN basis.
The DN connection to the DNN defined within the present subclause can be of PDU session type "IPv4", "IPv6", "IPv4v6", Ethernet or Unstructured (see 3GPP TS 23.501 [7]). If a DN connection to an DNN defined within the present subclause is of type "IPv4v6" then the MC service client shall use configuration data to determine whether to use IPv4 or IPv6.
…
For MC service UEs who utilize EPS and 5GS 3GPP TS 23.280 [3] clause 5.2.7 applies.
A.2 Initial MC service UE configuration data
The configuration data defined in 3GPP TS 23.280 [3] in Annex A.6 apply, with the following exceptions:
- DNN and the corresponding DN credentials instead of the PDN credentials shall be used;
- Network slice identification and corresponding network slice credentials may be provided per MC service.
Support of DN and SNSSAI
Stage-2 requirements
Table A.6-1: Initial MC service UE configuration data (on-network)

## Slide 2
References to DN-info
C1-221693
A) PDN connectivity information
Reuses existing H/VPLMN structure
Reuses MC*-con-ref for APN/DNN references(1-3),
  extended with MC*-con-ref-SNSSAI per service.
All info related to a DN in a new separate element DN-Info. The APN/DN Name is the reference.
B) Application plane server identity information
Keeps only information related to Application plane service in <MC*-Service-Details>
PDU_session_type could also be placed here
Mapping stage-2 to stage-3 alternatives
Stage-2 structure
Table A.6-1: Initial MC service UE configuration data (on-network)
A)PDN connectivity information
HPLMN ID and optionally VPLMN ID to which the data pertains
> MC services PDN
  >> APN
  >> PDN access credentials
> MC common core services PDN
  >> APN
  >> PDN access credentials
> MC identity management service PDN
  >> APN
  >> PDN access credentials
B) Application plane server identity information
> Identity management server
  >> Server URI
> Configuration management server
  >> Server URI
> Key management server
  >> Server URI (also known as KMSUri for security domain managed by KMS)
> Indication of whether the UE shall use IPv4 or IPv6 for on-network MCPTT
> MCPTT Server
  >> Server URI
> Indication of whether the UE shall use IPv4 or IPv6 for on-network MCData
> MCData Server
  >> Server URI
> Indication of whether the UE shall use IPv4 or IPv6 for on-network MCVideo
> MCVideo Server
  >> Server URI
> Location management server
  >> Server URI
Per service/PLMN details
C1-221239
A)PDN connectivity information
The existing con-ref to be deprecated. If present, they should be match the service details
All info moved to <MC*-Service-Details>
VPLMNs info to be also moved under <MC*-Service-Details> (essentially deprecating the whole <HPLMN> element
B) Application plane server identity information
Expand each <MC*-Service-Details> with List of <VPLMN-MCPTT-Service-Details> one entry per PLMN
All info under a DN-info element for each PLMN/Service.
Even if the same DN-info is to be used, the info has to be replicated per PLMN/service

## Slide 3
1)AnyExt assumed always to exist vs NBC solution Rel-17 Vs new parallel structure per PLMN
2) Resolution of potential conflict of existing IPV6required with new PDU session Type
Open Issues