## Slide 1: Draft for discussion on SLAC representation
ID_UAS rapporteur

## Slide 2: Current coding of SLAC
Service-level-AA container IE
Service-level-AA device ID
Service-level-AA server address
Service-level-AA response
Service-level-AA payload type
Service-level-AA pending indication
Service-level-AA payload
UUAA payload
C2 authorization payload
“UUAA payload”
“C2 authorization payload”
UAV-C pairing info
Flight auth info
C2 auth result
C2 session security info

## Slide 3: Proposed coding of SLAC in C1-221627
Service-level-AA container IE
Service-level-AA device ID
Service-level-AA server address
Service-level-AA response
Service-level-AA payload type
Service-level-AA pending indication
Service-level-AA payload
Change part in RED
UUAA payload
C2 authorization payload
“UUAA payload”
“C2 authorization payload”
C2 aviation payload
C2 auth result
C2 aviation payload will include
- UAV-C pairing info,
- Flight auth info,
- C2 session security info
which are transparent to NAS

## Slide 4: Proposed coding of SLAC in C1-221248
Service-level-AA container IE
Service-level-AA device ID
Service-level-AA server address
Service-level-AA response
Service-level-AA payload type
Service-level-AA pending indication
Service-level-AA payload
UUAA payload
C2 authorization payload
“UUAA payload”
“C2 authorization payload”
C2 aviation payload(UL)
Change part in BLUE
C2 authorization payload(DL)
UUAA aviation payload(UL)
UUAA authorization payload(DL)
C2 aviation payload will include
- UAV-C pairing info,
- Flight auth info,
- C2 authorization info
which are transparent to NAS
C2 authorization parameter will include
- UAV-C IP address
- C2 authorization result
- C2 session security info
which are transparent to NAS
Or C2 communication payload
Not visible to NAS
Not visible to NAS
Not visible to NAS
Not visible to NAS

## Slide 5: Distinction
C1-221627
1. C2 aviation payload can carry UAV-C pairing info, Flight auth info, and C2 session security info, which are transparent to NAS. (it should be clarified that those are included in the payload as a NOTE)
2. Keep others as it is
C1-221248
1. Change name of C2 authorization payload of the service-level-AA payload to either “C2 payload” or “C2 communication payload”
2. UUAA payload and C2 payload are only visible to NAS
3. Mentioning a NOTE to clarify payload name used in SA2 spec regarding UL direction and DL direction
4. UAV-C pairing info, Flight auth info, and C2 session security info, and C2 authorization result are carried in C2 payload