## Slide 1: GCF-PTCRB UICC test solutions for devices with non-removable (e)UICCs/iSIMs
Qualcomm, Apple, and Comprion
Meeting: CT6#109-bis-e C6-220048
Jan 18th 2022 – Jan 21st 2022

## Slide 2
Background
Proposed nrUICC Device Test Methods
Implicit verification-based Test Method
Test Toolkit Event based Test Method
Seamless interface testing based on BB APDU Logging
Requirements for nrUICC Device Test Methods
Pros and Cons of proposed Test Methods
Test Method Applicability table
Possible GCF-CC Annex F6.1 update for each Test Method
Content

## Slide 3
Background
Test cases defined in 3GPP TS 31.121 and TS 31.124 imply unrestricted access to the UICC-terminal interface.
  So, todays test systems mostly use UICC simulators and rely on direct tracing of APDUs sent via the UICC-terminal interface.
  This approach is not feasible for devices operated with a non-removable (e)UICC/iSIM*.
  UICC-Terminal interface conformance requirements for nrUICC devices cannot be verified in a way accepted and certifiable by GCF and PTCRB.
3GPP CT6 shall currently develop new specifications to facilitate testing of nrUICC devices.
  Currently three different verification methods are proposed.
  Each method comes with its own benefits and all three methods may be required to cover all use cases and nrUICC types.
* non-removable (e)UICC/iSIM: nrUICC

## Slide 4
Proposed nrUICC Device Test Methods
  Test Toolkit Event based test method,
  Implicit verification-based test method,
  Seamless eSIM/iSIM testing based on baseband APDU logging.
Each proposed test method uses a different approach to verify the conformance requirements given (mostly inherited from 3GPP TS 31.121 and 3GPP TS 31.124).
Test cases defined for the new specifications will use the Implicit verification method wherever possible to support at least minimal testing for devices/eUICC/iSIMs.
Test Toolkit Event based testing and/or Seamless eSIM/iSIM testing allow directly verifying content and format of APDUs.

## Slide 5: Implicit verification-based Test Method
Test System updates certain EFs at TC start/run time with unpredictable random data with message content verification on the NW Simulator. This is considered as an indirect indication for successful and compliant data exchange between card and terminal, but might require extensive test procedures.
The verification of EF content updates is used at the end of the test execution where required
Exact APDU communication in the SIM-ME interface is not verified.
Standard Toolkit Events used by Test Toolkit Applets for USAT testing similar to TS 31.124. Few Terminal Responses and direct EF reading cannot be verified by applets
GCF/PTCRB Test Platform
Std. Toolkit Events
DUT
Baseband
UICC interface
nrUICC
U
S
B
UICC/Terminal Interface Tester
Configuration Commands
Test Toolkit Applet
NW Simulator
Card OS/
Runtime Env.
Std. Toolkit Events
UICC Interface
Command Interface
Test Application
U
S
B
Command Interface
eSIM Lines

## Slide 6: Test Toolkit Event based Test Method
Unlike with eSIM or removable SIM solutions, integrated SIM solutions (iSIM) includes additional Software layers and processors between the Baseband and iSIM.
Hence this test method allows verification of APDU content at the non-removable SIM it is suitable for the devices with integrated SIM (iSIM) and it can be used for all others as well.
For TS 31.121/31.127 and REFRESH TCs in 31.124/31.117 Card OS (eg: Test Card OS) is required to support two new Test Toolkit Events for APDU content verification using a Test Toolkit Applet.
Standard Toolkit Events and handlers in the Test Toolkit Applet can be used for 31.124/ 31.117 testing except for the file read verification for REFRESH TCs.
This Test method can be used for all devices/nrUICCs with Toolkit capabilities if supported by the iSIM/(e)UICC.
GCF/PTCRB Test Platform
Std. Toolkit Events
DUT
Baseband
UICC interface
nrUICC (iSIM)
U
S
B
UICC/Terminal Interface Tester
Configuration Commands
Test Toolkit Applet
NW Simulator
Card OS/
Runtime Env.
Std. Toolkit Events
UICC Interface
Command Interface
Test Application
U
S
B
Command Interface
SW Interface for iSIM

## Slide 7: Seamless interface testing based on BB APDU Logging
APDU Communication in SIM-ME interface is verified through Baseband logging
The Device is required to provide a logging interface to the test system to allow monitoring and verification.
A Command handler in the Baseband handles APDU logging and nrUICC commands.
Standard Toolkit Events and handlers can be used in Test Toolkit Applets for 31.117 (USAT) testing.
Direct verification of all Terminal Responses and EF reading possible at Baseband for devices with eSIM as the complete APDU traffic logging is available to the test system. However, for devices with iSIM the SW interface between BB and the iSIM is not verified.
GCF/PTCRB Test Platform
Std. Toolkit Events
DUT
Baseband
UICC interface
nrUICC
U
S
B
UICC/Terminal Interface Tester
APDU Logging
Configuration
Commands
Test Toolkit Applet
NW Simulator
Card OS/
Runtime Env.
Std. Toolkit Events
UICC Interface
Command Interface/Handler APDU logging
Test Application
U
S
B
Logging/Command Interface
eSIM Lines

## Slide 8: Requirements for nrUICC Device Test Methods
Requirements for all test methods:
  A means to verify acceptance criteria for content and format of APDU communication on the SIM-ME interface
  An interface for sending commands to the non-removable SIMs, e.g. AT+CSIM for updating EFs
  A test profile with known credentials, e.g. OTA keys, required functionality, e.g. test algorithm, etc., must be installable and usable in the (e)UICC/iSIM. Provisioning via RSP or pre-installed by the device vendor.
  The test profile can be e.g. the GSMA TS.48 or directly a USIM/USAT test profile with the required config.
  4. Test Toolkit Applet is required for USAT tests.
  5. Extended APDU logging capabilities from Baseband for displaying APDU communication during testing.
Conditional requirements:
  The Test Toolkit Applet shall be enhanced for USIM tests when using Test Events
  Use APDU log packets from Baseband to validate APDUs for Seamless Testing.
  Defined test cases might require a combination of different test methods
Each proposed Test method uses a different approach to verify the content and format of APDUs. Depending on the chosen method some verifications or tests may not be executable.
Without agreement on the test methods and related feature support in the device/(e)UICC/iSIM, device certification might need to be performed with different test quality levels and different test coverage

## Slide 9: Pros and Cons of proposed Test Methods
Test Method | Test method details | Pros | Cons
Test Toolkit Events-based Test Method | Test toolkit Applet registers for two new Test Toolkit Events. Upon receiving the Test Events, APDUs required for the Acceptance criteria are saved in the output data Test EF. Test verdict depends on the NW simulator verdict and the data retrieved from the iSIM. Test toolkit Applet is required for USIM and USAT tests AT or MMI commands are used for updating input data Test EF for test initial conditions and Toolkit Events registrations. | Can verify SW interface between BaseBand and integrated-SIM. No change is required for tests defined in TS 31.121. | Support of toolkit and the new events in the Test Card OS is required in the non-removable SIM. Terminal Responses for SETUP EVENT LIST cannot be verified for 31.124/31.117. (Note: This can be eliminated if the TERMINAL RESPONSE for this command is verified using APDU logging at Baseband.)
Implicit APDU verification-based Test Method | Based on end-to-end testing where dedicated, but for unpredictability randomly altered, data is updated in the non-removable UICC (e.g.: IMSI will be 24608135793579x and the last digit x will be a random digit between 0 – 9 updated during the TC execution). Verification of OTA signaling messages on the network simulator is considered as an indirect indication for successful and compliant data exchange between card and terminal. Test toolkit Applet is required for SIM Toolkit Tests. AT or MMI commands can be used for updating Test EFs for test initial conditions and for verification of EF content when finishing the test procedure | This method can be used for all devices/eSIMs, also those not supporting SIM Toolkit. No Test card OS change is required. Only needs to support test profile installation, and profile updates | APDU Communication in SIM-ME interface is not verified explicitly Modification to the test specification is required for USIM tests similar to 31.121. Some of the current conformance requirements in 31.121 and 31.124 cannot be verified. Terminal Responses for SETUP EVENT LIST cannot be verified for 31.124/31.117. (Note: This can be eliminated if the TERMINAL RESPONSE for this command is verified using APDU logging at Baseband.)
Seamless eSIM/iSIM testing based on BB APDU Logging | APDU Communication in SIM-ME interface is verified through Baseband logging Device shall provide a logging interface to the test system for monitoring APDU communication in the ME-SIM interface. Test toolkit Applet is required for SIM Toolkit Test. AT or MMI commands can be used for updating Test EFs for test initial conditions. | This method can be used for all devices/eSIMs, also those not supporting SIM Toolkit (USIM testing is applicable, but USAT testing not applicable if toolkit is not supported by the device). | The ME has to provide a specific command handler that accesses and logs the data transfer between baseband and non-removable SIM and provides this to the test system. SW interface between Base band- iSIM can’t be tested in case of iSIM is in the device.

## Slide 10: Test Method Applicability table
Non-removable SIM Type | Test requirement for the DUT | Examples of Test Packages or device types | Applicable Test Method |  |  | 
 |  |  | Test Toolkit Event based Test Method | Implicit APDU verification-based Test Method | Seamless eSIM/iSIM testing based on BB APDU Logging | SIM Simulator based verification using a physical adaptor (for some Test samples only)
eSIM | UICC tests for a Consumer Device with eSIM | 3GPP 31.127 and 31.117 | ✓ | ✓ | ✓ | ✓
 | UICC Electrical testing for a Test sample with eSIM | ETSI 102 230 for eSIM | NA | NA | NA | ✓
 | UICC tests for a Device with eSIM without Toolkit capability | IoT devices (3GPP 31.127) | NA | ✓ | ✓ | ✓
iSIM | UICC tests for a Consumer Device with iSIM | 3GPP 31.127 and 31.117 | ✓ | ✓ | ✓ | NA
 | UICC tests for a Device with iSIM without Toolkit capability | IoT devices (3GPP 31.127) | NA | ✓ | ✓ | NA
Any | Non-UICC tests for a Device with any NSR SIM | RAN5 test suites (eg: 3GPP 38.521) | NR | ✓ | NR | NR
Test Environment/Method Applicability will be defined in the new test specifications TS 31.127 (USIM for nrDevices) and TS 31.117 (USAT for nrDevices).
it will be up to Carriers, OEMs, and Chipset vendors to choose the best test solution depending on the type of non-removable SIM being used in the device and the level of verification needed.
NA - Not Applicable/Available
NR - Not Required

## Slide 11: Possible GCF-CC Annex F6.1 update for each Test Method
UICC Conformance Test Method | Possible GCF-CC Annex F6.1 update
Test Toolkit Events-based Test Method | If TERMINAL RESPONSE for SETUP EVENT LIST proactive command is not verified : TERMINAL RESPONSE for SETUP EVENT LIST proactive command is not verified and that the event is supported by the device is validated at the test step receiving the ENVELOPE command from the Terminal. Implicit assumption in case of received Event: Terminal Response indicated "Command performed successfully". If TERMINAL RESPONSE for SETUP EVENT LIST proactive command is verified using APDU logging : Above comment is not required since TERMINAL RESPONSE for SETUP EVENT LIST proactive command is verified at Baseband and it is also implicitly validated by the Test Applet at the test step receiving the ENVELOP command from the Terminal.
Implicit APDU verification-based Test Method | Content and format of non-toolkit APDUs is not verified, and it is implicitly verified by verifying the OTA messages at the NW simulator. If TERMINAL RESPONSE for SETUP EVENT LIST proactive command is not verified : TERMINAL RESPONSE for SETUP EVENT LIST proactive command is not verified and that the event is supported by the device is validated at the test step receiving the ENVELOPE command from the Terminal. Implicit assumption in case of received Event: Terminal Response indicated "command performed successfully". If TERMINAL RESPONSE for SETUP EVENT LIST proactive command is verified using APDU logging : Above comment is not required since TERMINAL RESPONSE for SETUP EVENT LIST proactive command is verified at Baseband and it is also implicitly validated by the Test Applet at the test step receiving the ENVELOP command from the Terminal. Verification that the device has read all EFs which shall be read due to REFRESH commands will not be performed as it results in extremely long and complex tests
Seamless eSIM/iSIM testing based on BB APDU Logging | For devices with integrated-SIM: APDU content and format is verified using the logging provided by the Baseband and does not verify the SW interface between Baseband – iSIM.

## Slide 12: Thank you !