3GPP TS 51.010-4 V13.3.0 (2017-09)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Core Network and Terminals;

Mobile Station (MS) conformance specification;

Part 4: Subscriber Identity Module (SIM)

application toolkit conformance test specification

(Release 13)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

GSM, SIM, testing

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2017, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC).

All rights reserved.

UMTS™ is a Trade Mark of ETSI registered for the benefit of its members

3GPP™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners
LTE™ is a Trade Mark of ETSI currently being registered for the benefit of its Members and of the 3GPP Organizational Partners

GSM® and the GSM logo are registered and owned by the GSM Association

Contents

1	Scope	9

2	References	9

3	Definitions and abbreviations	11

3.1	Mobile station definition and configurations	11

3.2	Applicability	11

3.2.1	Applicability of the present document	11

3.2.2	Applicability of the individual tests	11

3.2.3	Applicability to terminal equipment	11

3.2.4	Definitions	11

3.2.4.1	Format of the table of optional features	11

3.2.4.2	Format of the applicability table	12

3.2.4.3	Status and notations	12

3.3	Table of optional features	13

3.4	Applicability table	18

3.5	Conventions for mathematical notations	54

3.6	Conventions on electrical terms	54

3.7	Terms on test conditions	54

4	Test equipment	54

5	Testing methodology in general	54

5.1	Testing of optional functions and procedures	54

5.2	Test interfaces and facilities	54

5.3	Different protocol layers	54

5.4	Information to be provided by the apparatus supplier	54

5.5	Definitions of transmit and receive times	55

6	Reference test methods	55

7	Implicit testing	55

8	Measurement uncertainty	55

9	Format of tests	55

10	Generic call set up procedures	58

11 - 26 	Not used	58

27	Testing of the SIM/ME interface	58

27.1 - 27.21	Void	58

27.22	SIM Application Toolkit	58

27.22.1A 	General Test purpose	58

27.22.2A 	Definition of default values for SIM Application Toolkit testing	59

27.22.1	Initialization of SIM Application Toolkit Enabled SIM by SIM Application Toolkit Enabled ME (Profile Download)	65

27.22.1.1	Definition and applicability	65

27.22.1.2	Conformance requirement	65

27.22.1.3	Test purpose	65

27.22.1.4	Method of test	65

27.22.1.4.1	Initial conditions	65

27.22.1.4.2	Procedure	66

27.22.1.5	Test requirement	67

27.22.2	Contents of the TERMINAL PROFILE command	67

27.22.2.1	Definition and applicability	67

27.22.2.2	Conformance requirement	67

27.22.2.3	Test purpose	68

27.22.2.4	Method of test	68

27.22.2.4.1	Initial conditions	68

27.22.2.4.2	Procedure	68

27.22.2.5	Test requirement	68

27.22.3	Servicing of proactive SIM commands	68

27.22.3.1	Definition and applicability	68

27.22.3.2	Conformance requirement	68

27.22.3.3	Test purpose	68

27.22.3.4	Method of test	69

27.22.3.4.1	Initial conditions	69

27.22.3.4.2	Procedure	69

27.22.3.5	Test requirement	69

27.22.4	Proactive SIM commands	69

27.22.4.1	DISPLAY TEXT	69

27.22.4.1.1	DISPLAY TEXT (Normal)	69

27.22.4.1.2	DISPLAY TEXT (Support of "No response from user")	78

27.22.4.1.3	DISPLAY TEXT (Display of extension text)	79

27.22.4.1.4	DISPLAY TEXT (Sustained text)	81

27.22.4.1.5	DISPLAY TEXT (Display of icons)	85

27.22.4.1.6	DISPLAY TEXT (UCS2 display supported)	90

27.22.4.2	GET INKEY	92

27.22.4.2.1	GET INKEY(normal)	92

27.22.4.2.2	GET INKEY (No response from User)	98

27.22.4.2.3	GET INKEY (UCS2 format display)	100

27.22.4.2.4	GET INKEY (UCS2 format of entry)	102

27.22.4.2.5	GET INKEY ("Yes/No" Response)	104

27.22.4.2.6	GET INKEY (display of Icon)	106

27.22.4.2.7	GET INKEY (Help Information)	113

27.22.4.3	GET INPUT	116

27.22.4.3.1	GET INPUT (normal)	116

27.22.4.3.2	GET INPUT (No response from User)	128

27.22.4.3.3	GET INPUT (UCS2 format display)	130

27.22.4.3.4	GET INPUT (UCS2 format of entry)	133

27.22.4.3.5	GET INPUT (default text)	136

27.22.4.3.6	GET INPUT (display of Icon)	140

27.22.4.3.7	GET INPUT (Help Information)	147

27.22.4.4	MORE TIME	149

27.22.4.4.1	Definition and applicability	149

27.22.4.4.2	Conformance requirement	149

27.22.4.4.3	Test purpose	149

27.22.4.4.4	Method of test	149

27.22.4.4.5	Test requirement	150

27.22.4.5	PLAY TONE	150

27.22.4.5.1	Definition and applicability	150

27.22.4.5.2	Conformance requirement	150

27.22.4.5.3	Test purpose	150

27.22.4.5.4	Method of test	150

27.22.4.6	POLL INTERVAL	163

27.22.4.6.1	Definition and applicability	163

27.22.4.6.2	Conformance requirement	163

27.22.4.6.3	Test purpose	163

27.22.4.6.4	Method of test	163

27.22.4.6.5	Test requirement	164

27.22.4.7	REFRESH	164

27.22.4.7.1	REFRESH (normal)	164

27.22.4.7.2	REFRESH (IMSI changing procedure)	172

27.22.4.8	SET UP MENU and ENVELOPE MENU SELECTION	176

27.22.4.8.1	SET UP MENU (normal) and ENVELOPE MENU SELECTION	176

27.22.4.8.2	SET UP MENU (help request support) and ENVELOPE MENU SELECTION	187

27.22.4.8.3	SET UP MENU (next action support) and ENVELOPE MENU SELECTION	189

27.22.4.8.4	SET UP MENU (display of icons) and ENVELOPE MENU SELECTION	192

27.22.4.8.5	SET UP MENU (soft keys support) and ENVELOPE MENU SELECTION	197

27.22.4.9	SELECT ITEM	199

27.22.4.9.1	SELECT ITEM (mandatory features for ME supporting SELECT ITEM)	199

27.22.4.9.2	SELECT ITEM (next action support)	212

27.22.4.9.3	SELECT ITEM (default item support)	213

27.22.4.9.4	SELECT ITEM (help request support)	215

27.22.4.9.5	SELECT ITEM (icons support)	216

27.22.4.9.6	SELECT ITEM (presentation style)	220

27.22.4.9.7	SELECT ITEM (soft keys support)	223

27.22.4.9.8	SELECT ITEM (Support of "No response from user")	225

27.22.4.10	SEND SHORT MESSAGE	226

27.22.4.10.1	SEND SHORT MESSAGE (normal)	226

27.22.4.10.2	SEND SHORT MESSAGE (UCS2 support)	243

27.22.4.10.3	SEND SHORT MESSAGE (icon support)	245

27.22.4.11	SEND SS	250

27.22.4.11.1	SEND SS (normal)	250

27.22.4.11.2	SEND SS (Icon support)	262

27.22.4.11.3	SEND SS (UCS2 support)	268

27.22.4.12	SEND USSD	269

27.22.4.12.1	SEND USSD (normal)	269

27.22.4.12.2	SEND USSD (Icon support)	279

27.22.4.12.3	SEND USSD (UCS2 support)	285

27.22.4.13	SET UP CALL	287

27.22.4.13.1	SET UP CALL (normal)	287

27.22.4.13.2	SET UP CALL (second alpha identifier)	299

27.22.4.13.3	SET UP CALL (display of icons)	301

27.22.4.14	POLLING OFF	309

27.22.4.14.1	Definition and applicability	309

27.22.4.14.2	Conformance requirement	309

27.22.4.14.3	Test purpose	309

27.22.4.14.4	Method of test	310

27.22.4.14.5	Test requirement	312

27.22.4.15	PROVIDE LOCAL INFORMATION	312

27.22.4.15.1	Definition and applicability	312

27.22.4.15.2	Conformance requirement	312

27.22.4.15.3 	Test purpose	312

27.22.4.15.4	Method of tests	312

27.22.4.15.5	Test requirement	319

27.22.4.16	SET UP EVENT LIST	319

27.22.4.16.1	SET UP EVENT LIST (normal)	319

27.22.4.17	PERFORM CARD APDU	328

27.22.4.17.1	PERFORM CARD APDU (normal)	328

27.22.4.17.2	PERFORM CARD APDU (detachable card reader)	345

27.22.4.18	POWER OFF CARD	346

27.22.4.18.1	POWER OFF CARD (normal)	346

27.22.4.18.2	POWER OFF CARD (detachable card reader)	348

27.22.4.19	POWER ON CARD	349

27.22.4.19.1	POWER ON CARD (normal)	349

27.22.4.19.2	POWER ON CARD (detachable card reader)	352

27.22.4.20	GET READER STATUS	354

27.22.4.20.1	GET READER STATUS (normal)	354

27.22.4.20.2	GET CARD READER STATUS (detachable card reader)	363

27.22.4.21	TIMER MANAGEMENT and ENVELOPE TIMER EXPIRATION	364

27.22.4.21.1	TIMER MANAGEMENT (normal)	364

27.22.4.21.2	ENVELOPE TIMER EXPIRATION (normal)	401

27.22.4.22	SET UP IDLE MODE TEXT	407

27.22.4.22.1	SET UP IDLE MODE TEXT (normal)	407

27.22.4.22.2	SET UP IDLE MODE TEXT (Icon support)	416

27.22.4.22.3	SET UP IDLE MODE TEXT (UCS2 support)	422

27.22.4.23	RUN AT COMMAND	424

27.22.4.23.1	RUN AT COMMAND (normal)	424

27.22.4.23.2	RUN AT COMMAND (Icon support)	427

27.22.4.24	SEND DTMF	433

27.22.4.24.1	SEND DTMF (Normal)	433

27.22.4.24.2	SEND DTMF (Display of icons)	438

27.22.4.24.3	SEND DTMF (UCS2 support)	443

27.22.4.25	LANGUAGE NOTIFICATION	445

27.22.4.25.1	Definition and applicability	445

27.22.4.25.2	Conformance Requirement	445

27.22.4.25.3	Test purpose	445

27.22.4.25.4	Method of Test	445

27.22.4.25.5	Test requirement	447

27.22.4.26	LAUNCH BROWSER	448

27.22.4.26.1	LAUNCH BROWSER (No session already launched)	448

27.22.4.26.2	LAUNCH BROWSER (Interaction with current session)	453

27.22.4.26.3	LAUNCH BROWSER (UCS2 support)	457

27.22.4.26.4	LAUNCH BROWSER (icons support)	459

27.22.4.27	OPEN CHANNEL	463

27.22.4.27.1	Void	463

27.22.4.27.2	Open Channel (related to GPRS)	463

27.22.4.28	CLOSE CHANNEL	479

27.22.4.28.1	Definition and applicability	479

27.22.4.28.2	Conformance requirements	479

27.22.4.28.3	Test purpose	479

27.22.4.28.4	Method of Test	479

27.22.4.29	RECEIVE DATA	485

27.22.4.29.1	Definition and applicability	485

27.22.4.29.2	Conformance requirements	485

27.22.4.29.3	Test purpose	485

27.22.4.29.4	Method of test	485

27.22.4.30	SEND DATA	494

27.22.4.30.1	Definition and applicability	494

27.22.4.30.2	Conformance requirements	494

27.22.4.30.3	Test purpose	494

27.22.4.30.4	Method of test	495

27.22.4.31	GET CHANNEL STATUS	507

27.22.4.31.1	Definition and applicability	507

27.22.4.31.2	Conformance requirements	507

27.22.4.31.3	Test purpose	507

27.22.4.31.4	Method of test	507

27.22.5	Data Download to SIM	516

27.22.5.1	SMS-PP Data Download	516

27.22.5.1.1	Definition and applicability	516

27.22.5.1.2	Conformance requirement	516

27.22.5.1.3	Test purpose	516

27.22.5.1.4	Method of Test	516

27.22.5.1.5	Test requirement	521

27.22.5.2	SMS-CB Data Download	522

27.22.5.2.1	Definition and applicability	522

27.22.5.2.2	Conformance requirement	522

27.22.5.2.3	Test purpose	522

27.22.5.2.4	Method of Test	522

27.22.5.2.5	Test requirement	525

27.22.6	CALL CONTROL BY SIM	525

27.22.6.1	Procedure for Mobile Originated calls	525

27.22.6.1.1	Definition and applicability	525

27.22.6.1.2	Conformance requirement	525

27.22.6.1.3	Test purpose	525

27.22.6.1.4	Method of tests	525

27.22.6.1.5	Test requirement	548

27.22.6.2	Procedure for Supplementary (SS) Services	548

27.22.6.2.1	Definition and applicability	548

27.22.6.2.2	Conformance requirement	548

27.22.6.2.3	Test purpose	548

27.22.6.2.4	Method of tests	549

27.22.6.2.5	Test requirement	556

27.22.6.3	Interaction with Fixed Dialling Number (FDN)	556

27.22.6.3.1	Definition and applicability	556

27.22.6.3.2	Conformance requirement	556

27.22.6.3.3	Test purpose	556

27.22.6.3.4	Method of tests	556

27.22.6.3.5	Test requirement	562

27.22.6.4	Support of Barred Dialling Number (BDN) service	563

27.22.6.4.1	Definition and applicability	563

27.22.6.4.2	Conformance requirement	563

27.22.6.4.3	Test purpose	563

27.22.6.4.4	Method of tests	563

27.22.6.4.5	Test requirement	570

27.22.7	EVENT DOWNLOAD	570

27.22.7.1	MT Call Event	570

27.22.7.1.1	MT Call Event (normal)	570

27.22.7.2	Call Connected Event	572

27.22.7.2.1	Call Connected Event (MT and MO call)	572

27.22.7.2.2	Call Connected Event (ME supporting SET UP CALL)	574

27.22.7.3	Call Disconnected Event	577

27.22.7.3.1	Call Disconnected Event	577

27.22.7.4	Location Status Event	581

27.22.7.4.1	Location Status Event (normal)	581

27.22.7.5	User Activity Event	584

27.22.7.5.1 	User Activity Event (normal)	584

27.22.7.6	Idle screen available event	586

27.22.7.6.1	Idle Screen Available (normal)	586

27.22.7.7	Card reader status event	587

27.22.7.7.1	Card Reader Status (normal)	587

27.22.7.7.2	Card Reader Status(detachable card reader)	592

27.22.7.8	Language selection event	594

27.22.7.8.1	Language selection event (normal)	594

27.22.7.9	Browser termination event	596

27.22.7.9.1	Browser termination (normal)	596

27.22.7.10	Data available event	598

27.22.7.10.1	Definition and applicability	598

27.22.7.10.2	Conformance requirements	598

27.22.7.10.3	Test purpose	598

27.22.7.10.4	Method of test	598

27.22.7.11	Channel Status event	602

27.22.7.11.1	Definition and applicability	602

27.22.7.11.2	Conformance requirements	602

27.22.7.11.3	Test purpose	602

27.22.7.11.4	Method of test	602

27.22.8	MO SHORT MESSAGE CONTROL BY SIM	606

27.22.8.1	Definition and applicability	606

27.22.8.2	Conformance requirement	606

27.22.8.3	Test purpose	606

27.22.8.4	Method of tests	606

27.22.8.4.1	Initial conditions	606

27.22.8.4.2	Procedure	607

27.22.8.5	Test requirement	615

Annex A: Void	616

Annex B: Void	617

Annex C: Void	618

Annex D (normative): Details of Test-SIM (TestSIM)	619

Annex E (normative): Details of terminal profile support	621

Annex F (informative): Change History	626

Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document describes the technical characteristics and methods of test for testing the SIM Application Toolkit implemented in Mobile Stations (MS) for the Pan European digital cellular communications system and Personal Communication Systems (PCS) operating in the 450 MHz, 480 MHz, 700 MHz, 750 MHz, 850 MHz, 900 MHz, 1 800 MHz and 1 900 MHz frequency band (GSM 400, GSM 700, GSM 750, GSM 850, GSM 900, DCS 1 800 and PCS 1 900) within the European digital cellular telecommunications system, in compliance with the relevant requirements, and in accordance with the relevant guidance given in ISO/IEC 9646-7 [19] and ETS 300 406 [20].

The present document is valid for MS implemented according to GSM Phase2+ R96, or R97, or R98, or R99.

The present document covers the minimum characteristics considered necessary in order to provide sufficient performance for mobile equipment and to prevent interference to other services or to other users, and to the PLMNs.

It does not necessarily include all the characteristics which may be required by a user or subscriber, nor does it necessarily represent the optimum performance achievable.

The present document is part of the GSM-series of technical specifications. The present document neither replaces any of the other GSM technical specifications or GSM related ETSs or ENs, nor is it created to provide full understanding of (or parts of) the GSM 400, GSM 700, GSM 850, GSM 900, DCS1800 and PCS1900 systems . The present document lists the requirements, and provides the methods of test for testing the SIM Application Toolkit implemented in a MS for conformance to the GSM standard.

For a full description of the system, reference should be made to all the GSM technical specifications or GSM related ETSs or ENs. Clause 2 provides a complete list of the GSM technical specifications, GSM related ETSs, ENs, and ETRs, on which this conformance test specifications is based.

If there is a difference between this present conformance document, and any other GSM technical specification or GSM related ETS or EN, or 3GPP TS, then the other GSM technical specification or GSM related ETS or EN or 3GPP TS shall prevail.

Normative requirements for the SIM and SIM Application Toolkit are only specified up to Rel-4. The present document is only available in this release for allowing maintenance of test cases. The core features related to those test cases remain applicable only to the releases in which they have been specified.

The conformance test aspects for this Release are identical with those for the latest Release of TS 51.010-4 [23].

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the relevant Release.

-	For a GSM Phase 2+ Release 1999 MS, references to GSM documents are to version 8.x.y (for 01.-series to 12.-series) or (3.x.y for 21.-series to 35.-series), when available.

-	For a GSM Phase 2+ Release 1998 MS, references to GSM documents are to version 7.x.y, when available.

-	For a GSM Phase 2+ Release 1997 MS, references to GSM documents are to version 6.x.y, when available.

-	For a GSM Phase 2+ Release 1996 MS, references to GSM documents are to version 5.x.y,. when available.

Note:	References to 3GPP Technical Specifications and Technical Reports throughout the present document shall be interpreted according to the Release shown in the formal reference in this clause, based upon the Release of the implementation under test.

EXAMPLE:	References for a R99 MS shall be interpreted as:

[1]		3GPP TS 21.905 R99

[2]		3GPP TS 22.001 R99

etc.

[1]	Void.

[2]	Void.

[3]	Void.

[4]	Void.

[5]	Void.

[6]	Void.

[7]	Void.

[8]	Void.

[9]	Void.

[10]	Void.

[11]	Void

[12]	Void.

[13]	Void.

[14]	Void.

[15]	Void.

[16]	Void.

[17a]	Void.

[17b]	Void.

[18]	Void.

[19]	ISO/IEC 9646-7 (1995): "Information technology - Open Systems Interconnection - Conformance testing methodology and framework - Part 7: Implementation Conformance Statements".

[20]	Void.

[21]	Void.

[22]	3GPP TS 31.111: "USIM Application Toolkit (USAT)"

[23]	3GPP TS 51.010-4: "Mobile Station (MS) conformance specification ; Part 4: Subscriber Identity Module (SIM) application toolkit conformance test specification (Release 14)".

# 3	Void

# 4	Void

# 5	Void

# 6	Void

# 7	Void

# 8	Void

# 9	Void

# 10	Void

# 11 - 26 	Not used

# 27	Void

Annex A:
Void

Annex B:
Void

Annex C:
Void

Annex D Void

Annex E Void

Annex F (informative):
Change History

| TSG# | WG TD# | CR | Rev | Subject | New Ver |
| --- | --- | --- | --- | --- | --- |
| SMG#30 | - | - | - | Approved as release 1996 at SMG#30 | 5.0.0 |
|  |  | A001 | - | Corrections to SIM Application Toolkit Test Specification | 5.1.0 |
|  |  |  | - | Version update to 5.1.1 for Publication | 5.1.1 |
|  |  | A002 | - | Editorial and coding corrections | 5.2.0 |
|  |  | A003 | - | Correction of wrong coding for SIM Application Toolkit test 27.22.4.2 | 5.3.0 |
|  |  | A004 | - | Corrections for Test Case 27.22.5.1 (SMS-PP Data Download) | 5.3.0 |
|  |  | A005 | - | Correction of wrong coding for SIM Application Toolkit 27.22 | 5.4.0 |
|  |  | A006 | - | Corrections for Test Case 27.22.4.7 (REFRESH) | 5.5.0 |
|  |  | A007 | - | Corrections for Test Case 27.22.5.2 (SMS-CB Data Download) | 5.5.0 |
|  |  | A008 | - | Upgrade of the MS SAT test specification to Release 99 | 8.1.0 |
|  |  | A010r1 | - | Addition of Terminal Profile information, suppression of PLAY TONE Test sequence 1.2 | 8.2.0 |
|  |  | A011 | - | References to 11.10-1 replaced. Reference to 11.10-2 removed. | 8.3.0 |
|  |  | A012 | - | Corrections to Send Short Message, Sequence 1.4 | 8.4.0 |
|  |  | A013 | - | Redial in Set Up Call | 8.4.0 |
|  |  | A014 | - | Correction to Terminal Response: Set Up Call 1.7.1 | 8.4.0 |
|  |  | A015 | - | Select Item: Support of "No response from user" | 8.4.0 |
|  |  | A016 | - | Correction of Emergency Call test cases | 8.4.0 |
|  |  | A017 | - | Essential corrections to default values for SIM Application Toolkit testing |  |
|  |  | A018 | - | Clarification on comprehension required flag usage | 8.5.0 |
|  |  | A019 | - | Essential corrections to Display text test cases |  |
|  |  | A020 | - | Essential corrections to Get Inkey test cases |  |
|  |  | A021 | - | Essential corrections to Get Input test cases | 8.5.0 |
|  |  | A022 | - | Essential corrections to Set Up Menu test cases |  |
|  |  | A023 | - | Essential corrections to Play Tone test cases |  |
|  |  | A024 | - | Essential corrections to Poll Intervall test case |  |
|  |  | A025 | - | Essential corrections to Polling off test case | 8.5.0 |
|  |  | A026 | - | Essential corrections to Provide Local Information test cases | 8.5.0 |
|  |  | A027 | - | Essential corrections to Send Short message test cases | 8.5.0 |
|  |  | A028 | - | Essential corrections to Language Notification test cases | 8.5.0 |
|  |  | A029 | - | Essential corrections to Send SS test cases |  |
|  |  | A030 | - | Essential corrections to Set Up Call test cases | 8.5.0 |
|  |  | A031 | - | Essential corrections to Send USSD test cases |  |
|  |  | A032 | - | Essential correction to Set Up Idle Mode Text test cases | 8.5.0 |
|  |  | A033 | - | Essential corrections to Power Off Card test case |  |
|  |  | A034 | - | Essential corrections to Perform Card APDU test cases |  |
|  |  | A035 | - | Essential correction to Get Reader Status test cases |  |
|  |  | A036 | - | Essential corrections to Send DTMF test cases |  |
|  |  | A037 | - | Essential corrections to CALL CONTROL BY SIM test cases | 8.5.0 |
|  |  | A038 | - | Essential corrections to CALL CONTROL BY SIM (Interaction with FDN/ BDN) test cases | 8.5.0 |
|  |  | A039 | - | Essential corrections to Select Item test cases |  |
|  |  | A040 | - | Essential corrections to card reader status event download test cases |  |
|  |  | A041 | - | Essential corrections to language selection and browser termination event download test cases | 8.5.0 |
|  |  | A042 | - | Essential corrections to Close Channel test cases | 8.5.0 |
|  |  | A043 | - | Essential corrections to Launch Browser test cases | 8.5.0 |
|  |  | A044 | - | Essential corrections to Open Channel test cases |  |
|  |  | A045 | - | Essential corrections to Receive Data test cases |  |
|  |  | A046 | - | Essential corrections to Send Data test cases |  |
|  |  | A047 | - | Essential corrections to channel status event download test case |  |
|  |  | A048 | - | Essential corrections to Get Channel Status test cases |  |
|  |  | A049 | - | Essential corrections to CB data download test cases |  |
|  |  | A050 | - | Essential corrections to location status, user activity and idle screen available event download test cases | 8.5.0 |
|  |  | A051 | - | Corrections in the REFRESH test sequences (with inclusion of T3-030535’s contents) | 8.5.0 |
|  |  | A052 | - | Essential corrections to test requirement references | 8.5.0 |
|  |  | A053 | - | Essential corrections to CALL CONTROL BY SIM (supplementary services) test case |  |
|  |  | A054 | - | Essential corrections to MT Call, Call connected and Call disconnected event download test cases | 8.5.0 |
|  |  | A055 | - | Introduction of “MO Short Message Control by SIM” envelope testing | 8.6.0 |
|  |  | A056 | - | Re-Introduction of changes already approved at the last T3. | 8.6.0 |
|  |  | A057 | - | Essential corrections | 8.6.0 |
|  |  | A058 | - | Essential corrections to 27.22.4.14 “POLLING OFF” | 8.6.0 |
|  |  | A059 | - | Essential corrections to Send DTMF test cases | 8.6.0 |
|  |  | A060 | - | Introduction of BIP testing in GPRS | 8.6.0 |
|  |  | A061 | - | Correction of image instance descriptor for colour icons | 8.7.0 |
|  |  | A062 | - | Essential correction on Terminal Profile for the BIP Inclusion of tests on Open Channel for GPRS, on the user confirmation | 8.7.0 |
|  |  | A063 | - | CR 11.10-4 Launch Browser test cases | 8.7.0 |
|  |  | A064 | - | CR 11.10-4 R99: Essential corrections | 8.7.0 |
|  |  | A065 | - | CR 11.10-4 R99: Essential correction of coding convention | 8.7.0 |
|  |  | A071 | - | Correction of Cell Broadcast message download test | 8.8.0 |
|  |  | A066 | - | Essential corrections | 8.8.0 |
|  |  | A067 | - | Support of GSM 700, GSM 850 and PCS 1900 | 8.8.0 |
|  |  | A068 | - | Corrections of applicability table | 8.8.0 |
|  |  | A070 | - | Correction on allowing optional parameters in ENVELOPE(CALL CONTROL) command for call set-ups when testing Call Control procedures | 8.8.0 |
|  |  | A069 | - | Essential corrections to Call Control test cases | 8.8.0 |
|  |  | A076 | - | Essential corrections of Event Download test cases | 8.9.0 |
|  |  | A073 | - | Essential corrections | 8.9.0 |
|  |  | A072 | - | Clarification of call hang up in 27.22.4.5 Play Tone | 8.9.0 |
|  |  | A074 | - | Removal of misleading comment from Refresh SIM Reset tests | 8.9.0 |
|  |  | A075 | - | Correction of poll interval related tests | 8.9.0 |
|  |  | A077 | - | Correction of Send Short Message test case | 8.10.0 |
|  |  | A078 | - | Correction of Select Item test case | 8.10.0 |
|  |  | A079 | - | Correction of Language Notification test case | 8.10.0 |
|  |  | A080 | - | Correction of Select Item (Next action identifier) test case | 8.10.0 |
|  |  | A081 | - | Correction of PROFILE DOWNLOAD test case – incorrect P2 | 8.10.0 |
|  |  | A082 | - | Correction of CALL CONTROL test cases | 8.10.0 |
|  |  | A083 | - | Incorrect specification of file codings | 8.10.0 |
|  |  | A084 | - | Correction of Refresh test case | 8.10.0 |
|  |  | A085 | - | Correction of MO SM CONTROL BY SIM test case | 8.10.0 |
|  |  | A086 | - | Correction of Errors | 8.10.0 |
|  |  | A087 | - | Clarification of PLAY TONE test case | 8.10.0 |
|  |  | A088 | - | Clarification of RECEIVE DATA test case | 8.10.0 |
|  |  | A089 | - | Corrections for Test Case 27.22.5.1 (SMS-PP Data Download) | 8.10.0 |
|  |  | A090 | - | Modification of 27.22.1 PROFILE DOWNLOAD | 8.10.0 |
|  |  | A091 | - | Correction of Set Up Idle Mode Text test case | 8.10.0 |
|  |  | A092 | - | Correction of Timer Management test cases | 8.10.0 |
|  |  | A093 | - | Essential Corrections on Launch Browser | 8.10.0 |
| TP-27 | T3-050096 | A094 | - | Correction of terminal profile test | 8.11.0 |
| TP-27 | T3-050097 | A095 | - | Correction of Set Up Call test | 8.11.0 |
| TP-27 | T3-050098 | A096 | - | Essential Corrections | 8.11.0 |
| TP-27 | T3-050099 | A097 | - | Correction of Call Connected Event test | 8.11.0 |
| TP-27 | T3-050100 | A098 | - | Correction of Call Control test cases | 8.11.0 |
| TP-27 | T3-050125 | A099 | - | Corrections of references | 8.11.0 |
| TP-27 | T3-050155 | A100 | - | Clarification on LAUNCH BROWSER test case | 8.11.0 |
| TP-27 | T3-050194 | A101 | - | Correction of network related tests | 8.11.0 |
| TP-27 | T3-050195 | A102 | - | Correction of Timer Management test | 8.11.0 |
| TP-27 | T3-050196 | A103 | - | Correction of coding of SS RETURN RESULT in 27.22.4.12 SEND USSD | 8.11.0 |
| TP-27 | T3-050197 | A104 | - | Correction of Expected sequence 2.4 in section 27.22.4.22.2.4 SET UP IDLE MODE TEXT (icon support) | 8.11.0 |
| TP-27 | T3-050198 | A105 | - | Correction on Timer Management test cases | 8.11.0 |
| CT-28 | C6-050354 | A106 | - | Correction of coding in MT Call Even | 8.12.0 |
| CT-28 | C6-050381 | A107 | - | Essential corrections | 8.12.0 |
| CT-28 | C6-050382 | A109 | - | Too many digits in PCS 1900 for the Called Party BCD number | 8.12.0 |
| CT-29 | C6-050629 | A110 | - | CR 11.10-4: Correction of applicability and terminal profile support tables | 8.13.0 |
| CT-29 | C6-050631 | A111 | - | CR 11.10-4: Correction of Refresh tests | 8.13.0 |
| CT-29 | C6-050632 | A112 | - | CR 11.10-4: Correction of EF_BDN coding | 8.13.0 |
| CT-29 | C6-050634 | A127 | - | CR 11.10-4 R99: Essential correction to Terminal Profile table E.1 | 8.13.0 |
| CT-29 | C6-050636 | A113 | - | CR 11.10-4: Incorrect Dialling Number string in clause 27.22.4.13.1 SEQ 1.9 for PCS 1900 | 8.13.0 |
| CT-29 | C6-050640 | A115 | - | CR 11.10-4: Incorrect Ti Flag value for SET UP 1.4.1 in clause 27.22.4.16.1 | 8.13.0 |
| CT-29 | C6-050642 | A116 | - | CR 11.10-4: Correction of TP-MR (TP Message Reference) of the SMS SUBMIT TPDU submitted to the SS (Network) | 8.13.0 |
| CT-29 | C6-050644 | A117 | - | CR 11.10-4: Corrections in the Logical description and BER encoding in clause 27.22.6.2 and 27.22.4.11 | 8.13.0 |
| CT-29 | C6-050646 | A118 | - | CR 11.10-4: Incorrect DCS in SMS-CB data download tests | 8.13.0 |
| CT-29 | C6-050662 | A119 | - | CR 11.10-4: Essential Corrections in clause 27.22.8 MO SHORT MESSAGE CONTROL BY SIM | 8.13.0 |
| CT-29 | C6-050664 | A120 | - | CR 11.10-4: Essential Corrections | 8.13.0 |
| CT-29 | C6-050671 | A121 | - | CR 11.10-4 R99: Essential corrections in clause 27.22.4.7.2 REFRESH (IMSI changing procedure) | 8.13.0 |
| CT-29 | C6-050672 | A122 | - | CR 11.10-4 R99: Incorrect SMS-PP 1.4.1 TPDU in clause 27.22.4.22.1 | 8.13.0 |
| CT-29 | C6-050674 | A123 | - | CR 11.10-4 R99: Missing interactions in Bearer Independent Protocol test cases | 8.13.0 |
| CT-29 | C6-050669 | A124 | - | CR 11.10-4 R99: Applicability of TC 27.22.4.7.1 and TCs related to FDN and BDN | 8.13.0 |
| CT-29 | C6-050703 | A126 | - | Correction of CB message identifier | 8.13.0 |
| CT-29 | C6-050714 | A125 | - | Essential corrections in display icons Setup Menu and Select Item | 8.13.0 |
| - | - | - | - | editorial corrections due to the CRs approved at CP-29 | 8.13.1 |
| CT-30 | CP-050483 | A114 | - | Corrections of Set Up Call (second alpha identifier) test | 8.14.0 |
| CT-30 | CP-050483 | A129 | - | Essential Corrections of Set Up Menu test | 8.14.0 |
| CT-30 | CP-050483 | A130 | - | Essential Corrections in clause 27.22.4.11 | 8.14.0 |
| CT-30 | CP-050483 | A131 | - | Corrections to Select Item (icons support) | 8.14.0 |
| CT-30 | CP-050483 | A132 | - | 27.22.7.4.1 Location Status Event (normal) | 8.14.0 |
| CT-30 | CP-050483 | A134 | - | Correction of applicability table | 8.14.0 |
| CT-30 | CP-050483 | A135 | - | Correction in SMS-PP 1.4.1 TPDU of clause 27.22.4.22.1 | 8.14.0 |
| CT-30 | CP-050483 | A136 | - | Essential Corrections of SMS-PP download message in Refresh test case | 8.14.0 |
| CT-30 | CP-050483 | A137 | - | Essential Correction in MO SHORT MESSAGE CONTROL BY SIM Deletion of sequence 1.9 | 8.14.0 |
| CT-30 | CP-050483 | A138 | - | Deletion of SEQ 1.3 in clause 27.22.4.13.1 | 8.14.0 |
| CT-31 | CP-060014 | A148 | - | Essential Corrections in clause 27.22.4.11 | 8.15.0 |
| CT-31 | CP-060014 | A151 | - | Essential Corrections in clause 27.22.8 MO SHORT MESSAGE CONTROL BY SIM | 8.15.0 |
| CT-31 | CP-060014 | A147 | - | Essential correction in SEQ 1.4 of clause 27.22.4.11.1 SEND SS (normal) | 8.15.0 |
| CT-31 | CP-060014 | A146 | - | Essential corrections of Run AT Command tests | 8.15.0 |
| CT-31 | CP-060014 | A152 | - | Essential corrections to SET UP CALL test sequences | 8.15.0 |
| CT-31 | CP-060012 | A158 | - | Essential correction of Refresh IMSI changing tests | 8.15.0 |
| CT-31 | CP-060012 | A141 | - | Essential correction of UCS2 related test case applicability | 8.15.0 |
| CT-31 | CP-060012 | A142 | - | Removal of SEQ 2.2 in clause 27.22.4.12.2 | 8.15.0 |
| CT-31 | CP-060012 | A150 | - | Essential correction of Channel Data length in SEQ 1.1 of clause 27.22.4.30 | 8.15.0 |
| CT-31 | CP-060012 | A145 | - | Essential correction of SMS-CB (data download) tests | 8.15.0 |
| CT-31 | CP-060013 | A139 | - | Deletion of Send Data test sequence | 8.15.0 |
| CT-31 | CP-060013 | A140 | - | Essential correction of Provide Local Information (IMEI) test | 8.15.0 |
| CT-31 | CP-060013 | A143 | - | Essential Correction in SEQ 1.8 of clause 27.22.8 | 8.15.0 |
| CT-31 | CP-060013 | A144 | - | Essential correction on 27.22.7.3.1 Call Disconnected Event | 8.15.0 |
| CT-31 | CP-060013 | A149 | - | Essential correction of Channel Data length in clause 27.22.4.30 | 8.15.0 |
| CT-31 | CP-060015 | A154 | - | Essential Correction in TERMINAL RESPONSE coding of clause 27.22.4.31 | 8.15.0 |
| CT-31 | CP-060015 | A156 | - | Essential corrections to Timer Expiration tests | 8.15.0 |
| CT-31 | CP-060015 | A153 | - | BER-TLV suppressions | 8.15.0 |
| CT-31 | CP-060016 | A155 | - | Creation of a new TS 51.10-4, Rel-4 specification coming from TS 11.10-4 R99 | 51.010-4v4.0.0 |
| CT-32 | CP-060236 | 0001 | - | Essential correction to prevent optional ME features being mandatorily tested | 4.1.0 |
| CT-32 | CP-060236 | 0004 | - | Essential correction of Language Selection Event test | 4.1.0 |
| CT-32 | CP-060242 | 0002 | - | Essential correction of BIP tests | 4.1.0 |
| CT-32 | CP-060242 | 0003 | - | Essential Correction in REGISTER 1.2B message coding of clause 27.22.4.11.1 SEND SS (normal) | 4.1.0 |
| CT-32 | CP-060242 | 0005 | - | Essential correction of 27.22.4.13.1 SET UP CALL, seq 1.4 | 4.1.0 |
| CT-32 | CP-060242 | 0006 | - | Essential correction of second card reader test applicability | 4.1.0 |
| CT-32 | CP-060242 | 0007 | - | Correction of TON/NPI coding for Call Control Test case | 4.1.0 |
| CT-32 | CP-060242 | 0008 | - | Essential corrections on 27.22.4.11.1 sequence. 1.2 | 4.1.0 |
| CT-33 | CP-060382 | 0016 | 1 | Essential correction of GET INPUT test | 4.2.0 |
| CT-33 | CP-060382 | 0018 | 1 | Essential correction of SEND DATA test | 4.2.0 |
| CT-33 | CP-060382 | 0019 | 1 | Correction of various typographical errors | 4.2.0 |
| CT-33 | CP-060382 | 0010 | 2 | Essential correction of BIP test cases | 4.2.0 |
| CT-33 | CP-060517 | 0012 | 1 | Essential corrections Set Up Call, seq. 1.9 | 4.2.0 |
| CT-33 | CP-060475 | 0014 | 1 | Essential corrections of MMI entries in table E.1 | 4.2.0 |
| CT-33 | CP-060475 | 0009 | 1 | Corrections to SET UP CALL test case 27.22.4.13.1 | 4.2.0 |
| CT-33 | CP-060475 | 0020 | 2 | Essential corrections to SEND SS concerning longForwardedToNumber | 4.2.0 |
| CT-33 | CP-060475 | 0017 | 2 | Corrections to MO SHORT MESSAGE CONTROL BY SIM tests | 4.2.0 |
| CT-34 | CP-060539 | 0023 | - | Essential corrections on TC 27.22.4.29, sequence 1.1 | 4.3.0 |
| CT-34 | CP-060540 | 0021 | - | Correction of APN Coding in Open Channel test case | 4.3.0 |
| CT-34 | CP-060540 | 0013 | 2 | Essential corrections of BIP entries in table E.1 | 4.3.0 |
| CT-34 | CP-060540 | 0022 | 2 | Essential correction of Result TLV handling | 4.3.0 |
| CT-34 | CP-060540 | 0024 | 1 | Essential correction of expected sequence in OPEN CHANNEL test case | 4.3.0 |
| CT-35 | CP-070062 | 0032 |  | Essential correction of Send USSD applicability | 4.4.0 |
| CT-35 | CP-070062 | 0030 | 1 | Essential correction of GPRS QoS parameter in BIP tests | 4.4.0 |
| CT-35 | CP-070062 | 0036 | 1 | Test execution recommendation for terminals supporting both, SAT and USAT | 4.4.0 |
| CT-35 | CP-070063 | 0029 |  | Essential correction of 27.22.5.2 | 4.4.0 |
| CT-35 | CP-070063 | 0027 | 1 | Essential correction of Terminal Profile Support table | 4.4.0 |
| CT-35 | CP-070063 | 0026 | 1 | Essential correction of 27.22.4.13.1 Expected Sequence 1.7 | 4.4.0 |
| CT-36 | CP-070290 | 0037 | - | Correction of reference to ISO/IEC 7816-3 | 4.5.0 |
| CT-36 | CP-070290 | 0038 | 1 | Essential correction of test case applicability for 27.22.6.1 | 4.5.0 |
| CT-36 | CP-070290 | 0039 | 1 | Essential correction on 27.22.8 | 4.5.0 |
| - | - | - | - | MCC Table formatting throughout document (reduces page count) | 4.5.0 |
| CT-37 | CP-070609 | 0040 | - | Essential correction to 27.22.8 | 4.6.0 |
| CT-37 | CP-070610 | 0041 | 1 | Essential correction of 27.22.6.2 | 4.6.0 |
| CT-37 | CP-070610 | 0042 | - | Essential correction of 27.22.4.13.1, seq. 1.9 | 4.6.0 |
| CT-37 | CP-070609 | 0043 | - | Essential Correction to insert a missing Carriage Return | 4.6.0 |
| CT-38 | CP-070843 | 0044 | 1 | Essential correction of 27.22.4.7.1, seq. 1.6 | 4.7.0 |
| CT-38 | CP-070843 | 0045 | 1 | Essential correction of 27.22.8, seq. 1.3 | 4.7.0 |
| CT-38 | CP-070843 | 0046 | 1 | Essential correction of 27.22.4.26.2.4.2, seq. 2.2 | 4.7.0 |
| CT-38 | CP-070843 | 0047 | - | Correction to add optional support of Call Hold Supplementary Service | 4.7.0 |
| CT-39 | CP-080170 | 0048 | 1 | Essential correction to network dependency of several tests | 4.8.0 |
| CT-40 | CP-080389 | 0050 | 1 | Essential correction of icon test case applicability | 4.9.0 |
| CT-40 | CP-080389 | 0052 | 3 | Essential correction of test case applicability of 27.22.6.2 and 27.22.4.11 | 4.9.0 |
| CT-41 | CP-080590 | 0053 | 1 | Essential correction of TC 27.22.4.11.1 Seq. 1.4B | 4.10.0 |
| CT-42 | CP-080948 | 0055 | - | Essential correction of TC 27.22.7.8.1 network dependency | 4.11.0 |
| CT-42 | CP-080948 | 0056 | - | Essential correction of GPRS QoS parameter in browser tests | 4.11.0 |
| CT-42 | CP-080948 | 0056 | - | Essential correction of 27.22.4.26.2 Seq. 2.2 | 4.11.0 |
| CT-42 | CP-080948 | 0056 | - | Pre-conditions for Launch browser | 4.11.0 |
| CT-43 | CP-080189 | 0059 |  | Essential correction to 27.22.4.3.6 (GET INPUT (display of Icon)), sequence 6.1A | 4.12.0 |
| CT-43 | CP-080189 | 0060 |  | Essential correction to 27.22.4.11.2 and 27.22.4.11.3 (SEND SS) | 4.12.0 |
| CT-43 | CP-080189 | 0061 |  | Essential correction to 27.22.4.31 (GET CHANNEL STATUS) sequence 1.3 | 4.12.0 |
| CT-43 | CP-080189 | 0062 |  | Essential correction 27.22.4.14 (POLLING OFF) | 4.12.0 |
| CT-43 | CP-080189 | 0063 | 1 | Essential correction to BIP tests - usage of ME's default channel identifier | 4.12.0 |
| CT-44 | CP-090460 | 0064 | 1 | Test case and test case applicability changes for terminals with reduced SAT capabilities | 4.13.0 |
| CT-45 | CP-090720 | 0066 |  | Essential correction of applicability and terminal profile table | 4.14.0 |
| CT-45 | CP-090720 | 0065 | 3 | Essential correction to icon test applicability | 4.14.0 |
| -------- | --------------- | - | - | Correction of misimplementation of CR 0064 | 4.14.1 |
| CT-47 | CP-100179 | 0067 | 1 | Correction of typo error | 4.15.0 |
| CT-47 | CP-100179 | 0069 | - | Essential correction to the condition table | 4.15.0 |
| CT-47 | CP-100179 | 0068 | - | Correction of applicability for 'no alpha identifier presented' sequences | 4.15.0 |
| CT-49 | CP-100591 | 0071 | 1 | Essential correction of Table E.1 regarding 'Width reduction when in a menu' | 4.16.0 |
| CT-49 | CP-100591 | 0073 | 1 | Essential correction to test case applicability of letter class C features | 4.16.0 |
| CT-49 | CP-100591 | 0072 | 3 | Essential correction to Open Channel 27.22.4.27.2 sequence 2.4 test | 4.16.0 |
| CT-49 | CP-100619 | 0070 | 1 | Essential correction of test 27.22.4.9.3 | 4.16.0 |
| CT-50 | CP-100833 | 0074 | - | Essential correction of the applicability of test 27.22.4.22.1 Seq. 1.4 | 4.17.0 |
| CT-50 | CP-100833 | 0076 | 1 | Clarification of 'ELSE' parts in Table E.1 | 4.17.0 |
| CT-51 | CP-110229 | 0077 | - | Correction of Send Short Message test case redundancy | 4.18.0 |
| CT-52 | CP-110505 | 0078 | - | Correction of Additional test Execution Recommendation AER002 due to incorrect implementation of CR 0077 | 4.19.0 |
| CT-53 | CP-110592 | 0080 | 1 | Essential correction of Data Destination Address settings in BIP and Launch Browser tests | 4.20.0 |
| CT-54 | CP-110906 | 0081 | 1 | Essential correction to SMS-CB Applicability | 4.21.0 |
| CT-54 | CP-110906 | 0079 | 2 | Essential correction to Play Tone test | 4.21.0 |
| CT-54 | CP-110906 | 0083 | 1 | Correction to the condition ID of Table B.1 | 4.21.0 |
| CT-55 | CP-120151 | 0084 | 1 | Test applicability correction of Open Channel with user rejection tests | 4.22.0 |
| CT-56 | CP-120394 | 0085 | 2 | Test applicability correction for terminals operating in PS mode | 4.23.0 |
| CT-56 | CP-120394 | 0086 | 1 | Correction of expected Terminal Reponse for unsuccessful Open Channel commands | 4.23.0 |
| CT-57 | CP-120628 | 0087 | 2 | Modification of the initial conditions for clause 27.22.4.7.1 | 4.24.0 |
| CT-57 | CP-120629 | 0088 | 2 | Essential correction of Launch Browser tests | 4.24.0 |
| CT-57 | CP-120629 | 0090 | 2 | Essential correction of Launch Browser tests | 4.24.0 |
| CT-59 | CP-130149 | 0092 | 1 | Applicability of tests for MEs with reduced capabilities | 4.25.0 |
| CT-60 | CP-130373 | 0093 |  | Correction to Applicability of test case 27.22.4.1, seq. 4.4 | 4.26.0 |
| CT-60 | CP-130373 | 0094 | 2 | Changes in LAUNCH BROWSER test cases | 4.26.0 |
| CT-62 | CP-130793 | 0097 |  | Essential correction for Applicability table related to Open Channel sequence 2.8 | 4.27.0 |
| CT-64 | CP-140419 | 0106 | 1 | Creation of Rel-12 | 12.0.0 |
| CT-64 | CP-140421 | 0098 | 1 | Essential correction of mismatch between proactive command coding and expected text to be displayed. | 12.0.0 |
| CT-65 | CP-140704 | 0109 | 1 | Usage of URL in test cases for LAUNCH BROWSER command | 12.1.0 |
| CT-65 | CP-140704 | 0110 | 1 | Corrections of the Text String coding format and General Result reference | 12.1.0 |
| CT-65 | CP-140704 | 0111 | 1 | Addition of test case applicability for Rel-4 | 12.1.0 |
| CT-66 | CP-140965 | 0112 | 1 | Change of test sequence for LAUNCH BROWSER with default URL | 12.2.0 |
| SP-70 |  |  |  | Automatic upgrade to Rel-13 | 13.0.0 |
| CT-73 | CP-160548 | 0114 | 1 | Relaxing the mandatory clause and making features optional | 13.1.0 |
| CT-74 | CP-160791 | 0115 | 1 | Correction of test case for Location status event | 13.2.0 |
| CT-77 | CP-172063 | 0116 | 1 | Deletion of Rel-13 content of TS 51.010-4 and pointer to the next release | 13.3.0 |