## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #101, Bangalore, India
Sep 11th – 15th, 2023
RP-231507

## Slide 2: Executive Summary
Total 743 Tdocs at submission deadline (excluding LSin received from other groups) in Q3
  2% LSs and related documents
  18% Maintenance: Rel-17 & earlier
  3% Corrections and enhancements: Rel-18
  77% Documents to Rel-18 WIs/SIs
Updated endorsed guidelines for f2f meeting with 1-way remote access: R3-233703
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-234494
R18 SDT WI and eNPN WI are completed in RAN3, all related CRs will be submitted to Dec RAN plenary meeting.
RAN3 #121 | Aug 21st – 25th, 2023 Toulouse, France
RAN #101 | Sep 11th – 15th, 2023 Bangalore, India

## Slide 3: Election activities
Gen Cao was re-elected as RAN3 Vice Chair in RAN3#121. Congratulations!

## Slide 4: Tdoc submitted to RAN3
The total number of contributions around 700 for each RAN3 meeting is affordable
Notes: w

## Slide 5: Tdocs for each Topic

## Slide 6: Overview of RAN3-led Rel-18 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
941009 | Mobile IAB (Integrated Access and Backhaul) for NR WI | NR_mobile_IAB-Core | 23/12/2023 | 60% | WID: RP-222671 | 70% | 
941008 | Enhancement on NR QoE management and optimizations for diverse services WI | NR_QoE_enh-Core | 23/12/2023 | 50% | WID: RP-223488 | 70% | Reply LS to RAN2 on area scope for QoE measurements in R3-234767. LS to RAN2, SA2 on QMC support in RRC_IDLE and RRC_INACTIVE in R3-234745. LS to RAN2 on RAN3 progress on QoE in NR-DC in R3-234750.
941010 | Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN WI | NR_AIML_NGRAN-Core | 23/12/2023 | 60% | WID: RP-231159 | 80% | 
941007 | Further enhancement of data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) WI | NR_ENDC_SON_MDT_enh2-Core | 23/12/2023 | 60% | WID: RP-231157 | 80% | Reply LS to RAN2 on SHR and SPR in R3-234716. LS to RAN2 on RACH enhancement in R3-234643. LS on MDT for NPN to RAN2, SA5 in R3-234744.
940088 | Enhancement for resiliency of gNB-CU-CP SI | FS_gNB_CU_CP_resiliency | 22/09/2022 | 100% | SID: RP-221438 |  | 
991137 | Core part: Network Slicing Phase 3: NR aspects | eNS_Ph3-NR-Core | 23/12/2023 | 30% | WID: RP-230787 | 70% | 
991138 | Core part: Non-Public Networks Phase 2: NG-RAN aspects | eNPN_Ph2-NGRAN-Core | 23/09/2023 | 90% | WID: RP-230788 | 99% | RAN3 intends to have REL-18 specs only in Dec.23
991136 | Core part: NR Timing Resiliency and URLLC enhancements | TRS_URLLC-NR-Core | 23/12/2023 | 25% | WID: RP-230754 | 60% | 
WI: Black
SI: Blue
CompletedWI/SI: Red

## Slide 7: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-231508, which includes:
  50 CRs were agreed in Q3.
  4 Rel-15: 4 Cat.F CRs
  14 Rel-16: 10 Cat.F CRs, 4 Cat.A CRs
  32 Rel-17: 18 Cat.F CRs, 14 Cat.A CRs
    1 Cat.F TEI17 CRs with TEI identifier
      Correction on the local NG-RAN Node Identifier on Xn [RRCInactive], which is related to R3-222599 approved in RAN #95-e
    3 Non-Backwards-Compatible (NBC) CRs for Rel-16 and Rel-17
      Rel-17: R3-234511, R3-234080, R3-234081
    (Here is how 3GPP works with NBC changes)
  5 endorsed draftCRs to RAN2 specs.

## Slide 8: Experience for GTW Usage in f2f meeting
RAN3 had one meeting room for main session which supports 1-way remote access. RAN3 had a seperate breakout room for offline discussion, which is used sufficiently in Aug meeting, the improvement on the overbooking issue on Wednesday and Thursday needs to be further checked!
In general, the number of remote participants for main session is limited, less than 10. The audio device test for remote access needs to be performed before daily session starts.
MCC and IT support during the meeting is sufficient.

## Slide 9: R18 SON/MDT WI
Progress in the last quarter
For SHR and SPCR:
  In case of MN initiated PSCell change, MN will have the final say on the T310/T312 SPR thresholds.
  Support correlation of SHR and LTE RLF Report in case both are generated during an inter-RAT HO from NR to LTE
  In order to support correlation, C-RNTI (either source C-RNTI or Target C-RNTI) and time between HO execution and SHR retrieval can be used if reported by the UE. It is up to RAN2 to decide whether to use source C-RNTI or Target C-RNTI.
  If RAN2 agrees to use Target C-RNTI in order to support correlation, Target C-RNTI should be included in the Xn HANDOVER REPORT. SN Mobility Information is identified to be used for SN initiated PSCell change and MN initiated PSCell change scenarios.
For MRO:
  Include CPC candidate cell list and CPC execution condition(s) to the message from the MN to the source SN.
  The MN performs the initial analysis when SCGFailureInformation is received from the UE e.g. whether it is CPA or CPC, if CPC whether it is MN initiated or SN initiated.
  Convert the WA into agreement “Define a new handover report type in the Inter-system HO Report over S1 and NG”.
For RACH enhancement:
  It can be left to gNB implementation whether and how to forward the SN RA Reports in case there is no X2/Xn connectivity between the node retrieving the RA Report from the UE and the node serving the PSCells indicated by UE in the RA Report.
For SON/MDT Enhancements for Non-Public Networks:
  The maximum number of SNPNs in the MDT SNPN list should be 16.
  No need for SNPN-wide area scope.

## Slide 10: R18 SON/MDT WI
Progress in the last quarter
For SON for NR-U:
  Convert the following WA into agreement: WA: introduce an optional load metric on Radio Resource Status per NR-U Channel in XnAP RESOURCE STATUS UPDATE message and in F1AP RESOURCE STATUS UPDATE message.
  Introduce an optional load metric on Radio Resource Status per NR-U Channel in XnAP RESOURCE STATUS UPDATE message and in F1AP RESOURCE STATUS UPDATE message.
  There is no need to transfer the UL EDT in F1AP RESOURCE STATUS UPDATE message.
Next steps
FFS whether SN can propose its preferred T310/T312 SPR thresholds to MN.
FFS whether the T310/T312 timer values can be provided as assistance information from SN to MN (e.g., to assist in the root cause analysis).
FFS whether the objective of T304 SPR trigger is to only optimize RACH access issues in target SN or whether it can be also used to optimize mobility configurations in the initiating node.
For CPA or MN initiated CPC, there are two options on the table. For SN initiated CPC, there are two options on the table.
Whether the MRO for fast MCG recovery needs to support pre-R18 UEs?
For HO execution, FFS whether the source node can deduce from UE reports – excluding UL LBT failures information - whether the target node suffered from DL LBT issues during the HO execution.

## Slide 11: R18 QoE WI
Progress in the last quarter
No need for UEs in RRC_INACTIVE and RRC_IDLE to perform RVQoE measurement collection.
New gNB needs to know measurement session status, service type, WA: available RVQoE metrics.
When UE is in RRC_CONNECTED, the area scope checking is done by RAN by Area Scope of QMC IE. When UE is in either RRC_INACTIVE or RRC_IDLE, UE performs area scope checking.
Reuse legacy procedures for the MN-SN coordination in NR-DC to support QoE.
For s-based QoE configuration received by MN
- MN sends the QoE configuration via SRB1
- QoE reports can be sent via SRB4 or SRB5
For management based QoE, there is no need for SN to explicitly indicate to the MN whether it wants to configure the UE directly via SRB3 or via a container and SRB1.
Modify the previous agreement as follows:
In case the SN is interested in configuring a UE with an m-based QoE measurement configuration, the MN can decide and notify the SN whether:
- The MN sends the configuration information to the UE, or
- The SN should send the configuration to the UE
Define two different reporting leg indications for QoE and RVQoE.
For a UE in NR-DC, each legacy QoE configuration can have only one corresponding RVQoE configuration when needed.
The discussion on Threshold-based triggers for RAN visible QoE is suspend in RAN3 and whether further discussion is needed is pending on progress in RAN2 and SA4.
DU can deactivate RVQoE reporting over F1 per UE or per DU (which means all the UEs served by DU). The details on the solution, e.g., whether the F1AP procedure for deactivation of RVQoE reporting is UE-associated or non-UE-associated can be further discussed.

## Slide 12: R18 QoE WI
Progress in the last quarter
QoE measurement continuity from NR to LTE/5GC and vice versa can be supported by the current Area Scope for QMC IE.
The scenario where a UE is handed over from NR to LTE/5GC and then back to NR is not considered in the context of continuity of QoE measurements during intra-5GC inter-RAT HO.
HO from LTE/5GC to NR can be supported without introducing any new IEs.
Impacts and dependencies on other WGs
How to handle the MBS QoE configuration retrieve when UE switches from RRC_IDLE to RRC_CONNECTED depends on SA2 and RAN2 reply.
Discussion on threhosld-based trigger depends on RAN2 and SA4 progress.
Discussion on assistance information depends on SA5 response.
Next steps
Whether the slice scope for multicast, area scope, and/or MDT alignment is needed in new gNB.
Further discuss the MBS QoE issues based on rely LS from other WGs.
Further refine the procedures and IEs for MN and SN coordination in NR-DC.
Further discuss the procedure used for DU to deactivate RVQoE reporting over F1AP
Discuss other issues, considering the progress of other realted WGs.

## Slide 13: R18 AI RAN WI
Progress in the last quarter
Timing Info:
  The encoding of Requested Prediction time as Integer with maximum value as 60 seconds with extensible IE structure.
  The prediction in each DATA COLLECTION UPDATE message is generated at a requested prediction time by shifting by the existing reporting periodicity.
Load Balancing:
  Introduce cause value(s) indicating failures due to timing issues.
  A new IE is introduced in the Data Collection Request, indicating the Reporting Duration for the UE Performance Feedback, starting at successful Handover Execution. Any UE Performance Feedback reporting should occur no later than the expiration of the Reporting Duration.
  Periodic and one time UE Performance Feedback Reporting are supported.

## Slide 14: R18 AI RAN WI
Progress in the last quarter
Mobility Optimization:
  The measurement object to request the report of the UE Trajectory IE should be introduced in the Report Characteristics IE included in the DATA COLLECTION REQUEST message.
  The AI/ML Measurement ID in HANDOVER REQUEST from source gNB is reused to trigger the target node feedback the UE trajectory information to the source gNB.
  The Measured UE Trajectory reporting is one-time report.
  Report time duration and configured number of intra-NG-RAN node inter-cell handovers are included in DATA COLLECTION REQUEST message.
Energy Saving:
  Define the Energy Cost IE as an INTEGER (0..10000,…), it can be revisited based on reply from SA5.
  Work on the measured EC transmission from gNB-DU to gNB-CU over F1 in R18.
Next steps
Continue to finalize the stage2/stage3 normative work.

## Slide 15: R18 mobile IAB WI
Progress in the last quarter
Agree the 38.401 TP for ST2 procedure of Xn-based consecutive mIAB-MT migration.
For the case of DU migration, F1AP signalling from the target logical mIAB-DU is selected for providing the gNB-ID of the mIAB-MT’s CU to the target mIAB-DU’s CU. Option B will be considered as baseline for transferring of remaining information i.e. the ID of the IAB MT.
New class 2 non UE associated procedures are used for the triggering of F1 setup for the purpose of DU migration and/or for the reporting of the outcome of the F1 Setup procedure for the target logical DU.
The following WA is turned into an agreement: “As an enhancement to legacy handovers, the IAB-node may provide to the source DU’s CU a mapping between the source DU’s activated cells and the target DU’s activated cells so that the source DU’s CU can perform handover for the connected UEs. This agreement does not relate to the configuration sharing between two logical collocated mIAB-DUs.”
It is agreed that a Mobile-IAB indication is included in the NGAP Initial UE message.
Agree to introduce a Mobile-IAB-authorization status indication in the Path Switch Request Ack for the mIAB-MT.
Agree that the mIAB-DU’s CU to be informed about the mIAB-authorized status by mIAB-MT´s CU when IAB MT and IAB DU connect to different IAB donor CUs.
In case the mIAB-DU’s CU obtains “non-authorized” indication for the mIAB-node, it performs an orderly F1 release.
Agree the stage 3 TP to 38.413 for Mobile-IAB indication/Mobile-IAB-authorization status indication.
Agree the stage 3 TPs to 38.473 for F1 setup trigger/report and transfer of gNB ID of MT CU.
Next steps
Continue to work on stage 2 and stage 3.

## Slide 16: R18 Mobility Enh. WI
Progress in the last quarter
LTM
  A new Class-2 procedure is introduced to notify gNB-CU about the LTM cell switch
  The gNB-CU uses the UE Context Setup procedure to collect the TCI state configurations of candidate cells in LTM configuration phase for inter-DU LTM.
  After LTM configuration, the gNB-CU indicates the collected TCI state configurations of candidate cells to the source gNB-DU and all candidate DUs via UE Context Modification procedure for the UE.
  The LTM Cell Change Notification procedure is reused to transfer the selected beam from the source gNB-DU to the target gNB-DU via gNB-CU.
  CU shall send the TA value to the source DU.
  For inter-gNB-DU LTM, the RS configuration needs to be sent from C-DU to S-DU via CU.
  The gNB-CU uses the UE Context Modification Request procedure to transfer the RS configuration of candidate cells to the source gNB-DU and/or other candidate gNB-DUs to generates the L1 configurations.
  In inter-DU LTM, the gNB-CU provides the CFRA resource received from the candidate gNB-DU to the source gNB-DU via UE Context Modification procedure.
  How the source DU detect failure of TA info acquisition is up to implementation (eg., based on timer in source DU).
  Source DU is in charge of checking the TA validity.
  In case that L3 handover is triggered earlier than LTM (the gNB-DU receives the L3 handover command before LTM is triggered), L3 handover has high priority.
  In case that LTM is triggered earlier than L3 (the gNB-CU receives the LTM notify message from gNB-DU before L3 handover is triggered), LTM has high priority.

## Slide 17: R18 Mobility Enh. WI
Progress in the last quarter
Support CHO in NR-DC
  For CHO with multiple SCGs among different T-SNs, include list of info of multiple SCGs in Handover Request Ack message, This agreement can be revisited after RAN2 agreement.
  The initiating node provides “maximum number of Conditional reconfigurations to prepare” in Rel-17, “(maximum) number of Conditional reconfigurations to prepare” could be indicated.
  Enhancement of Handover SUCCESS message considering early data forwarding, to inform S-SN which PSCells/T-SN in the HO Req ACK is selected in the HO Req ACK message. T-SN ID could be enough.
  The target MN needs to know the direct path availability of S-SN<-> T-SN(existing IE) and that of S-MN<->T-SN(new IE or codepoint) in order to have correct behavior for data forwarding handling.
  The target MN needs to know whether a bearer is S-SN terminated or S-MN terminated (the target MN knows this from the RRC container).
  Introduce a new IE or a new codepoint in SN Additional Request ACK to indicate to the target MN about the direct path availability between target SN and source MN.
Subsequent CPAC
  The information of other candidate PSCells in other candidate target SNs should be provided in the SN Addition Request message/SN Modification Request message from the MN to the candidate target SNs, if RAN2 agrees.
  After CPC execution from the source SN to other SN, the MN should inform the source SN of the CPC execution and start late data forwarding.
  - Case 1: if the source SN is configured as a candidate SN for subsequent CPAC, the source SN needs to be informed.
  - Case 2: if the source SN is not configured as a candidate SN for subsequent CPAC, the source SN is released.
  The SN reconfiguration complete message is sent to the selected SN after CPC execution.
Impacts and dependencies on other WGs
More RAN2 input is expected and helpful.
Progress in the last quarter
Continue to work on stage 2 and stage 3.

## Slide 18: R18 MBS WI
Progress in the last quarter
Topic#1 : Network sharing for Broadcast
  NG-U and F1-U tunnel management impacts to NGAP (e.g., new Broadcast Session Transport procedure defined), F1AP and E1AP, for MOCN and for multiple cell-ID broadcast scenario.
  Adopt the option of Multiple F1AP contexts/messages, and multiple E1AP context/message, one per PLMN, for MOCN scenario.
  Associated session ID and MBS service area should be introduced in E1AP for shared NG-U termination scenario.
  with agreed BLCR and TPs.
Topic#2 : Multicast reception for UE in RRC_INACTIVE
  Introduce Multicast CU to DU RRC Information IE in F1AP Multicast Context Setup/Modification Request message which includes PDCP configuration and (multicast specific) mtch-neighbourCell
  gNB-CU indicates Multicast session status (active, deactivated) to gNB-DU via F1AP Multicast Context Setup/Modification Request messages.
  CU/CU-CP makes the final decision on whether to enable/disable “Inactive reception” mode for specific multicast session.
  An indication should be introduced in F1AP Group Paging message to inform DU that inactive reception is allowed for this MBS session and thereby DU could notify UE via Uu Group Paging message.
  with agreed BLCR and TPs

## Slide 19: R18 MBS WI
Impacts and dependencies on other WGs
Further work might depend on SA2 and RAN2 progress.
Next steps
MRB-PDCP-ConfigBroadcast for multiple cell-ID broadcast scenario.
Procedure and message for the PTM configuration from the gNB-DU to enable UEs being configured with the PTM configuration before moving the UE to RRC_INACTIVE
FFS on the aspects of enabling/disabling “Inactive reception” mode (e.g. per cell, per DU, per session, per UE, etc.) and whether additional assistance information is needed from DU to CU to make decision on activation of “Inactive reception” for specific multicast session.
Whether and how to support “temporary no data” and “DL data arrival” from CU-UP to CU-CP for multicast session. FFS on whether to introduce a new procedure. To be discussed sin TEI17 first, then check whether the issue and solution in TEI17 apply in R18.

## Slide 20: R18 Sidelink Relay WI
Progress in the last quarter
RAN3 needs to enhance “5G ProSe authorised” information in Xn/F1/NG to include authorization for L2 U2U relay operation.
RAN3 agrees on proactive Data forwarding from source gNB to target gNB.
  WA: RAN3 agrees to limit mode 1 resource allocation scheme for U2N remote UE under only in intra-DU scenario under multi-path relay.
Next steps
  FFS on E1 impact to support D5.
  Check with SA2 (possible via an LS) to get feedback related to the handling of the UE location information in the multi-path operation.
  Discuss which node to decide the DL RRC messages sent over split SRB is transmitted over the direct path or the indirect path.
  Whether to reuse the existing SpCell ID for path addition in the F1AP signaling
  Setup the tunnels for different paths, focus on stage-3 details
  How to support and capture Scenario 2 in the BL CRs, e.g., stage-3 details
  Continue working on path addition/release

## Slide 21: R18 NR NTN WI
Progress in the last quarter
Providing the target cell’s servingCellConfigCommon to the source cell is not supported in Rel-18 timeline.
Turn WA to agreement: It’s un-necessary to exchange multiple TACs over Xn for NTN.
No specification impact on TACs exchange.
HO cancel is applicable to CHO with time condition over Xn.
No further discussion on the issue whether the location verification can be performed in parallel with UE service.
Next steps
Whether LMF is configured with the satellite information without any impact on RAN3 or with NRPPA changes depends on RAN1 progress.

## Slide 22: R18 IoT NTN WI
Progress in the last quarter
Add the handover window start and duration IEs to S1AP Source eNB to Target eNB Transparent Container IE.
Enhance the early data forwarding with data discarding for S1 HO, i,e. Introduce the DL Discarding IE in eNB Early Status Transfer Transparent Container IE.
When time-based trigger condition is used, the source eNB should consider the time indicated to the UE to decide when start the early data forwarding to the target eNB.
Other stage 2 and stage 3 alignment with NR NTN.
Next steps
Continue to align with the progress in NR NTN WI.

## Slide 23: R18 NR MT-SDT WI
Progress in the last quarter
DL SDT Data Size threshold shall be introduced in E1: Bearer Context Setup/ Modification message.
If the amount of the received DL SDT data is above the threshold provided by gNB-CU-CP, the gNB-CU-UP shall send DL DATA NOTIFICATION message with the SDT volume threshold crossed indication. The gNB-CU-CP may terminate the ongoing SDT procedure.
When a DL non-SDT data is coming, the gNB-CU-UP shall send R17 DL DATA NOTIFICATION message, with legacy IE (i.e., excluding R18 MT-SDT Information IE, not introducing a new IE). The behavior shall be clarfied in R17 stage 2 specification.
Agree to add “Corresponding to the SDAP SDU size of the received DL data” in Semantics Description of 9.3.1.xxx MT-SDT Information.
Next steps
The R18 NR MT-SDT WI is completed in RAN3.

## Slide 24: R18 NR Redcap Enhancement WI
Progress in the last quarter
Topic#1 : MT-communication Handling
  Introduce a new IE NR Paging Long eDRX Information for RRC INACTIVE IE including two mandatory present IEs
  Rename into UE Reachability Indication IE the HLCom Deactivate IE, keep same encoding
Topic#2 : DL Data Notification
  Agree renaming of procedure to “RAN Paging Request”
  Introduce an explicit indication DL Signaling IE ENUMERATED (true,…) to differentiate DL signaling and DL data in the DL DATA NOTIFICATION message.
Topic#3: Signaling of RRC Inactive long eDRX over XnAP and F1AP
  Keep the existing NR Paging eDRX Information for RRC INACTIVE IE as it is, remove added changes in the BL CR.
  Define new NR Paging long eDRX Information for RRC INACTIVE IE
  WA: the Rel-18 long eDRX info is signalled to DU
Topic#4: NR eRedCap Indication
  Introduce a new eRedCap Broadcast Information IE in XnAP and F1AP Served Cell Information NR IE
  FFS how to indicate HD-FDD allowed-bit indication for Rel-18 eRedCap UE
  For F1AP, introduce NR eRedCap UE indication IE to the F1AP: INITIAL UL RRC MESSAGE TRANSFER message for the early identification(s).
Impacts and dependencies on other WGs
Further work might be depended on SA2 reply and RAN2 progress.
Next steps
Continue to work on stage2 and stage3.

## Slide 25: R18 Positioning WI
Progress in the last quarter
WA: LMF provides the validity area as a list of cells, and SRS recommendation to the serving gNB. The serving gNB replies with a single SRS configuration (as in legacy positioning information exchange procedure).
Initial normative work to support additional reporting granularity, carrier phase positioning, SRS bandwidth aggregation.
Impacts and dependencies on other WGs
Wait for RAN1/RAN2 further progress
Next steps
Further discuss the signaling flow of LHPAP.
Continue to finalize the normative work based on RAN1/RAN2 progress.

## Slide 26: R18 NR Network ES WI
Progress in the last quarter
Introduce a new cause value “SSB not Available” in XnAP and F1AP to indicate that none of the requested SSB beam(s) can be successfully activated.
Maximum SSB areas is 64
In F1AP BLCR, keep the criticality “reject” for the SSBs within the cell to be Activated List IE included in the GNB-CU CONFIGURATION UPDATE message, and remove the FFS.
Take the texts in the SoD as baseline, and send the draft reply LS to SA2 in Oct. meeting when we receive RAN2 reply LS.
Working assumption: To support CN paging enhancement, the recommended SSB list for Paging could be transferred in the NGAP UE context release complete message, and sent back in the NGAP Paging message in the transparent container
WA: Support the exchange of the Cell DTX/DRX configuration over Xn.
Impacts and dependencies on other WGs
Further work on cell DTX/DRX depends on RAN2 progress.
Support on CN paging enhancement depends on RAN2 reply.
Next steps
Further discuss the sub-topics above and work on stage 2 /stage 3.

## Slide 27: R18 NR XR WI
Progress in the last quarter
Add the PDU Set QoS Parameters in the QoS Flow Level QoS Parameters IE over NGAP, XnAP, F1AP and E1AP.
The PDU Set QoS parameters includes:
  PDU Set Delay Budget (PSDB).
  PDU Set Error Rate (PSER).
  PDU Set Integrated Handling Information (PSIHI).
PDU Set Information as below needs to be transferred over NG-U, Xn-U and F1-U:
  PDU Set Sequence Number.
  Indication of End PDU of the PDU Set.
  PDU Sequence Number within a PDU Set.
  PDU Set Size in bytes.
  PDU Set Importance, which identifies the relative importance of a PDU Set compared to other PDU Sets within a QoS Flow.
End of Data Burst information needs to be transferred over NG-U, Xn-U and F1-U.
Next steps
Continue to work on stage 2 and stage 3.

## Slide 28: R18 eNPN WI
Progress in the last quarter
Add the Selected NID in S-NODE ADDITION REQUEST and S-NODE MODIFICATION REQUEST in XnAP.
Set the criticality of the Equivalent SNPNs IE to “reject” in NGAP and XnAP.
Impacts and dependencies on other WGs
The R18 eNPN WI is completed in RAN3.

## Slide 29: R18 TRS and URLLC WI
Progress in the last quarter
The (NGAP) TIMING SYNCHRONISATION STATUS REPORT message includes the RAN Timing Synchronisation Status IE and the RAN TSS Scope IE (indicating whether the scope of the RAN TSS is “all cells within a single gNB” or “list of Cell IDs within a single gNB”). The detail IE design needs to be further discussed.
Confirm the WA as agreement - When Clock Quality Detail Level IE has value “clock quality metrics”, all clock quality metrics supported by the gNB implementation are delivered to the UE.
The gNB is responsible for determining whether to provide clock quality information to the UE. In cases of CU/DU split, this decision is made by the gNB-CU.
Agree TPs for TS 38.401/38.413/38.473 to introduce a new Timing Synchronisation Status procedure (class 1) to enable the AMF/gNB-CU to initiate RAN TSS reporting by the gNB/gNB-DU.
Impacts and dependencies on other WGs
Discussion on integration with TSN may depend on SA2 progress
Next steps
Continue to discuss the RAN impact of TSN network.
Continue to work on stage 2 and stage 3.

## Slide 30: R18 RAN Slicing WI
Progress in the last quarter
For RAN impact on Partially Allowed NSSAI:
  Add the Partially Allowed NSSAI in corresponding NGAP messages.
  The total number of allowed/partially allowed S-NSSAI should not exceed 8.
Impacts and dependencies on other WGs
Stage 2 update can be wait for SA2’s response.
For NGAP, whether to signal both original slice and alternative slice (replaced slice) is still open.
Next steps
Continue to discuss the RAN impact and the corresponding standardization work.

## Slide 31: TEI Corrections
Progress in the last quarter
Correction on semantics description:
  Routing ID over NG
  UDC Parameters over E1
IE tabular ans ASN.1 alignment:
  CHO Information over X2
  PRS CONFIGURATION REQUEST message over F1
  TAI in QoE over Xn/X2
  Boradcast relate messages over NG
  Shared NG-U Multicast TNL Information over NG
  MBS Session Forwarding Adress over E1
  Mobility Information over NG
Corrections to NR MBS:
  MBS Distribution setup procedure and condition of successful MBS Broadcast Context Setup to F1AP, and location Dependent Service impacts to NGAP in TEI17
  LS approved to SA2 on MBS broadcast reception for RedCap UEs.
Corrections to NR IAB:
  Addition of IAB authorized info in NGAP path switch request ACK message
  Correction on IAB bar configuration
  Correction on BH information for DRBs support CA based duplication

## Slide 32: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and all the support during the meeting!
  Help to organize "RAN3 Friday Wow Party" after the meeting has closed for celebration and relaxing in the meeting room!
Seonggu (RAN WG3 Secretary)
  For impressive hard work and kind support!
Man, Georg, Yazid, Sean, Mingzeng
  For their positive and hard work on moderating some tough email discussions and good support!
All Rapporteurs and moderators
  For their efforts to R18 WIs/SIs and R17/R18 TEI corrections!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!