## Slide 1: Form factor considerations for XR devices
Futurewei Technologies, Inc.
3GPP TSG RAN Meeting #101
Bangalore, India, September 11 – 15, 2023
Agenda Item: 9.3.2.9
RP-231597

## Slide 2: Agreement in RP-230740 (RAN#99/March 2023)
Step-1: Recognize that form factor limitations of a subset of XR devices can make it impossible for these devices to support 4 antenna ports
  Exact characterization and form factor limitations of these devices are to be studied in RAN plenary. Contributions are invited to TSG-RAN#100 to address this.
Step-2: Contingent on the outcome of the Step-1: Recognize the importance of identifying these devices in the network, and potential network impact (e.g. performance, coverage, capacity) and UE impact
  Details of Step-2 will be further defined following the maturity of Step-1

## Slide 3: Agreement in RP-231483 (RAN#100/June 2023)
Handheld smartphone devices are excluded from any 2Rx relaxation for XR wearables.
Possible candidate options for characterization of non-RedCap XR devices to which a 2-Rx relaxation could apply, including, but not necessarily limited to:
Type of device:
  (see TR26.928), e.g. [glasses, other XR wearables (further definition required)]
  E.g. devices that are supported by ears and/or nose without straps over or behind head?
Rx-chain-usable volumetric measure:
  E.g. smaller than a benchmark of approx. [derived from volume of a smartphone?]
    Consider how to take into account volume that is not available for Rx-chain use
Rx-chain-usable surface area measure:
  E.g. smaller than a benchmark of approx. [derived from surface of a smartphone?]
    Consider how to take into account surface area that is not available for Rx-chain use

## Slide 4: Our Mission in RAN#101
Decide what is “Impossible”?
  Step 1 requires a characterization of devices such that either
    A subset of device types (e.g., glasses, but not other types) are considered “impossible” for 4RX
    A characteristic value (e.g. surface area of X cm2) is defined below which is considered “impossible” for 4RX
In this contribution we discuss device types and propose to move to step 2 at least for the glasses type of XR device
  Target is rel-18
  Can continue to discuss other types and characteristic values in parallel

## Slide 5: Devices and form factors (TR26.928)
Most devices are clearly POSSIBLE
  Smartphones, OR
  Large goggle/headset form factor, OR
  Not optical see-through ( more surface area)
Some may be IMPOSSIBLE
  “AR wearable glass standalone” (XR5G-A4)
  “Smart AR wearable glass wireless” (XR5G-A5)
  Optical see-through
Figure 4.8-1: XR Form Factors

## Slide 6: Glasses vs Goggles
Personal Protective Equipment (PPE) differentiates glasses and goggles
  Glasses have gaps with the face and are (typically) supported by a nose bridge and arms. (Straps are optional). Safety glasses have side shields.
  Goggles fit flush with the face and have straps. (Prescription glasses may even be able to fit under the goggles).
Observation: Goggles may be large enough to support 4RX
Observation: Glasses might not be able to support 4RX
Notes: https://www.elcosh.org/document/4152/d001457/EYE+PROTECTION%253A+A+BASIC+UNDERSTANDING+OF+THE+OSHA+STANDARD.html
https://www.safeopedia.com/what-is-the-difference-between-safety-glasses-and-goggles/7/1177

## Slide 7: Resolution for step 1 at RAN#101
Proposal
  Move to step 2 at least for the glasses type of XR device with a target of Rel-18
    Optical see-though
    Have gaps with the face
    Supported by a nose bridge and arms (straps are not necessary)
  Other types and/or characteristics may be further discussed
Note
  No definition of glasses will be 100% perfect, as long as most of the potential market is covered it should be OK
  i.e. “rec-specs” (protective glasses with no arms and a strap) will be considered goggles