## Slide 1: Proposals on Rel-19 RAN4-led SI/WI

## Slide 2: Topics on RF Enhancement
Further RF enhancement for sidelink
  PC3 SL-U
  Intra-band con-current operation of NR-U and SL-U @ Un-licensed band
  3Tx for inter-band con-current operation w/ sidelink
  4Tx for sidelink
FR2 RF enhancement
  Inter-band UL CA in FR2-1 based on CBM
  UL256QAM for frequency > 45GHz FR2-1
New frequency range
  Study feasibility on the upper-mid band (e.g., 7-24GHz frequency range)
  Study feasibility of sub-THz frequency (e.g., 100-275GHz frequency range)

## Slide 3: Topics on RRM Enhancement
RRM Enhancement in FR2
  RRM requirement enhancement with multi-Rx activation in FR2
    RRM requirements for Inter-cell based mTRP scenario
    RRM requirements for non-mTRP scenario
  RRM requirements in inter-band CA based on CBM
Measurement Gap Enhancement
  Independent measurement gap configuration for DC (PCell and PSCell)
    EN-DC, NE-DC, NR-DC scenario for FR1 and FR2
  Overhead reduction for multiple types of measurement gap
  Leftover issues for Rel-18 NR_MG_enh2

## Slide 4: Further RF enhancement for sidelink
Motivation
  PC3 SL-U
    In Rel-18, due to lack of time, only power class 5 is specified in SL-U.
    PC3 SL-U is agreed to be specified in future release.
  Intra-band con-current operation of NR-U and SL-U @ Un-licensed band
    In Rel-18, NR-U has been specified and SL-U is being specified in un-licensed band (n46, n96, n102)
      NR-U : PC3(Rel-18), PC5(Rel-17)
      SL-U : PC5
    In Rel-17, NR V2X intra-band con-current operation on a licensed band was specified.
    On a un-licensed band, SL-U con-current operation with NR-U needs to be specified.
    This could be discussed under spectrum work item.
  3Tx for inter-band SL con-current operation
    In Rel-18, 3Tx with two bands for inter-band UL CA or EN-DC is being specified for high power UE, such as power class 2 and 1.5
      PC3 FDD(1Tx) + PC3/PC2 TDD(2Tx)
      PC3 TDD(1Tx) + PC2 TDD(2Tx)
      PC3 FDD(1Tx) + PC1.5 TDD(2Tx)
    The existing requirements of inter-band SL con-current operation were specified as follows with limitation of PC3 on Uu.
      PC3 FDD/TDD NR (1Tx) + PC3 TDD NR SL(1Tx)
    3Tx with two band for inter-band SL con-current operation needs to be specified
  4Tx for SL
    In Rel-18, 4Tx RF requirements is being specified for high power UE, i.e, power class 1.5
    The existing SL requirements were specified with power class 3 and power class 2.
      To enhance SL communication range, the higher power class is required.
    Power class 1.5 can be implemented by 4Tx (4x23dBm)
Annex

## Slide 5: Further RF enhancement for sidelink
Objective
  PC3 SL-U
    Specify PC3 SL-U RF requirements.
  Intra-band con-current operation of NR-U and SL-U @ Un-licensed band
    Specify RF requirements for SL-U intra-band con-current operation with NR-U on un-licensed band (n46, n96, n102)
      PC5 NR-U + PC5 SL-U
      PC3 NR-U + PC5 SL-U
      PC5 NR-U + PC3 SL-U
      PC3 NR-U + PC3 SL-U
  3Tx for inter-band SL con-current operation
    Study and specify RF requirements for inter-band SL con-current operation with 3Tx for two band as follows
      PC3 TDD NR (2Tx, UL MIMO) + PC3 TDD NR SL(1Tx)
      PC2 TDD NR (2Tx, UL MIMO and TxD) + PC3 TDD NR SL(1Tx)
      PC3 TDD NR (1Tx) + PC2 TDD NR SL(2Tx, UL MIMO)
      PC3 FDD NR (1Tx) + PC3 TDD NR SL(2Tx, UL MIMO)
      PC3 FDD NR (1Tx) + PC2 TDD NR SL(2Tx, UL MIMO and TxD)
  4Tx for SL
    Study and specify UE RF requirements for 4Tx SL
Annex

## Slide 6: FR2 RF enhancement
Motivation
  Inter-band UL CA in FR2-1 based on CBM
    So far, inter-band UL CA in FR2-1 has been specified based on IBM (independent beam management) even though discussing CBM based UE in earlier release.
  UL256QAM for frequency > 45GHz in FR2-1
    In Rel-18, UL 256QAM is specified for 28GHz and 39GHz in FR2-1.
Objective
  Inter-band UL CA in FR2-1 based on CBM
    Specify CBM based inter-band UL CA in FR2-1
  UL256QAM for frequency > 45GHz in FR2-1
    Study feasibility considering advanced RF technology and specify UL256QAM requirement for frequency > 45GHz in FR2-1
Annex

## Slide 7: New frequency range : upper-mid band
Motivation
  In Rel-16, study item for 7.125 – 24.250 GHz frequency range was performed
    The study did not reveal any blocking points for introducing the NR technologies to the frequency range between 7.125-24.250GHz
    Work item that develop the requirements for selected band(s) within the range can be started based on industry needs and proposals
  RAN4 should update the earlier study with focus on changes in regulative landscape and improvements in RF technology
Objective
  Update the regulatory landscape in 7-24GHz frequency range
  Co-existence study if needed
  Update the RF technology considerations
    BS aspects
    UE aspects
Annex

## Slide 8: New frequency range : sub-THz
Motivation
  The demand of hyper-immersive media communication is growing
    Hologram : Hundreds of Gbps, UHD-XR: > 1Gbps
  Sub-THz radio communication gives a strong potential for wider BW provisioning and can achieve low OTA latency.
  The system level demonstrations for sub-THz are successfully performed by industries/academics.
  Candidate bands (GHz)
    102 ~109.5, 140~147, 151.5 ~ 164, 167 ~174.8, 191.8 ~200, 209 ~226, 252~275
Objective
  Study the regulatory aspect and RF feasibility in sub-THz communication
    Study the spectrum regulatory and define the candidate bands
      1st priority candidate bands(GHz): around 150GHz
    Co-existence study if needed
    RF feasibility
      Common issues for UE and BS
      RF feasibility study from UE/BS perspective (e.g. reference architecture, Tx/Rx characteristics)
Annex
Example of RF implementation in sub-THz

## Slide 9: RRM Enhancement in FR2: Multi-Rx activation
Motivation
  In FR2, RRM requirements such as evaluation, detection, measurement delay that take into account Rx beam sweeping cause longer latency.
    Rx beam sweeping factor N = 8 for FR2-1, and N = 12 for FR2-2
  In Rel-18, RAN4 is discussing RRM requirements for simultaneous reception using multi-panels from mTRP based on Rel-17 group-based L1-RSRP measurement and report in FR2 with limited scenario
  It is expected enhanced RRM requirements with multi-panels activation to receive signal in FR2
    E.g., Handover, SCell activation, L3 measurement requirements, inter-cell based mTRP, etc
Objective
  Study and specify RRM enhancement for mTRP scenario in FR2
    L3 measurements related requirements for intra-cell based mTRP
    RRM requirements for inter-cell based mTRP
  Study and specify enhanced RRM requirements with multi-panel activation under non-mTRP scenario in FR2 (e.g., FR2-1 and FR2-2)
Annex

## Slide 10: RRM Enhancement in FR2: Inter-band CA CBM
Motivation
  RAN4 only considered RRM requirements based on IBM (independent beam management) in inter-band CA
  CBM based inter-banc CA related RRM works for FR2-1 was dropped due to no RF requirements of CBM based inter-band CA even though discussing CBM based UE in earlier release.
Objective
  Specify RRM requirements in inter-band CA based on CBM for FR2-1
Annex

## Slide 11: Measurement Gap Enhancement
Motivation
  Maximum 2 MGs are supported for UE not supporting per-FR gap and for UE supporting per-FR gap.
  For Dual-Connectivity mode, it is not efficient in aspect of measurement period due to MG sharing between PCell and PSCell.
    In EN-DC
      per-UE gap and FR1 gap are configured by MN
      FR2 gap is configured by SN
    In NE-DC and NR-DC
      per-UE gap, FR1 gap, and FR2 gap are configured by MN
  Multiple types of measurement gap would be impact on throughput. Further consideration for overhead reduction of multiple types of measurement gap configuration should be studied.
  Leftover issues in Rel-18
Objective
  Study and specify RRM requirements related to the concurrent MG configured independently per PCell and PSCell in DC mode
  Study and specify RRM requirements to reduce measurement gap overhead by multiple types of measurement gap configuration
  Leftover issues in Rel-18
Annex