## Slide 1: On Multi-Carrier Enhancements in Rel-19
RP-231754
3GPP TSG RAN Meeting #101
Bangalore, India, 11th – 15th September, 2023
Agenda Item 8A.2.12.2
Source: Nokia, Nokia Shanghai Bell

## Slide 2
Background
MC Enhancement in Rel-18 – two objectives
Multi-cell scheduling with a single DCI
Multi-carrier UL operation
  UL Tx Switching across 3 or 4 bands
  Support for multiple TAG configurations with UL Tx Switching
MC Enhancements in June/2023 Workshop
  The proposed areas for possible enhancements are quite diverging and wide
  Careful examination is necessary in terms of real commercial needs
1. Specify a solution for multi-cell PUSCH/PDSCH scheduling (one PDSCH/PUSCH per cell) with a single DCI [RAN1]
Identify the maximum number of cells that can be scheduled simultaneously
Consider both intra-band and inter-band CA operation
Consider both FR1 and FR2
The single DCI shall be optimized for 3 or more cells for the multi-cell PUSCH/PDSCH scheduling
2. Study and if necessary specify following enhancements for multi-carrier UL operation [RAN1, RAN2, RAN4]
UL Tx switching schemes across up to 3 or 4 bands with restriction of up to 2 Tx simultaneous transmission for FR1 UEs, including mechanisms to enable more configured UL bands than its simultaneous transmission capability and to support dynamic Tx carrier switching across the configured bands for both single TAG and multiple TAGs configurations (RAN1, RAN4)
  UE capability and RRC configuration related signalling (RAN2)
  Note: strive for RAN1/2 design agnostic with the number of bands, i.e., common design between 3 and 4 bands
  Note: no additional TAG is introduced for UL transmission on a carrier without corresponding DL carrier
  Note: this objective does not target to extend the SUL framework to support more than 1 SUL for 1 NUL
  Note: The number of TAGs is limited to up to 2.
  Note: Extension of TX switching for 2 bands to multiple TAG configurations is included in the scope. The work is limited to RAN4.
Switching time and other RF aspects, and RRM requirements for above UL Tx switching schemes across up to 3 or 4 bands (RAN4)
  Note: Prioritize UL Tx switching across up to 3 bands is to be addressed first and then that for up to 4 bands can also be addressed
[RP-222251]

## Slide 3
Potential considerations for Rel-19
June workshop 1): The proposed areas for possible enhancements are quite diverging and wide
June WS did not reveal an obvious primary candidate or candidates for the WI scope
Potential objectives that could be considered for the Rel-19 MC Enhancements WI
  Multi-cell scheduling enhancements (leftovers of Rel-18 multi-cell scheduling objective)
    Allowing cells scheduled by another cell with multi-cell DCI to also self-schedule would make the multi-cell scheduling DCI mode deployable. This would be a straight-forward continuation of the Rel-18 work
  Uplink-only Secondary Cell
    DL-only SCell is The Basic Building Block of carrier aggregation
    UL-only SCell would complete the CA framework and enable flexible DL/UL association
June workshop 2): Careful examination is necessary in terms of real commercial needs
Scope fitting to 1 TU allocation for RAN1/RAN4 should be the goal
Inclusion/Exclusion of this WI to R19 needs to be considered together with all other WI candidates