## Slide 1: Discussion on scope of Rel-19 XR enhancement
Bangalore , 11-15 September, 2023
3GPP TSG RAN Meeting #101
RP-231761
Agenda Item: 8A.2.8
Source: Xiaomi
Document for : Discussion and decision

## Slide 2: Discussing on scope of Rel-19 XR enhancement(1)
  New use cases/scenarios (e.g., multi-modality interactions, XR, Metaverse, etc) addressing coordinated parallel transmission impose new requirements for 5G system.
      Multi-modal Data consists of more than one Single-modal Data, and there is strong dependency among each Single-modal Data. Similar as multi-modality communication services as XR, Metaverse services would involve coordination of input data from different devices to enable immersive remote collaboration.
  SA2 progress:
      TS 22.261 has documented a synchronization threshold;
      a Multi-modal Service ID has been introduced for multiple IP data flows associated to a multi-modal service;
      =>Xiaomi’s view:
      To support Multi-modality and Metaverse, RAN is kindly requested to consider coordinated parallel transmission(based on SA2’s inputs);
      Study and specify the control plane procedure design for coordinated parallel transmission, including coordinated RRC connection management from the UE device(s);
      Study and specify the user plane procedure design for coordinated parallel transmission, including coordinated scheduling to fulfil the QoS coordination, traffic synchronization from the UE device(s) .

## Slide 3: Discussing on scope of Rel-19 XR enhancement(2)
  In Rel-18, RAN2 introduced DSR reporting while the delay information is additionally reported to the network in order to request the uplink scheduling in time. However, with current LCP procedure, the LCG that triggered DSR can still not be prioritized and lead to long queueing delay and packet discarding;
  For PDCP, the transmitting PDCP entity performing PDCP duplication for PDUs of certain type(s) of PDU Set (e.g., inferred from the PDU Set Importance) while not performing PDCP duplication for PDUs of other types will ensure reliable transmission of the PDU set with high importance and save the radio resource when in presence of congestion;
  In current PDCP spec, the receiving PDCP entity only triggers status report mostly for AM mode on a PDCP entity re-establishment or a PDCP data recovery or uplink data switching. We can further study whether the transmitting PDCP entity needs to get the delivery status more timely for PDU set discarding.
  UTO-UCI should be extended to multiple CG configurations in Rel-19 XR WI for the following reasons:
      XR traffic can be configured to map to Multiple CG configurations
      Possibility for earlier indication of the unused CG PUSCH occasions
      Possibility to indicate unused TO for the first CG PUSCH occasion of a CG configuration.
      =>Xiaomi’s view:
      To further study the enhancements related to capacity, RAN is kindly requested to consider LCP enhancement for UL delay-aware scheduling and PDCP enhancement;
      For the enhancements related to capacity, RAN is kindly requested to consider UTO-UCI for multiple CG configurations.

## Slide 4: Discussing on scope of Rel-19 XR enhancement(3)
  In Rel-18, RAN2 considered PDU Set of different importance in a single DRB can be mapped to multiple RLC/LCH and was excluded based on SA2’s assumption that different types of PDU set sharing the same PDU set QoS parameters (and other QoS characteristics, e.g. 5QI, ARP) in the same QoS flow.
  Currently, SA2 is considering QoS handling enhancement for XRM services in 5GS XRM Ph2, e.g., study whether and how enhancements can be done for traffic detection and QoS Flow mapping for multiplexed data flows (different media types multiplexed within the same 5-tuple traffic flow).
      =>Xiaomi’s view:
      For the enhancements for XR Awareness, RAN is suggested to consider QoS handling enhancement for XRM services based on SA2’s new requirement, e.g., split bearers based on PDU Set Info to further improve QoS handling.

## Slide 5: Discussing on scope of Rel-19 XR enhancement(4)
  XR power saving is essential for XR equipment and has clear commercial prospects.
  XR power saving techniques are extensively studied and evaluated in R18 XR SI. XR power saving techniques combining with C-DRX/PDCCH skipping/SSSG switching/LP WUS shows obvious power saving gains in simulation
      XR power saving combined with LP WUS shows outstanding flexibility and power saving performance.
      XR power saving for CA scenario should be supported since it is XR traffic typically has large packet size and tight transmission delay requirement.
      =>Xiaomi’s view:
      To better support XR, RAN is kindly requested to consider XR power saving.

## Slide 6: Summary
  Proposal 1: RAN is suggested to consider the following objectives for Rel-19 XR enhancement:
For coordinated parallel transmissions from UE device(s) to support Multi-modality and Metaverse (RAN2, RAN3, RAN1): Study and specify the control plane procedure, including coordinated RRC connection management from the UE device(s); Study and specify the user plane procedure design, including coordinated scheduling to fulfil the QoS coordination, traffic synchronization from the UE device(s; Further enhancements related to capacity (RAN2, RAN1): LCP enhancement for UL delay-aware scheduling; Selective PDCP duplication; PDCP control PDU for notifying about PDU discarding; UTO-UCI for multiple CG configurations. Further enhancements for XR Awareness (RAN2, RAN3): split bearers based on PDU Set Info to further improve QoS handling; Note: Need for this work task depends on SA2 Rel-19 progress. Further enhancement for power saving(RAN1, RAN2): Reduce PDCCH monitoring for CA scenario;

## Slide 7
THANKS!