## Slide 1
Discussion on multi-carrier enhancement in Rel-19 Agenda Item: 8A.2.12.2 Source: OPPO Document for: Discussion
3GPP TSG RAN Meeting #101
Bangalore, India, September 11th-15th, 2023
RP-231781

## Slide 2: R18 Multi-Carrier Scheduling
Support a single DCI scheduling multi-cell PUSCH/PDSCH
One DCI schedules PDSCHs/PUSCHs on multiple co-scheduled cells from a set of up to 4 cells that share the same SCS.
  Per RAN #97 decision, it is not supported in Rel-18 for a SCell to schedule multiple cells including P(S)Cell.
One UE can be configured with up to 4 sets of co-scheduled cells

## Slide 3: Motivations for R19 Multi-carrier Enhancements
Support more use cases than in R18
  Cells with different SCS can be co-scheduled
  PCell and SCell(s) can be co-scheduled by a SCell
  More than 4 cells can be co-scheduled

## Slide 4: Potential Enhancements for R19 Multi-carrier (I)
Co-scheduled cells with different SCS configuration
  Legacy determination of the slot allocated for PDSCH/PUSCH/PUCCH can be extended for DCI format 0_3/1_3
    PDSCH : or
    PUSCH: or
    PUCCH: PUCCH is in UL slot n+k, where is the last UL slot for PUCCH transmission that overlaps with the DL slot for the PDSCH reception

## Slide 5: Potential Enhancements for R19 Multi-carrier (II)
PCell can be configured in a set of cells which are co-scheduled by a SCell
  PCell supports self-scheduling, but does not schedule any SCell

## Slide 6: Potential Enhancements for R19 Multi-carrier (III)
Support of more than 4 co-scheduled cells with the same DCI payload size restriction as in Rel-18
  Define additional Type 1 DCI fields from Rel-18 Type 2 fields
  Compression on FDRA field

## Slide 7: Proposal
  To take into account the following for Rel-19 multi-carrier enhancements：
  The different SCS configurations across co-scheduled cells in a cell set.
  A single DCI on SCell to schedule PDSCH/PUSCH on multiple co-scheduled cells including PCell, where PCell may schedule no more than itself
  One DCI scheduling more than 4 co-scheduled cells, with the same DCI payload size limitation as in Rel-18