## Slide 1: R19 3Tx enh and antenna evaluations
OPPO 2023/09
3GPP TSG-RAN Meeting #101 RP-231786 Bangalore, India, September 11-15, 2023

## Slide 2: 3Tx background
3Tx for inter-band UL CA/ENDC was introduced in Rel-18
3Tx is supported by FWA/CPE now, and has been commercialized in serval countries. The demand for this feature is urgent in the market.
Rel-18 3Tx WI has reached good progress in defining general requirements, however, it only covers limited cases in power configurations and UE types
  Only FWA UE type
  No increased high power limit feature
  Only inter band CA/ENDC with total power class PC2/PC1.5 and limited power configurations
Band A
Band B
LO1
LO2

## Slide 3: 3Tx proposals for Rel-19
3Tx can be enhanced in Rel-19 in following aspects
For inter-band UL CA/ENDC
  Handheld UE with 3Tx can be supported in Rel-19
  Increase high power limit can be supported, e.g. PC3+PC2, PC3+PC1.5
  Introduce more power combinations, e.g.
For single CC or intra-band CA
  FWA UE type
  Introduce 3Layer UL MIMO
  Introduce 3TxD to improve UL coverage
3Tx basket WI :
To cover new band combination demands with Rel-18 power configurations in current 3Tx WID if not introduced in Rel-18
PC2 in total |  | band A 1Tx |  |  | 
 |  | FDD PC3 | FDD PC2 | TDD PC3 | TDD PC2
band B 2Tx | FDD PC3 |  |  |  | 
 | FDD PC2 | R19 |  | R19 | R19
 | TDD PC3 | R18 |  |  | 
 | TDD PC2 | R18 |  | R18 | R19
PC1.5 in total |  | band A 1Tx |  |  | 
 |  | FDD PC3 | FDD PC2 | TDD PC3 | TDD PC2
band B 2Tx | FDD PC2 | x |  | x | 
 | TDD PC2 | x |  | x | 
 | TDD PC1.5 | R18 | R19 | R19 | R19

## Slide 4: Antenna evaluation proposal 1
MSD OTA test method
MSD requirements are defined with antenna coupling interference included
In RF conduct tests the antenna coupling interference is missing which makes the conduct MSD tests doesn’t show the real MSD that UE will face in the field
The antenna coupling impact will increase when UE PCB isolation is increased, i.e. antenna coupling interference becomes the dominant factor
  Antenna coupling impact will achieve 1dB/2dB/10dB/10dB for harmonics, IMD, harmonic mixing, and cross band leakage when PCB isolation is 80dB
Proposal: Study OTA based MSD test method, e.g. EIRP or TRP based test, the impact of antenna efficiency, antenna patter, test system and test time, etc.

## Slide 5: Antenna evaluation proposal 2
NTN OTA requirements and test method
Current TRP is defined as the average of whole sphere
For NTN, UE top region antenna performance is more important than other directions
Regional antenna requirements might be more suitable in NTN to increase the UL coverage
Proposal: Study regional antenna requirements and test methods for NTN UE, e.g. CDF based requirements
This region is more important

## Slide 6
Thanks!