## Slide 1
3GPP TSG RAN #101 RP-231799
Bangalore, Sep 11-15, 2023
Source: vivo
Document for: Discussion and Decision
Agenda Item: 8A.2.12.1
Rel-19 LP-WUS/WUR (RAN1-Led)

## Slide 2
Outlines
Use Cases, RRC States Identified in SI
SI Output and Conclusion:
  Power and Latency: RRC idle/inactive, RRC Connected
  Coverage Network Overhead and Network energy
  Time and Frequency Tolerance
  LP-WUR Architecture
  LP-WUS design
  Procedure
Potential Rel-19 WID Scope

## Slide 3
Use Cases and RRC States Identified in SI
RRC states identified in SI[1]
Observation: In SI, performance evaluations are performed covering all use cases and RRC states
IoT
Wearable
eMBB
Use cases identified in SI[1]
RRC Connected state
 | Latency
RRC IDLE/INACTIVE | I-DRX use cases: in the order of seconds eDRX use cases: larger than I-DRX case.
RRC CONNECTED | Up to tens of milliseconds
  primary for small form devices
  power-sensitive
  static, nomadic or limited mobility
IOT
  primary for small form devices,
  power-sensitive
  low/medium speed, FFS: high speed
Wearable
  devices form is various and not restricted
  power-sensitive
  low/medium speed, FFS: high speed
eMBB
RRC Idle/Inactive state
[1] R1-2308729, TR38.869v040, section 5, section 9.1 Conclusion

## Slide 4
SI Output and Conclusion: IDLE/INACTIVE operation
[1] R1-2308729, TR38.869v040, section 9.1 Conclusion.
  UE power saving benefit (RAN1 conclusions [1])
  PSG for IDLE/INACTIVE:
    For I-DRX operation: Significant UE power saving gain (up to more than 90%) is observed by using LP-WUS/WUR to trigger UE MR paging monitoring compared with I-DRX operation (with and without PEI), if sufficient relaxation to MR RRM measurement is applied.
      For duty-cycled LP-WUS monitoring and same duty ratio, higher power saving gain is observed if the relative power consumption of LP-WUR ON for LP-WUS monitoring is lower.
      For continuous LP-WUS monitoring, UE power saving gain is only observed if the relative power consumption of LP-WUR ON for LP-WUS monitoring is lower, e.g. no larger than 1 unit.
    For eDRX operation: Significant UE power gain and moderate paging latency increase is observed if LP-WUS monitoring is restricted within existing PTW of eDRX and existing paging occasion determination is reused.
  Necessity of UE MR RRM relaxation and/or offloading: UE power saving gain cannot be observed if the existing Rel-18 MR RRM measurement periodicity for serving and neighbour cells are applied and UE MR enters in ultra-deep sleep during LP LP-WUS monitoring, therefore MR serving and neighbour cell measurement with further time domain relaxation than that is allowed in Rel-18 specification for IDLE/INACTIVE and/or at least serving cell RRM offloaded from MR to LR are beneficial.

## Slide 5
SI Output and Conclusion: IDLE/INACTIVE operation
UE power saving and latency
[1] R1-2308729, TR38.869v040, section 9.1 Conclusion.
  Latency (RAN1 conclusions [1])
  For I-DRX operation
    If the MR enters ultra deep sleep while monitoring LP-WUS, compared with legacy I-DRX operation with same I-DRX cycle, moderate paging latency increase (e.g. ~400ms) is observed by using LP-WUS/WUR, due to the ramp up and re-sync procedure of MR from ultra-deep sleep state and if legacy paging occasion is reused.
    From RAN1 perspective, potential techniques to decrease the latency e.g. using shorter I-DRX cycles, dynamic paging occasion determination, UE MR transmit PRACH directly after wake-up by LP-WUS, UE MR entering deep sleep during LP LP-WUS monitoring, were proposed and evaluated.
  For I-DRX operation
    Significant paging latency reduction and moderate UE power saving gain is observed, if LP-WUS monitoring and the corresponding paging monitoring after MR wake-up is performed not restricted within existing PTW of eDRX.

## Slide 6
SI Output and Conclusion: CONNECTED mode
UE power saving and capacity, UPT impacts
[1] R1-2308729, TR38.869v040, section 9.1 Conclusion.
RAN1 Conclusion[1]:
For XR traffic and LP-WUS to trigger the UE MR PDCCH monitoring, compared to existing power saving techniques
  Moderate power saving gain (up to more than 10%) for different types of XR traffic and system loads, larger UE power saving gain can be observed if the UE MR can enter light sleep instead of micro sleep during LP-WUS monitoring by LR.
  Marginal impact to XR capacity for low load case. For high load scenarios, also marginal impact to XR capacity when UE MR enters micro sleep, relatively larger when MR enters the light sleep.
For FTP and IM traffic, and for the usage of LP-WUS to trigger the UE MR PDCCH monitoring,
  Compared to existing power saving techniques
    Significant power saving gain (up to more than 60%) and UPT improvement (up to more than 10%) when MR enters deep sleep, larger UPT improvement (up to more than 180%) for IM traffic.
    Relatively lower or no power saving gain when MR enters light sleep, but UPT improvement is higher (up to 50%).
  Compared with always-on PDCCH monitoring,
    Significant Power saving gain (up to more than 40%) and similar UPT performance when UE MR enters micro sleep.
For FTP and IM traffic, For the usage of LP-WUS as the wake-up mechanism of C-DRX similar to DCP, compared to existing power saving techniques
  Significant UE power saving gain (up to more than 30%) and moderate degradation to the UPT (less than 10%) can be observed, especially when the C-DRX cycle is shorter (e.g. 40ms) .

## Slide 7
SI Output and Conclusion: Coverage
[1] R1-2308729, TR38.869v040, section 9.1 Conclusion.
Note: RedCap and non-RedCap UE cases are not further distinguished; the above OFDM symbol assumes subcarrier spacing 30kHz;
RAN 1 Conclusion[1]:
For Urban scenario and single PUSCH MSG3 transmission
  For OOK-based LP-WUS, the required resource reported is 0.9~17.28 MHz*Symbol/bit
  For FSK-based LP-WUS, the required resource reported is 4.32~25.92 MHz*Symbol/bit
  For OFDM-based LP-WUS, the required resource reported is 0.31~4.32 MHz*Symbol/bit
For Rural scenarios and single PUSCH MSG3 transmission
  For OOK-based LP-WUS, the required resource reported is 0.18~8.64 MHz*Symbol/bit
  For FSK-based LP-WUS, the required resource reported is 4.32 MHz*Symbol/bit (one source)
  For OFDM-based LP-WUS, the required resource reported is 1.8~3.6 MHz*Symbol/bit
In general, it is much more challenging for LP-WUS to reach comparable MIL as legacy PDCCH with AL16/AL8, more resources occupancy and/or coverage enhancement techniques for LP-WUS transmission would be required to reach such challenging MIL target.

## Slide 8
SI Output and Conclusion: Resource Overhead and Network Energy
System Resource Overhead (RAN1 conclusion) [1]
Network Energy Consumption (RAN1 conclusion) [1]
RRC State | Signal | MIL target | Overhead
RRC IDLE/INACTIVE (System BW: 20MHz or 100MHz ) | OOK/FSK-2 based LP-WUS, up to 24bit | single PUSCH MSG 3 | Up to 1.98%
 | OFDM based LP-WUS, up to 24bits | single PUSCH MSG 3 | Up to 0.16%
 | OFDM based LP-WUS, up to 8bits | paging PDCCH (AL8/AL16) | Up to 0.19%
 | OOK-based LP-WUS , up to 48bits | paging PDCCH (AL8/AL16) | Up to 21%
 | OOK based LP-SS (8 beams, 320ms periodicity and 1 slot time) | single PUSCH MSG 3 | 0.4%
RRC CONNECTED (System BW: 100MHz ) | OOK-based LP-WUS , up to 12bits, XR traffic with 10 UEs per cell (maximum system capacity) | unicast PDCCH AL2-4Rx | Up to 4.3%
 | OOK-based LP-WUS , up to 12 bits, FTP3 traffic with 10 UEs per cell, RU 40% | unicast PDCCH AL2-4Rx | Up to 0.36%
LP-SS configuration | Load | Additional increase NW power consumption rate
320ms LP-SS periodicity, 4 or 8 beams and no more than 14 symbols LP-SS duration | Zero | 0.06%~3.9%
 | low | 0.07%~2.716%
 | medium | 0.388%~1.076%
320ms LP-SS periodicity, 8 beams and 42 symbols LP-SS duration | Zero | 11.4%
Lower impact to the network power consumption is expected when LP-SS is transmitted FDM with NR SSB/SIB-1. |  | 
Observation
Network Overhead: LP-WUS and LP-SS has marginal impact on the system resource overhead with PUSCH MSG3 as MIL target.
Network Energy Consumption: LP-SS has marginal impact on NW power consumption.
[1] R1-2308729, TR38.869v040, section 9.1 Conclusion.

## Slide 9
SI Output and Conclusion: Time and Frequency Error Tolerance
 | OOK (OOK-1/4)[2] | FSK (FSK-2)[2] | OFDM[2]
Timing Error Tolerance | Moderate robustness <=5us for OOK-1@30kHz <=3 us for OOK-4 M=2, <=1us for OOK-4 M=4. | Moderate robustness <=2us for FSK-2 M=1, <=2/3 us for FSK-2 M=2. | Tolerance to timing error varies with sliding window size, e.g., up to 4us but requires sliding window at receiver -> increased power consumption
Frequency Error Tolerance | The most robust 800kHz for OOK-4 M=4 | Good robustness 200kHz for M=2 | Less robustness 26kHz
Comparison on OOK, FSK, and OFDM
RAN 1 Conclusion for time error tolerance [1]
RAN1 Conclusion for frequency error tolerance [1]
OOK/FSK waveform with longer time segment and with a single or multiple frequency segments is comparable (0 us) or more robust (by 4us) to timing error than waveform with shorter time segment.
OFDMA: tolerate timing error up to 4us if proper sliding window size is assumed by a receiver.
Single frequency segment OOK-1/OOK-4: the most robust waveform to frequency error.
FSK-2 : good robustness to frequency error
OFDMA waveform: less robust than OOK and FSK if assuming no frequency compensation/synchronization.
Observation: OOK (OOK-1/4) has the most robustness to frequency error, both OOK (OOK-1/4) and FSK (FSK-2) provide moderate timing error tolerance.
[1] R1-2308729, TR38.869v040, section 9.1 Conclusion.
[2] R1-2308729, TR38.869v040, section 8.3.1, section 8.3.2

## Slide 10
SI Output and Conclusion: Receiver Architecture
Power and Noise Figure
Table 4 Comparison on receiver power consumption for OOK, FSK, and OFDM reception
Receiver architectures : power consumption and noise figure
Observation: Receiver power consumption OOK ≈ FSK <OFDM
For OOK/FSK, receiver power consumption of less than 1~4 unit is feasible
For OFDM, receiver power consumption of less than 10units is not guaranteed
 | Receiver power consumption
OOK (OOK-1/4) | Lowest power consumption LP-WUR ‘On’ power <=4units, and <=1 unit is reported by majority
FSK (FSK-2) | Similar or slightly higher than OOK (Note: Some of the inconsistent ranges for the architectures for OOK and FSK is due to the fact that not all sources provided analysis for all the architectures. )
OFDM | Highest power consumption LP-WUR ‘On’ power <= 30 units, and >=10 units reported by majority
Table 1 OOK-1/2/4 with homodyne/zero-IF architecture with baseband envelope detection [1]
Table 2 FSK with parallel homodyne architecture[1]
Source reference | [7A-1] | [7A-3] | [7A-5] | [7A-6] | [7A-7] | [7A-8] | [7A-9]
Power consumption (ON state) | 0.15~0.2 | 10 | 10~20 | 10~30 | 1~5 | 10~20 | ~5
Noise figure (dB) | 15 | 9.5 | 9.5 or 12 | 9 | 7~10 | 9 | 15~25
Table 3 OFDM-based signal with time-domain correlation [1]
Source reference | [7A-1] | [7A-2] | [7A-3] | [7A-4]
Power consumption (ON state) | 0.09 for single-branch, 0.01 or 0.02 for each additional branch | 0.5 | 0.1~1 | 0.1
Noise figure (dB) | 15 | 10~15 | [10~16] | 15
Source reference | [7A-1] | [7A-2] | [7A-3] | [7A-4] | [7A-5] | [7A-6] | [7A-7] | [7A-8] | [7A-9] | [7A-10]
Power consumption (ON state) | 0.09 for single-branch, 0.01 or 0.02 for each additional branch | 0.5 | 0.1~1 | 0.1 | 0.05~ 0.5 | 0.5~1 | 0.1~0.5 | 4 | ~1 | 0.1~0.5
Noise figure (dB) | 15 | 10~15 | [10-16] | 15 | 12 | 15 | 12~15 | 15 | ~15 | 12
[1] R1-2308729, TR38.869v040, section 7.1.1a.1, 7.1.1a.2, 7.1.1a.3 .

## Slide 11
Waveform
SI Output and Conclusion: L1 Signal Design
Proposal
Specify an unified LP-WUS design applicable for both envelop detection based LP-WUR and OFDM based LP-WUR.
OOK (OOK-1 and/or OOK-4) based LP-WUS is supported for envelop detection based LP-WUR
  OFDM sequence(s) can be additionally modulated on top of OOK for OFDM based LP-WUR to achieve better detection performance
Evaluation
RAN1 studied OOK/FSK and OFDMA waveform, with LLS performance, coverage, UE power consumptions and network impact.
Comparing FSK and OOK, OOK has lower power consumption, better or similar LLS performance, less resource to achieve Msg-3 coverage target and much more input to RAN1 study for OOK [1]
OFDMA requires larger power consumption/complexity than FSK/OOK and more sensitive to timing/frequency error, while smaller overhead for similar coverage[1].
RAN1 Conclusion
RAN1 concluded sequences to generate ON duration in OFDMA transmitter, if specified, can help receiver (with I/Q branches) performance [2].
RAN1 tried to recommend ‘OFDMA waveform and OOK waveform (with or without OFDMA sequences) with OOK1/4 scheme are recommended for possible down-selection’ in RAN1 114 meeting
[1]: R1-231815, Recommendation for LP-WUS waveform
[2]: R1-2308729, TR38.869v040, section 9.3
.

## Slide 12
Bandwidth & Content
SI Output and Conclusion: L1 Signal Design
RAN1 studied bandwidth and location for LP-WUS. RAN1 recommended at least one BW size <=5MHz for idle/inactive state [1].
Bandwidth
RAN1 & RAN2 studied LP-WUS content, at least information on which user(s) is/are targeted by the LP-WUS for idle/inactive/connected mode, and indication to wake-up to PDCCH monitoring for connected mode.
RAN1 evaluated LP-WUS performance with different payloads, e.g., from 1 to 48 bits.
  To provide similar subgrouping as in R17 PEI (align with RAN2’s assumption), we suggest LP-WUS capable to carry at least 8bits (excluding CRC, if any).
RAN1 studied alternatives to carry LP-WUS content, including sequence detection/selection and encoded bits.
Content
Proposal
    Information payload carried by LP-WUS can be [1~X] bits (excluding CRC, if any), with X>=8, upper limit to be decided in WI phase
[1]: R1-2308729, TR38.869v040, section 7.2.1.2
.

## Slide 13
LP-SS
SI Output and Conclusion: L1 Signal Design
RAN1 studied necessity for LP-SS, at least for synchronization and RRM measurement for idle/inactive UE. RAN1 concluded[1]:
  At least for LP-WUR that cannot receive existing PSS/SSS (i.e envelop detector based LP-WUR), periodic LP-SS signal is beneficial for the following functionalities: (a) RRM measurements by LP-WUR, if supported, (b) At least coarse time synchronization of LP-WUR, (c) At least coarse frequency synchronization of LP-WUR.
  For LP-WUR that can receive existing PSS/SSS potentially assisted by PBCH DMRS/TRS for synchronization (i.e. OFDM based LP-WUR), existing PSS/SSS potentially assisted by PBCH DMRS/TRS may be used for above functionality.
Necessity
Studied design
Proposal
  Specify an OOK (OOK-1 and/or OOK-4) based periodic LP-SS for synchronization and serving cell measurement performed by LP-WUR, with its coverage performance no worse than LP-WUS and periodicity no less than [320ms]
  RAN1 studied signal/channel structure for LP-SS, periodicity, coverage, and content.
    RAN1 concluded periodic LP-SS coverage should be equal to or better than that of LP-WUS [1].
    RAN1 evaluated OOK-based LP-SS with periodicity of at least 320ms [2].
  Note: Since OFDM based LP-WUR can receive existing PSS/SSS to achieve LP-SS function, only OOK-based LP-SS needs specify.
[1]: R1-2308729, TR38.869v040, section 7.2.2.1
[2]: R1-2308729, TR38.869v040, section 6.2.1
.

## Slide 14
RRM relaxation and offloading to LP-WUR
SI Output and Conclusion: Procedure
Proposal
Support further RRM relaxation of UE MR for both serving and neighbor cell measurements, including the possibility of offloading MR serving cell measurement(s) to LP-WUR in Rel-19 WI
RAN1 concluded: UE power saving gain cannot be observed if the existing Rel-18 MR RRM measurement periodicity for serving and neighbour cells are applied and UE MR enters in ultra-deep sleep during LP LP-WUS monitoring, therefore MR serving and neighbour cell measurement with further time domain relaxation than that is allowed in Rel-18 specification for IDLE/INACTIVE and/or at least serving cell RRM offloaded from MR to LR are beneficial [1].
Necessity
[1]: R1-2308729, TR38.869v040, section 9.1
[2]: R1-2308729, TR38.869v040, section 9.3
.
RAN1 studied measurement metrics, and evaluated RSRP&RSRQ measurement accuracy:
  RSRP&RSRQ for LP-SS: with SNR target X= {-3, -6, -9, -11} dB, depending on 90% accuracy of 3 or 5 dB, different number symbols (1 -70) spread over 1-5 periods is required for TDL-C channel. With SNR target X= {-9, -11} dB, and depending on 90% accuracy of 3 or 5 dB, different number symbols (1 -20) spread over 1-3 periods is required for AWGN channel [2] .
  RSRP for SSS: with SNR target X= [-3, -6] dB, depending on 90% accuracy of 3dB, 1 OFDMA symbol in 1 period is required for TDL-C channel [2] .
  RAN2 studied relaxed RRM measurement on serving & neighboring cell by MR, and measurement based on LP-SS by LP-WUR
Study & Evaluation

## Slide 15
For RRC idle/inactive mode UE
SI Output and Conclusion: Procedure
Proposal
For RRC idle/inactive mode, specify necessary procedures to allow UE MR (Main receiver) paging monitoring triggered by LP-WUS including the mechanisms to activate/deactivate the LP-WUS monitoring in Rel-19 WI
RAN1 & RAN2 studied:
  LP-WUS monitoring including LP-WUS Activation and deactivation
  Fallback to legacy operation after exiting LP-WUS monitoring
  UE MR performs PO monitoring or performs PEI monitoring after detecting LP-WUS
Studied design
RAN1 evaluated LP-WUS for RRC idle/inactive mode to trigger UE MR paging monitoring. With sufficient relaxation to MR RRM measurement, RAN1 observed significant power gain for LP-WUS compared with I-DRX (details in Page 4 &5 in this slides)
Evaluation

## Slide 16
For RRC connected mode UE
SI Output and Conclusion: Procedure
Proposal
For CONNECTED mode, specify necessary procedure to allow LP-WUS monitoring by LP-WUR when MR is in sleep mode(s) except for ultra-deep sleep, and MR PDCCH monitoring triggered by LP-WUS in Rel-19 WI
RAN1 evaluated LP-WUS for RRC connected mode with different traffic types, compared with existing power saving techniques. RAN1 observed power reduction and/or UPT gain for several cases (details in Page 6&7 in this slides)
Evaluation
RAN1 & RAN2 studied:
  LP-WUS functionality/purpose
  LP-WUS monitoring including LP-WUS Activation and deactivation
  The relationship/interaction between LP-WUS and legacy UE power saving techniques
Note: RAN1 assumed RRM/RLM/BFD/CSI performed by MR & ultra sleep is not allowed for MR
Studied design

## Slide 17
Potential Rel-19 WID Scope
Specify an unified LP-WUS design that is applicable for both envelop detection based LP-WUR and OFDM based LP-WUR, and for both IDLE/INACTIVE and CONNECTED mode usage. (RAN1, RAN2)
    OOK (OOK-1 and/or OOK-4) based LP-WUS is supported for envelop detection based LP-WUR
      OFDM sequence(s) can be additionally modulated on top of OOK for OFDM based LP-WUR to achieve better detection performance
    Information payload carried by LP-WUS can be [1~X] bits (excluding CRC, if any), with X>=8, upper limit to be decided in WI phase
    LP-WUS shall be able to reach at least the coverage of existing Msg3 PUSCH (single transmission).
    It shall be possible to generate the unified LP-WUS with existing hardware from gNB transmitter perspective
For IDLE INACTIVE modes,
  Specify necessary procedures to allow UE MR (Main receiver) paging monitoring triggered by LP-WUS including the mechanisms to activate/deactivate the LP-WUS monitoring (RAN1, RAN2)
  Specify an OOK (OOK-1 and/or OOK-4) based periodic LP-SS for envelop detection based LP-WUR for synchronization and serving cell measurement purpose, with its coverage performance no worse than LP-WUS and periodicity no less than [320ms] (RAN1)
    It shall be possible to generate the OOK based LP-SS with existing hardware from gNB transmitter perspective
    For OFDM based LP-WUR, existing NR signal, e.g., SSS can be used for synchronization and measurements, instead of LP-SS.
  Specify further RRM relaxation (at least 8 times) of UE MR for both serving and neighbor cell measurements, and offloading MR serving cell measurement(s) to LP-WUR (RAN2, RAN4, RAN1)
For CONNECTED mode, specify necessary procedure to allow LP-WUS monitoring by LP-WUR when MR is in sleep mode(s) except for ultra-deep sleep, and MR PDCCH monitoring triggered by LP-WUS (RAN1, RAN2)
  In CONNECED mode operation, UE RRM/RLM/BFD/CSI measurements are performed by MR
Specify UE RF core and RRM performance requirements (RAN4)

## Slide 19
Evaluation performance for different waveforms in RAN 1
Time error, Frequency error
Time error tolerance
Frequency error tolerance
Waveform | Tolerance up to timing error [us]
OOK-1 @30kHz SCS | 5
OOK-1 @60kHz SCS | 3
OOK-1@120kHz SCS | 1
OOK-3 (single source) | 4
OOK-2 M=2 | 4
OOK-2 M=4 | 3
OOK-4 M=2 | 3
OOK-4 M=4 | 1
OOK-4 M>4 | 1
FSK M=1 | 2
FSK-1 M=2 | 1
FSK-2 M=2 | 2/3
OFDMA (with sliding window) | 4
Waveform | Tolerance up to frequency error [kHz]
OOK-1@30kHz SCS | 800
OOK-1@60kHz SCS | 400
OOK-1@120kHz SCS | 400
OOK-3 (single source) | 9.984
OOK-2 M=2 | 300
OOK-2 M=4 | 200
OOK-4 M=2 | 1200
OOK-4 M=4 | 800
OOK-4 M>4 | 390
FSK M=1 | 300
FSK-1 M=2 | 130
FSK-2 M=2 | 200
OFDMA | 26
[1] R1-2308729, TR38.869v040, section 8.3.1, section 8.3.2